## Slide 1
Real-Time Co-optimization
ERCOT
March 6, 2019

## Slide 2: Workshop Outline
Real-Time Co-optimization Education
Examples with Automated Scenario Spreadsheet
Additional Discussion and Next Steps

## Slide 3: Antitrust Admonition
Antitrust Admonition
To avoid raising concerns about antitrust liability, participants in ERCOT activities should refrain from proposing any action or measure that would exceed ERCOT’s authority under federal or state law. For additional information, stakeholders should consult the Statement of Position on Antitrust Issues for Members of ERCOT Committees, Subcommittees, and Working Groups, which is posted on the ERCOT website.1
Disclaimer
All presentations and materials submitted by Market Participants or any other Entity to ERCOT staff for this meeting are received and posted with the acknowledgement that the information will be considered public in accordance with the ERCOT Websites Content Management Operating Procedure.
1 The document is available at http://www.ercot.com/about/governance/index.html .

## Slide 4: Workshop Outline
Real-Time Co-optimization Education
Examples with Automated Scenario Spreadsheet
Additional Discussion and Next Steps

## Slide 5: RTC Procedural History*
Initial white paper in late 2014, discussions at SAWG in 2015
White paper last updated in September 2017
PUCT Considered the issue in several proceedings:
  Project No. 47199 – Project To Assess Price-Formation Rules In ERCOT'S Energy-Only Market
    The IMM and ERCOT worked together to simulate the introduction of RTC in historical Security-Constrained Economic Dispatch (SCED) cases. Study of 2017 activity was completed and filed 6/29/2018 (Project No. 47199)
    ERCOT analyzed improvements that RTC could have on RTM operations and RUC optimization and provided comments filed “ERCOT RTC Benefits Study“ on 6/29/2018 (Project No. 47199)
  Project No. 41837 - PUCT Review of RTC in the ERCOT Region
  Project No. 48540 - Review of Real-Time Co-Optimization in the ERCOT Market
    The Commission decided ERCOT should move forward with the RTC project on 1/17/2019
PUCT requested that ERCOT host another workshop on RTC to reinitiate discussions
* See appendix for links to workshops and whitepapers

## Slide 6: Impacts of Ancillary Service Capacity (Reserves) on LMP
Regardless of methodology, reserves and energy come from the same supply pool.
Allocating portions of the supply pool to each requirement will, at times, impact the marginal clearing price of both.
In general, allocating resources to energy and reserves must be done simultaneously to minimize the impacts of one product on the other, in order to globally minimize the cost of both.
If allocating resources to energy and reserves is done sub-optimally, the impacts of one product on another will be overstated (i.e. when required Ancillary Services and energy are not procured simultaneously).

## Slide 7: What is RTC and How does it Differ from the Current ORDC?
RTC allows for the optimal coordination of the provision of energy and AS among all resources in the Real-Time Market and, similar to the current ORDC, the pricing of AS shortages in accordance with defined AS demand curves.
Unlike the current ORDC, a demand curve for each AS product would be applied within the SCED engine to allow SCED to internally optimize the provision of energy and AS among all resources, subject to each resources’ capabilities and offers.
  AS capacity is no longer blocked from SCED by the HASL
  ORDC price adders no longer exist
  Establishes offer-based prices for each AS type and energy in the Real-Time Market through SCED under normal operating conditions and under AS shortage conditions, in accordance with the defined AS demand curves

## Slide 8: Key Changes Associated with the Implementation of RTC
The pricing of operating reserve shortages as a function of VOLL and LOLP under RTC is generally consistent with the approximation achieved under ORDC B+
The following represent key changes associated with RTC beyond ORDC B+:
  Least-cost provision of energy and Ancillary Services
  Enhancement to RUC optimization and removal of SASM
  Reduced risk and increased opportunity for resources, including limited duration resources
  Fewer manual processes by ERCOT operators

## Slide 9: 1. Least-cost Provision of Energy and AS
Real-time conditions often vary from the day ahead, and the resources that are optimal to provide energy and AS can change between DAM and Real-Time.
Since the RTC process is executed with each SCED run, there is better visibility of the constraints and the capabilities of the resources. As a result, the system can be operated more economically and reliably.
For example, a transmission constraint could bind in the RTM and cause a resource that was selected in the DAM to provide AS to be more economic in real time to provide energy. Similarly, a resource not awarded in DAM to provide AS could be selected in real time to provide AS.
The resulting real-time awards in many intervals are economically advantageous to both resources, and this benefits loads by selecting the lowest cost resources to provide energy and AS.

## Slide 10: 2. Enhancement to RUC optimization and removal of SASM
Implementation of RTC would include modifications to the RUC engine, such that the ability to coordinate the provision of energy and AS among resources in the RTM would be recognized in RUC.
Compared to the current market, this potentially reduces RUC activity, particularly in broader, import-constrained areas.
RUC would also be enhanced to ensure that sufficient, qualified AS capability is expected to be available in real time.
The need for SASM activity would be removed due to the coordinated access to the ERCOT portfolio of resources for the provision of energy and AS in real time.

## Slide 11: 3. Reduced Risk and Increased Opportunity for Resources
Access by individual resources to the ERCOT portfolio of energy and AS in real time
  The removal of SASM activity and the added benefit of access to the ERCOT portfolio of energy and AS in real time will result in less financial risk compared to current SASM process.
  Increased opportunity for individual resources to economically optimize the provision of energy and AS in the Real-Time Market.
  This could be particularly relevant to limited duration resources and IRRs that are interested and qualified to provide AS.

## Slide 12: 4. Fewer Manual Processes by ERCOT Operators
Automated identification and resolution of cases in which energy is needed by a specific resource to resolve congestion that was otherwise scheduled to provide AS
Automated release of AS capacity to provide energy during AS shortage conditions
Reduced RUC recommendations and removal of SASM

## Slide 13: AS Imbalance Settlement [Overview]
With RTC, each SCED execution (nominally every 5 minutes) produces system-wide SCED AS MCPCs (RTASMCPCy) and resource specific AS awards (RTASAWDry) for each AS type
AS Imbalance Settlement is equivalent to Energy Imbalance Settlement in that we will have:
  One resource specific 15-minute MCPC (RTASRP) for each AS product and resource (like RTRMPR) that is award and interval length weighted
  One system-wide 15-minute MCPC (RTASMCPC) for each AS product that is SCED interval length weighted (like RTSPP)
The resource MCPC (RTASRP) is the price used to calculate payment for the 15-minute real-time awards (RTASAWDr)
The system-wide MCPC (RTASMCPC) is the price used to calculate buy back of the DAM awards (DAASAWDr)

## Slide 14: AS Imbalance Settlement [Calculation]
The AS imbalance amount per resource is calculated for each 15-minute settlement interval:
RTASIAMTr = (-1) * (0.25*(RTASAWDr * RTASRPr– DAASAWDr* RTASMCPC))
Where;
RTASAWDr = TWFy * RTASAWDry
RTASMCPC = TWFy * RTASMCPCy
RTASRPr = RWFry * RTASMCPCy
TWFy = TLMPy / TLMPy
RWFry = [max(0.001, RTASAWDry)*TLMPy] / [ max(0.001, RTASAWDry) * TLMPy]

## Slide 15: AS Imbalance Settlement – Example for a 15-Minute Interval “No difference in DAM award and RTC awards --- but increase in price”
RTASIAMT = zero since DAM QTY = RT QTY
 | Units | DAM |  | SCED 1 | SCED 2 | SCED 3 |  | sum | RTASAWDr | RTASMCPC | RTASRPr
SCED duration | seconds |  |  | 300 | 300 | 300 |  | 900 |  |  | 
award | MW | 100 |  | 100 | 100 | 100 |  | 300 |  |  | 
price | $/MW | 100 |  | 9000 | 100 | 100 |  | 9200 |  |  | 
TWFy |  |  |  | 0.33 | 0.33 | 0.33 |  | 1 |  |  | 
RWFy |  |  |  | 0.33 | 0.33 | 0.33 |  | 1 |  |  | 
 |  |  |  |  |  |  |  |  | 100 | 3066.67 | 3066.67

## Slide 16: AS Imbalance Settlement – Example for a 15-Minute Interval “Different awards and prices compared to DAM awards and prices”
RTASIAMT = additional payment as extra AS MW procured in SCED 1 at a higher price
 | Units | DAM |  | SCED 1 | SCED 2 | SCED 3 |  | sum | RTASAWDr | RTASMCPC | RTASRPr
SCED duration | seconds |  |  | 300 | 300 | 300 |  | 900 |  |  | 
award | MW | 100 |  | 200 | 0 | 70 |  | 270 |  |  | 
price | $/MW | 80 |  | 160 | 90 | 95 |  | 345 |  |  | 
TWFy |  |  |  | 0.33 | 0.33 | 0.33 |  | 1 |  |  | 
RWFy |  |  |  | 0.74 | 0.0 | 0.26 |  | 1 |  |  | 
 |  |  |  |  |  |  |  |  | 90 | 115.00 | 143.15
DAM Payment for 15 minute interval |  | ($2,000.00)
RTASIAMT for the 15 minute interval |  | ($345.83)

## Slide 17: AS Imbalance Settlement – Example for a 15-Minute Interval “Double the DAM quantity for each SCED interval”
RTASIAMT = additional payment. The dollar amount is the same as the DAM 15-minute revenue since the QTY doubled and RT prices were the same as the DAM price.
 | Units | DAM |  | SCED 1 | SCED 2 | SCED 3 |  | sum | RTASAWDr | RTASMCPC | RTASRPr
SCED duration | seconds |  |  | 300 | 300 | 300 |  | 900 |  |  | 
award | MW | 100 |  | 200 | 200 | 200 |  | 600 |  |  | 
price | $/MW | 100 |  | 100 | 100 | 100 |  | 300 |  |  | 
TWFy |  |  |  | 0.33 | 0.33 | 0.33 |  | 1 |  |  | 
RWFy |  |  |  | 0.33 | 0.33 | 0.33 |  | 1 |  |  | 
 |  |  |  |  |  |  |  |  | 200 | 100.00 | 100.00

## Slide 18: AS Imbalance Settlement – Example for a 15-Minute Interval “Resource A with a DAM award but no RT awards”
RTASIAMT = a charge. The charge is more than the DAM revenue because the price was higher in RT for one of the intervals. (See next slide for resource “B.”)
 | Units | DAM |  | SCED 1 | SCED 2 | SCED 3 |  | sum | RTASAWDr | RTASMCPC | RTASRPr
SCED duration | seconds |  |  | 300 | 300 | 300 |  | 900 |  |  | 
award | MW | 100 |  | 0 | 0 | 0 |  | 0 |  |  | 
price | $/MW | 80 |  | 140 | 80 | 80 |  | 300 |  |  | 
TWFy |  |  |  | 0.33 | 0.33 | 0.33 |  | 1 |  |  | 
RWFy |  |  |  | 0.33 | 0.33 | 0.33 |  | 1 |  |  | 
 |  |  |  |  |  |  |  |  | 0 | 100.00 | 100.00

## Slide 19: AS Imbalance Settlement – Example for a 15-Minute Interval “Resource B had no DAM award but received RT awards (provided the AS not provided by resource “A” on previous slide”
RTASIAMT = additional payment that is equal to the RTAISAMT charge for resource “A” on the previous slide since resource “B” provided the AS resource “A” was awarded in DAM.
 | Units | DAM |  | SCED 1 | SCED 2 | SCED 3 |  | sum | RTASAWDr | RTASMCPC | RTASRPr
SCED duration | seconds |  |  | 300 | 300 | 300 |  | 900 |  |  | 
award | MW | 0 |  | 100 | 100 | 100 |  | 300 |  |  | 
price | $/MW | 80 |  | 140 | 80 | 80 |  | 300 |  |  | 
TWFy |  |  |  | 0.33 | 0.33 | 0.33 |  | 1 |  |  | 
RWFy |  |  |  | 0.33 | 0.33 | 0.33 |  | 1 |  |  | 
 |  |  |  |  |  |  |  |  | 100 | 100.00 | 100.00

## Slide 20: Workshop Outline
Real-Time Co-optimization Education
Examples with Automated Scenario Spreadsheet
Additional Discussion and Next Steps

## Slide 21: Purpose of Tool
The tool was developed to illustrate the energy and AS pricing results with RTC under AS surplus and shortage conditions by decomposing the current ORDC into a reserve demand curve for each AS.
The tool allows the user to alter the inputs and analyze outcomes.

## Slide 22: Design of Tool – Overview Tab
Assumptions
  VOLL = $9,000
  Offer Cap = $2,000
  Max Reserve Demand Curve Value = $7,000.99
  No congestion
  Generators available from 0 to HSL for energy, available in quantities offered for each AS
  All RRS provided from generators for the purpose of this example

## Slide 23: Design of Tool – Overview Tab
AS demand curves
  Designed to approximate the 2017 summer peak minimum AS requirements prior to blending and shift by .25 standard deviation
    Typical minimum AS requirement: URS = 270, RRS = 2,300, NSRS = 1,375
  NSRS represented as Spinning Online Reserves (SOR from the white paper, basically online NSRS)
  170 MW of URS and 1,830 MW of RRS are priced at $7,000.99
  ~100 MW of URS and 100 MW of RRS are priced at values that approximate the steps of the current PBPC
  The remaining RRS is priced at values that approximate the existing ORDC from 1,930 to 2,300 MW
  The maximum value on the SOR demand curve is $1,425 and extends for 3,000 MW (beyond the 1,375 MW requirement)
  Tab “Reserve Demand Curves Example” shows charts with the resulting individual and aggregate AS demand curves
  Changing the demand curves is not automated at this time

## Slide 24: Design of Tool – Overview Tab
System set up
  G1 represents the sum of 50,000 MW of infra-marginal generation
  G2-G8 represent online generation with increasing energy offers and identical AS offer quantities
  G9 represents a quick-start unit that can only provide energy or SOR
  There is a field for a Capacity Offer Price for each reserve that is set to $0 in these examples
  In the optimization, AS shortages are represented as a cost
  The original excel sheet has been modified to only have 1 case that can be modified by the user
  “Optimization Engine” tab allows the user to change the case to simulate different conditions

## Slide 25: Design of Tool – Running a Case
The user can modify the blue shaded cells
  Change the offer quantity and price for each generator for energy and each AS product
  Change the quantity and price for each AS product’s demand curve
  Change the total system demand
  Change the reserve requirements for each AS product
Once the inputs are set up, the user clicks the ‘Solve’ button to run the optimization engine

## Slide 26: Design of Tool – Optimization Results
After Solver runs, the white cells will be populated with the results, including cost and awarded quantities for each generator, AS product cost and prices, total system awarded capacity and AS product shortages.
The “Results Summary” tab contains a system-wide summary and graphical representations of awards, requirements and clearing prices.
The Solver outputs two tabs, “Answer Report” and “Sensitivity Report,” for a deeper dive into the constraints, objective function totals and optimization details.

## Slide 27: Case A – Example of System Surplus
In the Optimization Engine, do not change the Qty and Offer $ for generators.
System has 58,000 MW in generation capacity.
The energy demand is set at 54,000 MW.
All of the requirements are met.
Prices reflect opportunity costs of energy and AS.
Chart: Awarded MW by Generator
| G2 | G3 | G4 | G5 | G6 | G7 | G8 | G9
Energy | 1000 | 980 | 650 | 450 | 450 | 450 | 20 | 0
URS | 0 | 20 | 50 | 50 | 50 | 50 | 50 | 0
RRS | 0 | 0 | 300 | 500 | 500 | 500 | 500 | 0
SOR | 0 | 0 | 0 | 0 | 0 | 0 | 430 | 1000

## Slide 28: Case A – Example of System Surplus
In the Optimization Engine, do not change the Qty and Offer $ for generators.
System has 58,000 MW in generation capacity.
The energy demand is set at 54,000 MW.
All of the requirements are met.
Prices reflect opportunity costs of energy and AS.
Chart: Total AS Awards and Min. Requirements
| URS | RRS | SOR
Awards | 270 | 2300 | 1430
Requirements | 270 | 2300 | 1375
Chart: Clearing Prices
| Energy | URS | RRS | SOR
 | 106 | 71 | 66 | 46
Notes:   G8 is marginal for energy, 106-60 = 46
  G3 is marginal for URS, 106-35=71
  G4 is marginal for RRS, 106-40=66
  SOR Demand curve sets price for SOR @ 46 as it is marginal

## Slide 29: Case B – Example of System Scarcity
In the Optimization Engine, do not change the Qty and Offer $ for generators.
System has 58,000 MW in energy offers.
The energy demand is set at 56,010 MW.
All of the AS requirements are shorted.
Prices reflect opportunity costs of energy and AS.
Chart: Awarded MW by Generator
| G2 | G3 | G4 | G5 | G6 | G7 | G8 | G9
Energy | 1000 | 1000 | 1000 | 660 | 450 | 450 | 450 | 1000
URS | 0 | 0 | 0 | 10 | 50 | 50 | 50 | 0
RRS | 0 | 0 | 0 | 330 | 500 | 500 | 500 | 0
SOR | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 30: Case B – Example of System Scarcity
In the Optimization Engine, do not change the Qty and Offer $ for generators.
System has 58,000 MW in energy offers.
The energy demand is set at 56,010 MW.
All of the AS requirements are shorted.
Prices reflect opportunity costs of energy and AS.
Chart: Clearing Prices
| Energy | URS | RRS | SOR
 | 7045.99 | 7000.99 | 7000.99 | 1425
Chart: Total AS Awards and Min. Requirements
| URS | RRS | SOR
Awards | 170 | 1820 | 0
Requirements | 270 | 2300 | 1375
Notes:   G5 is marginal for energy, 7045.99-45 = 7000.99
  URS Demand curve sets price for URS@ 7000.99 as it is marginal
  RRS Demand curve sets price for RRS@ 7000.99 as it is marginal
  SOR Demand curve sets price for SOR @ 1425 as it is marginal

## Slide 31: Case C - Example of Reserve Depletion
In the Optimization Engine, do not change the Qty and Offer $ for generators.
System has 58,000 MW in energy offers.
The energy demand is set at 57,000 MW.
All of the demand is met but AS requirements are not met.
Prices reflect opportunity costs of energy and AS.
Chart: Awarded MW by Generator
| G2 | G3 | G4 | G5 | G6 | G7 | G8 | G9
Energy | 1000 | 1000 | 1000 | 1000 | 1000 | 550 | 450 | 1000
URS | 0 | 0 | 0 | 0 | 0 | 0 | 50 | 0
RRS | 0 | 0 | 0 | 0 | 0 | 450 | 500 | 0
SOR | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 32: Case C - Example of Reserve Depletion
In the Optimization Engine, do not change the Qty and Offer $ for generators.
System has 58,000 MW in energy offers.
The energy demand is set at 57,000 MW.
All of the demand is met but AS requirements are not met.
Prices reflect opportunity costs of energy and AS.
Even though we have only 1,000 MW of reserves, the energy price is less than VOLL.
Chart: Total AS Awards and Min. Requirements
| URS | RRS | SOR
Awards | 50 | 950 | 0
Requirements | 270 | 2300 | 1375
Chart: Clearing Prices
| Energy | URS | RRS | SOR
 | 7055.99 | 7000.99 | 7000.99 | 1425
Notes:   G7 is marginal for energy, 7055.99-55 = 7000.99
  URS Demand curve sets price for URS@ 7000.99 as it is marginal
  RRS Demand curve sets price for RRS@ 7000.99 as it is marginal
  SOR Demand curve sets price for SOR @ 1425 as it is marginal

## Slide 33: Case D – Example of Hitting SWOC
In the Optimization Engine, change the offers for G7 and G8 to $2,000.
System has 58,000 MW in energy offers.
The energy demand remains at 57,000 MW.
All of the demand is met but AS requirements are not met.
Prices reflect opportunity costs of energy and AS.
Chart: Awarded MW by Generator
| G2 | G3 | G4 | G5 | G6 | G7 | G8 | G9
Energy | 1000 | 1000 | 1000 | 1000 | 1000 | 500 | 500 | 1000
URS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
RRS | 0 | 0 | 0 | 0 | 0 | 500 | 500 | 0
SOR | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 34: Case D – Example of Hitting SWOC
In the Optimization Engine, change the offers for G7 and G8 to $2,000.
System has 58,000 MW in energy offers.
The energy demand remains at 57,000 MW.
All of the demand is met but AS requirements are not met.
Prices reflect opportunity costs of energy and AS.
In this case, we hit VOLL, but 2 generators had to offer 2,000 MW at SWOC.
Chart: Total AS Awards and Min. Requirements
| URS | RRS | SOR
Awards | 0 | 1000 | 0
Requirements | 270 | 2300 | 1375
Chart: Clearing Prices
| Energy | URS | RRS | SOR
 | 9000.99 | 7000.99 | 7000.99 | 1425
Notes:   G7,G8 are both marginal for energy, 9000.99-2000 = 7000.99
  URS Demand curve sets price for URS@ 7000.99 as it is marginal
  RRS Demand curve sets price for RRS@ 7000.99 as it is marginal
  SOR Demand curve sets price for SOR @ 1425 as it is marginal

## Slide 35: Workshop Outline
Real-Time Co-optimization Education
Examples with Automated Scenario Spreadsheet
Additional Discussion and Next Steps

## Slide 36: Items raised in the PUCT 2/21/2019 request for comments*
Values of and processes for the System-Wide Offer Cap (SWOC) and the Value of Lost Load (VOLL)
  Expected to include how the values are coordinated with one another and with the Ancillary Service (AS) demand curves, Power Balance Penalty Curve, and the Low System-Wide Offer Cap (LCAP)
Set of AS products under Real-Time Co-optimization (RTC) (e.g., those approved under NPRR863)
Basis for the development of the AS demand curve (e.g., using the current approved ORDC methodology in the creation of the AS demand curves that will be incorporated in the RTC)
Rules for AS participation, including:
  The current physical binding nature of Day-Ahead Market (DAM) AS awards
  Existing or new market rules that should apply to the offering of AS in real-time
  Requirement of qualified capacity to offer AS
Monitoring of AS performance
Other policy issues
* These issues are part of PUCT Project Number 48540

## Slide 37: Discussion On Scope
Financial- only AS offers in DAM
  Being discussed at the PUCT
5 minute settlement
  ERCOT does not view this as part of RTC
Local reserves
  ERCOT Grid Operations has not identified a reliability need to define a local reserve product, however the RTC design will co-optimize the reserves that the system operator requires.

## Slide 38: Next Steps
Within the Market Stakeholder process, ERCOT is engaging TAC leadership to initiate and support a task force for further development of RTC principles and scope.
Interested parties are also encouraged to monitor PUCT Project 48540 regarding RTC.
Any final questions?

## Slide 39: Appendix- Links to Relevant Documents
5/8/2017 SAWG – Need to coordinate values on VOLL SWOC PBPC training:
  http://www.ercot.com/content/wcm/key_documents_lists/118092/RT_Co-Opt_Coordination_of_VOLL_SWOC_PBPC.pptx
7/14/2017 SAWG – Scarcity pricing examples under RTC - spreadsheet
  http://www.ercot.com/content/wcm/key_documents_lists/138525/13.__RT_Co-Optimization_Scenario_Automated_July_2017_SAWG.xlsm
9/18/2017 SAWG – RTC white paper (updated)
  http://www.ercot.com/content/wcm/key_documents_lists/131797/RT_Co-optimization_Scope_UPDATED_09292017.docx
2/1/2019 PUCT staff recommendation and next steps
  https://interchange.puc.texas.gov/Documents/48540_29_1006504.PDF
2/21/2019 PUCT staff : Review of RTC
  https://interchange.puc.texas.gov/Search/Documents?controlNumber=48540&itemNumber=32