## Slide 1
Options for the allocation of auxiliary equipment power cost and Consumption
Ino González
RCWG
March 12, 2019

## Slide 2: Auxiliary Equipment Power Costs
Verifiable Cost (VC) Manual requires a Resource’s Heat Rate to be based on Net Generation
Where,
Net Generation = Gross Generation - Auxiliary Power requirements
Some Generators operate auxiliary equipment utilizing power from third service providers and want to include the costs of electricity as a variable cost.
Currently, the VC Manual allows for the recovery of electricity consumption only for energizing the generator and included with Startup O&M.
The VC Manual also allows for the recovery of auxiliary equipment power consumption cost as part of the variable O&M.
Available options:
  Include power consumption in heat rates
  Include power consumption cost in O&M, or
  Not include in either a. or b. above

## Slide 3: Adjusted Heat Rates for Auxiliary Equipment Consumption
Power consumption for auxiliary equipment can be included in the Input/Outpu (I/O) curve using the following methodology:
Based on invoices or other supporting documentation, determine the total auxiliary equipment consumption for the period(s) in which electricity was purchased from a third provider: AuxEquipConsumption
For the same period(s) determine the total generation injected into the grid: GenToGrid
Calculate the ratio ADJ = AuxEquipConsumption / GenToGrid
Prior to determine the I/O curve, for each data point:
  calculate the adjusted output (MW) = actual output (MW) * (1-ADJ)
  keep the input the same (MMBtu/Hr)
Determine the I/O curve and A-D coefficients based on the actual input and the adjusted output.

## Slide 4: Questions?
Notes: https://castaylor.ercot.com/owa/redir.aspx?C=oPhl4_Wz9UCI7oVqJkGdaM-P4-MvhtMIRAMJFZ7-K5eOg6lo6esBMUiebAbXd4c8z8FTPzV8g8A.&URL=https%3a%2f%2ftheconversation.com%2fwhen-will-rooftop-solar-be-cheaper-than-the-grid-heres-a-map-54789%3futm_source%3dtwitter%26utm_medium%3dreferral%26utm_campaign%3dUTAustinNews
http://www.vox.com/2015/6/19/8808545/wind-solar-grid-integration
http://greeningthegrid.org/quick-reads
https://ec.europa.eu/energy/intelligent/projects/en/projects/pv-grid
http://energy.gov/eere/sunshot/systems-integration