## Slide 1
Resource Definition Task Force
Load Resources Review
Mar 2019

## Slide 2: Agenda
Updated Load Resource Framework
  Proposed Definitions
Proposed Composite Framework

## Slide 3
Load Resources
Non-Controllable Load Resources*
Controllable Load Resources
UFR @ 59.7 Hz Required
Distribution Connected Loads Only
Single Site
Aggregate Load Resource (ALR)
Each site < 10 MWs of Demand Response Capability and all sites located in same Load Zone
Current Protocol Load Resource Framework
* Also referred to in the Protocols as Load Resource controlled by high-set under-frequency relay, Load Resource other than Controllable Load, and other variations

## Slide 4
Controllable Load Resource w/ Gov Resp & LFC basepoints
Controllable Load Resource (SCED Dispatched)
Real-Time Energy Market
SCED Qualified Controllable Load Resource
NPRR 863 Framework
Controllable Load Resource (SCED Dispatched)
Aggregate Load Resource (SCED Dispatched)
Basic Load Resource (Manual 10 Minute Response)
UFR* Load Resource (30 cycle)
UFR** Load Resource (30 cycle)
Auto Dispatch Controllable Load Resource (30 cycle)
UFR** Load Resource (15 cycle)
Auto Dispatch Controllable Load Resource (15 cycle)
Controllable Load Resource w/ Gov Resp & LFC base points
Controllable Load Resource providing FRRS
Existing Load Resource Type
New Load Resource Type

## Slide 5
Updated Proposed Load Resource Framework
Controllable Load Resource
Load Resource
Rapid Response Load Resource
Basic Load Resource
Responsive Reserve Service
FFR
UFR
Fast Response Regulation Service
Register as a Basic Load Resource and deployed through Verbal Dispatch Only to provide ECRS,
Register as a RRLR Load Resource with either a 15 cycle (FFR) or 30 cycle(UFR) response time and may qualify to provide ECRS or Responsive Reserve Service.
Regulation Service
Primary Frequency Response
ECRS
Non Spin (SCED Qualified)
Real-Time Energy Market (SCED qualified)
Register as a Controllable Load Resource to qualify to provide one or more of the following: FRRS, Regulation Service, Primary Frequency Response, ECRS, Non-Spin, and Real-Time Energy Market. May be an aggregation for providing Non-Spin only.
ECRS
ECRS

## Slide 6
Merit Badge Load Resources Framework

## Slide 7
Proposed Framework for Loads providing any kind of service

## Slide 8
Proposed Combined Framework