## Slide 1
Dynamic Models Overview – Follow Up
Proposed Options to Improve Dynamic Models in ERCOT
John Schmall
ERCOT Transmission Planning
Resource Integration Workshop
March 21, 2019

## Slide 2: Background
Dynamic Models Overview Presentation at ROS, March 2019
  Increasing model complexity/new devices
  Add the dynamic model improvement to the ROS scope for 2019
  Request ERCOT to follow up and work with stakeholders to address challenges associated with dynamic models
Proposed Schedule
  Resource Integration Workshop on March 21, 2019
    Review model challenges
    Propose potential improvements
    Encourage of vendor participation in the April IBR workshop
  IBR Workshop on April 25, 2019
    Continue modeling discussion (only one component of workshop)
    Set meeting date(s) dedicated to addressing modeling issues

## Slide 3: Review of Model Challenges (PSS/e Models)
Presentation at March ROS Meeting
  UDM Models (Especially IBR)
  Model Interference Issues
  Diagnostic Challenges
  See Appendix for Presentation Slides

## Slide 4: High Level Proposals/Considerations
Short Term
Existing Requirements
Model Performance
Mid-Term
Model Testing
Long Term
Model Development
RE Engagement
UDM Versus Standard

## Slide 5: Short Term Options (Existing Requirements)
Do existing model requirements need to be enhanced or better enforced? How?
  Confirm the model and parameters accurately represent the Facility (Required by RE per MOD-026/027, RARF, DWG PM)
    Model validation against the measured response?
    Model validation against the PSCAD models?
  Confirm the model is compatible with the software and does not interfere with other models (Required by TP per MOD-026/027)
    Can be very difficult to diagnose specific issues
    TP can identify issue but resolution is RE responsibility

## Slide 6: Short Term Options (New Requirements?)
Should UDM model guidelines be transformed into enforceable requirements? How to enforce? Some examples:
  Control block diagram
  Description of the model usage and each model parameter
  Highlight the parameters that can be adjusted by user
  Why does model include parameters that should not be adjusted by user?
Do specific performance requirements need to be implemented?
  Current requirements are not very specific
    Ride-through, dynamic response, AVR response
  Model performance reviewed by ERCOT/TSP
    FIS, QSA, MOD-026/027, RARF model updates
    Should evidence of appropriate basic model performance be submitted by RE along with the model?

## Slide 7: Mid-Term Options
How to engage vendors since REs may not have SMEs? How to avoid/mitigate unnecessary communication burden?
Strengthen the MOD 26/27 requirements? Include more testing expectations/requirements in addition to NERC requirements?
UDMs must be implemented as standard library models to be updated and maintained properly by the software vendors?
UDMs need to be vetted and approved by a third party (software vender or other) prior to acceptance?
Allow RE participation in DWG meetings?
  Open sessions for stakeholder engagement
Require model compatibility with real time stability assessment tool?
  UDMs are currently provided for PSS/e per DWG Procedure Manual
  Not compatible with real time stability assessment tool (TSAT)
  Require models for both PSS/e and TSAT? Different software platforms?

## Slide 8: Long Term Options
Collaboration with WECC/NERC to further develop and improve generic models for inverter-based resources
New ERCOT dynamic modeling task force/working group for both TSP and RE?
  Is there sufficient interest?
  REs may be unwilling/unable to dedicate resources and fully participate based on DMTF/RDWG experience
Require full RE participation in DWG meetings/access to DWG cases?
  Should REs be given responsibility for ensuring models properly integrate into DWG cases (no interference, proper initialization, etc.)?
  Protocol change regarding dynamic models as protected information

## Slide 9: PSCAD Models?
Premature to establish detailed model requirements?
Maintain/enhance model guideline?

## Slide 10: Appendix: Presentation Slides from March ROS

## Slide 11: Example: How Generators are modeled?
Algebraic equation with no time step
Solved in < 1 sec
60 Hz, steady state
Parameters: ~tens, standardized
Time step of 1 ~ 4 ms
Simulation finished in 1 ~ 10 mins
Parameters: tens ~ hundreds, varies based on technology, vendor, and machine generation
Time step of 10 ~ 50 us
Simulation finished in 10 mins ~ hours
Parameters: tens ~ hundreds, varies based on
Steady State
(Electromechanical Transient)
(Electromagnetic Transient)

## Slide 12: Dynamic Models in ERCOT
Synchronous Generators
Mature Technology
Inverter Based Resources
Developing technology
Most projects use user defined models that were developed by various entities (manufacturer, consultant, software vendor)
Most projects use standard model library maintained by the simulation software vendor
More than 200 renewable projects with UDMs

## Slide 13: Why User Defined Models
ERCOT accepts dynamic models with model parameters that represent the dynamic behavior of the device.
  Standard or UDM
Why UDMs are provided to ERCOT?
  Suggested by the vendor to accurately represent unique features that are not available in the limited standard model library
  For special system condition, like weak grid

## Slide 14: Dynamic Model Challenges
Many Identified dynamic model issues are listed in the ERCOT User Defined Model Submittal Guideline
  http://www.ercot.com/content/wcm/lists/168307/Dynamic_Model_Templates_v2.zip
For examples:
  Limited description of UDMs and difficult to fully understand the response of the models , unhelpful error messages
  Inconsistent simulation time step requirements
  Model and library changes/updates without clear distinction
  Models with poor memory management
  Models may not adhere to simulation software UDM requirements
  Model with very restricted rule, like machine ID

## Slide 15: Potential Model Interference Issue
Model 1
Model 1
Model 1
Model 2
Model 2
Model 2
Model 3
Model 3
Model 3
Model 4
Model 4
Model 4
Model 1
Model 1
Model 1
Model 2
Model 4
Model 2
Model 3
Model 3
Model 3
Model 4
Model 4
Model 4
Good Models manages data only within its own array space
Every dynamic model is assigned a specific number of internal arrays
Bad Model 4 writes to Model 2 internal array space
An example of dynamic flat start simulation message below indicated possible erroneous array management and significantly affected the simulation results.

## Slide 16: DWG/ERCOT Work and Ongoing Efforts
Better communication and awareness of the model issues and expectations
Develop tools to detect model issues
Work with the Resource Entities, developers, TSPs, and manufacturers to correct the model (lots of communication, very time consuming)
However
  Some model issues may not be possible to be identified by users (no access to the details of the UDMs)
  Increasingly UDMs are developed by outside entities. Model quality is and will continue to be a challenge.

## Slide 17: Next Steps and Future Plan
ERCOT is working with DWG to mitigate this challenge
  Require UDMs to be vetted by the simulation software vendor to ensure model quality?
  Require information/tests to demonstrate the quality of the model?
  Better communication at early stage of FIS process?
Others
  How to ensure the UDM developers maintain good model quality and update/correct the models?
  Work with the industry to continue to improve the development of the standard model library to reduce/eliminate the need of UDMs and NERC unacceptable model list