## Slide 1
Analysis of RTORDPA Relaxation and Triggering Proposals
Market Analysis
3/25/2019

## Slide 2: Introduction
The current design of the Real-Time On-Line Reliability Deployment Price Adder (RTORDPA) has known weaknesses
  Non-zero price adders when zero price adders might be “expected”
  Zero price adders when non-zero price adders might be “expected”
  For further discussion see the presentation from the 12/3/2018 QMWG
Several approaches have been discussed as design enhancements
ERCOT programmed, ran, and compared the results from four approaches and two options for triggering the price adder
This was a substantial effort and analysis is still ongoing
This presentation contains some of the results

## Slide 3: Four Approaches to Relaxation in the RTORDPA
The current method in production
Three alternatives discussed at previous WMWG meetings
  One alternative: do not relax LDLs of non-ONRUC Resources
  Two additional alternatives: make relaxation of both LDLs and HDLs of non-ONRUC Resources conditional on the dispatch run base points being not equal to LDL or HDL (respectively)
    Relax to either Ancillary Service (AS) limits (LASL and HASL) (referred to as “Conditional 1”) or Sustainable Limits (LSL and HSL) (referred to as “Conditional 2”)

## Slide 4: Four Methods of Setting HDL and LDL of Non-ONRUC Resources
Methods | Relaxation of dispatchable non-ONRUC units’ LDL and HDL in SCED Pricing Run | 
 | LDL= | HDL=
Production | max(LASL, MW-60*RampDown) | min(HASL, MW+60*RampUp)
No LDL Relaxation | Dispatch Run LDL | min(HASL, MW+60*RampUp)
Conditional 1 (max AS Limits) | If Dispatch BP=LDL, Then Dispatch Run LDL Else max(LASL, MW-60*RampDown) | If Dispatch BP=HDL, Then Dispatch Run HDL Else min(HASL, MW+60*RampUp)
Conditional 2 (max sustainable limits) | If Dispatch BP=LDL, Then Dispatch Run LDL Else max(LSL, MW-60*RampDown) | If Dispatch BP=HDL, Then Dispatch Run HDL Else min(HSL, MW+60*RampUp)

## Slide 5: Two Triggers for Calculating the Reliability Deployment Price Adder
The Reliability Price Adder is calculated as
  min( max(0, P2_Sys_Lambda - D2_Sys_Lambda), 9000 - D2_Sys_Lambda - ORDC_Online_Adder)
These two trigger methods were evaluated for the periods studied
  Any ONRUC status Resource inside a RUC commitment block (“Always”)
  Any ONRUC status Resource with BP=LDL inside a RUC commitment block (“BP=LDL”)
The “BP=LDL” triggering method is intended to address cases in which there is non-zero price adder, even when the ONRUC status Resource has an equivalent BP in both the dispatch and pricing runs
These methods would not preclude other reliability deployments from triggering the RTRDPA as they currently do

## Slide 6: Modeled SCED Intervals
Modeled the alternative pricing run approaches and triggers for all SCED intervals with ONRUC Resources between 8/1/2018 and 12/31/2018
719 SCED intervals covering about 60 hours of time
Includes RUC commitments for capacity and transmission constraints

## Slide 7: Resulting RTORDPA Statistics
Relaxation Scenario | RTORDPA Trigger | Average | Minimum | 50th Percentile | Maximum
Production | Always | 2.65 | 0.00 | 0.65 | 118.87
 | BP=LDL | 2.63 | 0.00 | 0.62 | 118.87
No LDL Relaxation | Always | 2.22 | 0.00 | 0.14 | 112.00
 | BP=LDL | 2.22 | 0.00 | 0.13 | 112.00
Conditional 1 | Always | 12.13 | 0.00 | 0.68 | 908.05
 | BP=LDL | 10.34 | 0.00 | 0.65 | 908.05
Conditional 2 | Always | 10.30 | 0.00 | 0.57 | 908.05
 | BP=LDL | 9.07 | 0.00 | 0.55 | 908.05
Statistics from 719 SCED intervals

## Slide 8: Results for all 719 SCED Intervals
Chart: Always Triggering RTORDPA

## Slide 9: Results for all 719 SCED Intervals
Chart: Only Triggering RTORDPA when ONRUC BP=LDL

## Slide 10: Results for all 719 SCED Intervals, Detail
Chart: Always Triggering RTORDPA

## Slide 11: Results for all 719 SCED Intervals, Detail
Chart: Only Triggering RTORDPA when ONRUC BP=LDL

## Slide 12: Looking at Details of 10/4/2018
The largest differences between the approaches were observed on 10/4/2018
RUC commitment was for capacity, from 13:00 to 19:00
ONRUC Resource was mitigated from 13:00 to 14:00
ONRUC Resource had LSL of 120 MW and HSL of 435 MW
Chart: Price ($/MWh)

## Slide 13: 10/4/2018 Results—First Group
Results for 10/4/2018 fell into two groups
  Group 1: Production and No LDL Relaxation
  Group 2: Conditional 1 and Conditional 2
There are very small differences between the four approaches in Group 1
Chart: System Lambda + RTORDPA ($/MWh)

## Slide 14: 10/4/2018 Results—Second Group
There are larger differences between the four approaches in Group 2 than in Group 1, but the four still have very similar results
  Conditional 1 is nearly identical to Conditional 2
  Conditional 1 with BP=LDL trigger is nearly identical to Conditional 2 with BP=LDL trigger
Chart: System Lambda + RTORDPA ($/MWh)

## Slide 15: Additional HDL in Pricing Run on 10/4/2018
Production and No LDL Relaxation had significantly more HDL relaxation than the Conditional Relaxation approaches
However, the largest differences between the approaches’ price adders do not necessarily line up with the smallest values of HDL relaxation
Chart: Additional HDL in Pricing Run (MW)

## Slide 16: Developing a Target for Comparison
Different approaches give different prices—what are the “right” prices?
Need a point of comparison to say which approach is closer to the “right” price
RTORDPA is intended to mitigate the impact of the must-take LDL energy from the ONRUC Resource(s)
If the ONRUC Resource had LDL=0, would not have any must-take energy. This is why we relax the ONRUC LDL to zero in the pricing run.
Created a sequential SCED execution with the ONRUC LDL=0 in the dispatch run to create a reference for the “right” price
  Does not need a pricing run because the dispatch run allows ONRUC capacity to be price-setting all the way to BP=0

## Slide 17: Results of Sequential SCED for 10/4/2018
Chart: System Lambda + RTORDPA ($/MWh)
The largest differences between the approaches were observed on 10/4/2018
For this day, the Production group is generally a better match for the Sequential SCED Reference
Notes: Add ONRUC LDL to the graph

## Slide 18: Ongoing Work
ERCOT is continuing to study these results to understand the differences between the different approaches and the Sequential SCED reference
ERCOT is also running the Sequential SCED reference for other days with RUCs