## Slide 1
Today vs. Under RTC
Dave Maggio
April 4, 2019

## Slide 2: Acronyms
Ancillary Services (AS)
Current Operating Plan (COP)
Day-Ahead Market (DAM)
Energy Offer Curve (EOC)
ERCOT Contingency Reserve Service (ECRS)
High Ancillary Service Limit (HASL)
High Sustained Limit (HSL)
Load Frequency Control (LFC)
Locational Marginal Price (LMP)
Low Ancillary Service Limit (LASL)
Low Sustained Limit (LSL)
Market Clearing Price for Capacity (MCPC)
Nodal Protocol Revision Request (NPRR)
Non-Spinning Reserve (Non-Spin)
Operating Reserve Demand Curve (ORDC)
Qualified Scheduling Entity (QSE)
Real-Time Co-optimization (RTC)
Real-Time Market (RTM)
Regulation Down (Reg-Down)
Regulation Up (Reg-Up)
Reliability Unit Commitment (RUC)
Resource Limit Calculator (RLC)
Responsive Reserve Service (RRS)
Security-Constrained Economic Dispatch (SCED)
Supplemental Ancillary Service Market (SASM)
System-Wide Offer Cap (SWOC)
Under-Frequency Relay (UFR)
Value of Lost Load (VOLL)

## Slide 3: High-Level Flow Today of the Wholesale Market – DAM through Settlement
Day-Ahead Operations
Adjustment Period
Operating Period
Post Real-Time
DAM
RUC
RUC
SASM
Hour-Ahead
Operating Hour
(RTM)
Settlement
Reporting
Performance Monitoring

## Slide 4: High-Level Flow of the Wholesale Market Under RTC – DAM through Settlement
Day-Ahead Operations
Adjustment Period
Operating Period
Post Real-Time
DAM
RUC
RUC
Hour-Ahead
Operating Hour
(RTM)
Settlement
Reporting
Performance Monitoring
The SASM process goes away, and the RUC process will be used to ensure sufficient capacity is available to meet demand and minimum AS requirements for the RUC study horizon.
The flow largely remains the same, but the functionality, inputs and outputs may need to be changed or used in a new way.

## Slide 5: Operating Hour: Energy and AS Awards
Today
Only energy is optimized
  Output is base points for energy and energy prices (LMPs)
SCED solves power balance and congestion with capacity not reserved for AS
  Resource AS assignment taken as a given (base points limited by HASL/LASL)
Base points are subject to ramp rates via dispatch limits
Under RTC
Energy and AS are co-optimized
  Output is base points for energy, AS awards for each product, energy prices (LMPs) and AS prices (MCPCs) for each product
SCED solves power balance, congestion and AS needs (using penalty and AS demand curves)
  Base points no longer limited by an assumed HASL/LASL
Base points and AS awards take into consideration ramp rates, AS qualifications, other limitations

## Slide 6: Operating Hour: Energy and AS Awards Cont.
Today (pre-NPRR 863)
Non-Spin can be provided by on-line resource or off-line resources
  For off-line Non-Spin, specific to qualified resources with a status of “OFF” (show status of “OFFNS” when carrying the service in real time)
For the ORDC price adders, there are on-line reserves and off-line reserves (that are available after 30 minutes)
Under RTC
ECRS and Non-Spin can be provided by on-line resource or off-line resources
  For off-line ECRS, specific to qualified QSGRs with a status of “OFFQS”
  For offline Non-Spin, specific to qualified resources with a status of “OFF”
RTC will not consider energy offers from off-line resources (i.e., will not commit these resources – note that OFFQS will be considered on-line by RTC)
Changes largely associated with NPRR863

## Slide 7: Operating Hour: Prices
Today
Only energy is optimized and prices for energy are determined
The ORDC design is used to calculate the level of reserves and the price for those reserves as a post-process
  The price for on-line reserves is then added to the energy prices
Indicative prices are calculated
May execute a pricing run if a defined reliability deployment has occurred
Under RTC
Energy and AS are co-optimized to produce prices for both energy and each of the AS products
A post-process to determine the value of reserves is no longer needed
  No ORDC price adder
  Energy prices (LMPs) will include the opportunity costs for AS
Indicative prices are calculated
May execute a pricing run if a defined reliability deployment has occurred

## Slide 8: Operating Hour: Prices Cont.
Today (pre-NPRR 863)
Non-Spin AS prices (MCPCs) in the DAM are the same for on-line and off-line resources
Under RTC
ECRS prices (MCPCs) in the DAM and RTM are the same for on-line and off-line resources
Non-Spin AS prices (MCPCs) in the DAM and RTM are the same for on-line and off-line resources
Some changes associated with NPRR 863

## Slide 9: Operating Hour: AS Deployment/Procurement
Today (pre-NPRR863)
Reg-Up/Down deployed at the QSE portfolio-level by LFC
Non-UFR RRS deployed manually through LFC at the QSE portfolio level
  Release of HASL via schedule changes
UFR RRS deployed via relays or manually by ERCOT
On-line Non-Spin available to SCED but behind an EOC floor
Off-line Non-Spin deployed manually
Under RTC
Reg-Up/Down deployed at the resource-level by LFC
  Reg-Up/Down procurement driven by AS demand curves
Non-UFR RRS and ECRS procurement driven by AS demand curves
UFR RRS deployed via relays or manually by ERCOT
Load Resources, other then Controllable Load Resources, providing ECRS deployed manually
On-line Non-Spin procurement driven by AS demand curve
  Current offer floor goes away
Off-line Non-Spin deployed manually
Some changes associated with NPRR 863

## Slide 10: Adjustment Period: RUC
Today
Resource AS assignment taken as given (under high penalty)
RUC attempts to solve power balance and congestion with capacity not reserved for AS
  Base points are produced but not binding
Answers the question: “Given the resources planned to be on-line and how the AS is being carried, can power balance be met, and can congestion be resolved?”
Under RTC
Energy and AS are co-optimized, although base points and AS assignments are not binding
RUC attempts to solve power balance, congestion and AS needs
Answers the question: “Given the resources planned to be on-line, can power balance and minimum AS requirements be met, and can congestion be resolved?”
This applies to Day-Ahead and hourly RUC.

## Slide 11: Adjustment Period: Insufficient AS or AS Responsibility Replacement
Today
Use SASM for resource-specific awards when there is insufficient AS, a failure to provide, or infeasible AS between the DAM and Real-Time
Direct assignment of AS through RUC is a back stop
Under RTC
RUC attempts to solve power balance, congestion and AS needs
Ensures sufficient, qualified AS capability is projected to be on-line (or available off-line for applicable AS)
The set of resources projected to provide AS in the RUC solution may not necessarily be the same set of resources providing AS in real time
This applies to Day-Ahead and hourly RUC.

## Slide 12: Day-Ahead Operations: DAM
Today
Energy and AS are co-optimized
High, flat penalties for AS insufficiency
  If AS is insufficient, the price is based on the last cleared offer
AS awards are resource specific
AS self-arrangement is not resource specific and can exceed a QSE’s AS obligation amount or be negative
Under RTC
Energy and AS are co-optimized
Open question as to whether or not new AS demand curves will be used
  These new AS demand curves would presumably be based on the AS demand curves used in real time
Open question as to whether or not AS awards would necessarily have to be associated with a resource (i.e., virtual AS offers)