## Slide 1
ERCOT Proposed Changes to NPRR 916
David Maggio
Sr. Manager, Market Analysis & Validation
Technical Advisory Committee WebEx
April 4, 2019

## Slide 2: Negative Fuel Prices at the Waha Hub Coupled with the Mitigated Offer Floors are Creating Irrational Restrictions for CTs and CCGTs
The minimum of the Mitigated Offer Floor and the Reference LMP from Step 1 of SCED determine a lower bound for Energy Offer Curves in Step 2 of SCED.
  Per protocol, this lower bound is applied to all resources between Step 1 and Step 2, whether or not the resource is flagged for mitigation on the upper bound.
Currently, the floor is set at 1MMBtu/MWh * FIP for CCGTs and 6MMBtu/MWh * FIP/FOP for CTs and Gas/Oil Steam.
NPRR 916 changes these numbers to a straight value of $0/MWh.
While this change helps, it does not solve the problem.
  Recently, there have been several days in which the daily fuel index at the Waha hub has been negative.
  If gas prices are negative, a floor of zero is excessive relative to the resource’s optimal offer.
  For this reason, ERCOT proposes to change the offer floor to -$20/MWh. This proposal aligns CTs and CCGTs with the offer floor for coal and lignite units.
  This proposal is timely since NPRR 916 will be considered by the Board of Directors on April 9.

## Slide 3: Comparison of Recent Natural Gas Indexes
Chart: Transaction Date
| 43557 | 43556 | 43553 | 43552 | 43551 | 43550 | 43549 | 43546 | 43545 | 43544
Waha | -3.345 | -0.07 | -0.535 | -1.88 | -0.935 | -0.01 | -0.525 | 0.265 | -0.08 | 0.26
Houston Ship Channel | 2.69 | 2.74 | 2.66 | 2.64 | 2.63 | 2.715 | 2.72 | 2.8 | 2.87
No price published for the Houston Ship Channel hub on March 26, 2019.
Prices are not published on weekends.

## Slide 4: Additional Detail on ERCOT’s Proposal
Current version of NPRR 916:
  Changes the Mitigated Offer Floor for “Combined Cycle” and “Gas/Oil Steam and Combustion Turbine” Resource Categories to $0/MWh
  Proposed effective date of May 1, 2019
ERCOT is proposing:
  Implementation of NPRR 916, as approved by TAC, upon Board approval
    Would allow the floors of $0/MWh to become effective April 10, 2019
  A second phase of changes in which the Mitigated Offer Floor for “Combined Cycle” and “Gas/Oil Steam and Combustion Turbine” Resource Categories change from $0/MWh to -$20/MWh
    Second phase can be implemented in late May
    Expected cost for this phase is less than $10,000 and would be absorbed by O&M budgets