## Slide 1
“Informal” Distributed Generation Review
Includes Registered and Unregistered DG
April 12, 2019

## Slide 2: DER Awareness Issues in ERCOT
4 Different “Categories” of DG in ERCOT*
  Distribution Generation Resource
  A DG unit that has chosen to register as a Generation Resource to participate in the ERCOT Energy and Ancillary Services markets.
  Settlement-Only Distribution Generator
  DG units > 1 MW that export are required to register with ERCOT. QSEs representing these units are settled by ERCOT. (These units were previously referred to as “registered DG.”)
  Unregistered Distributed Self-Generator
  DG units > 1 MW that do not export and have registered as a Self-Generator with the PUC are not required to register with ERCOT.
  Unregistered Distributed Generator
  DG units < 1 MW are not required to register with ERCOT.
                *NPRR889
Registered DG
Unregistered DG

## Slide 3: Registered* DG in ERCOT
Distribution Generation Resources (DGR)
Full telemetry required
Dispatched by SCED
Full visibility in all systems
Settlement-Only Distribution Generator (SODG)
No telemetry
‘Self’ dispatched
Operational awareness only (DG mapping**)
*Registered with ERCOT
**NPRR866

## Slide 4: Settlement-Only Distributed Generation in ERCOT 2010-2018
Accumulated Count
Chart: 
| Prior to 2010 | Q1 2010 | Q2 2010 | Q3 2010 | Q4 2010 | Q1 2011 | Q2 2011 | Q3 2011 | Q4 2011 | Q1 2012 | Q2 2012 | Q3 2012 | Q4 2012 | Q1 2013 | Q2 2013 | Q3 2013 | Q4 2013 | Q1 2014 | Q2 2014 | Q3 2014 | Q4 2014 | Q1 2015 | Q2 2015 | Q3 2015 | Q4 2015 | Q1 2016 | Q2 2016 | Q3 2016 | Q4 2016 | Q1 2017 | Q2 2017 | Q3 2017 | Q4 2017 | Q1 2018 | Q2 2018 | Q3 2018 | Q4 2018
total | 96.66 | 101.46 | 101.46 | 116.32 | 124.52 | 127.72 | 127.72 | 138.52 | 138.52 | 167.32 | 217.88 | 217.88 | 217.88 | 217.88 | 367.96 | 380.23 | 389.61 | 409.37 | 413.37 | 418.37 | 430.64 | 449.91 | 473.64 | 482.77 | 484.35 | 507.21 | 516.34 | 527.34 | 536 | 544.04 | 571.9 | 605.2 | 670.49 | 686.83 | 723 | 748.2 | 818.43
Renewable MW | 80.66 | 85.46 | 85.46 | 100.32 | 100.32 | 103.52 | 103.52 | 106.72 | 106.72 | 106.72 | 146.08 | 146.08 | 146.08 | 146.08 | 146.08 | 146.08 | 146.08 | 156.07 | 156.07 | 156.07 | 156.07 | 165.57 | 167.57 | 167.57 | 169.15 | 169.15 | 170.72 | 181.72 | 181.72 | 181.72 | 181.72 | 190.51 | 246.23 | 250.31 | 250.31 | 260.31 | 320.31
ACCUMULATED COUNT | 16 | 17 | 17 | 19 | 20 | 21 | 21 | 23 | 23 | 26 | 32 | 32 | 32 | 32 | 48 | 50 | 51 | 55 | 56 | 57 | 59 | 62 | 66 | 67 | 68 | 71 | 73 | 75 | 82 | 94 | 114 | 125 | 142 | 155 | 181 | 196 | 215
Renewables
Non-renewables
Accumulated Count
SODGs are:
<10 MW
If >1 MW and inject to grid, must register with ERCOT
If <1 MW, registration optional

## Slide 5: Registered DG Trends 2015-2018 (includes DGR)

## Slide 6: Unregistered DG in ERCOT
Unregistered Distribution Self-Generator (> 1 MW that does not export)
  TDSPs submit annual reports to PUC for all interconnections
  ERCOT excludes information in the TDSP reports for backup and emergency generators that are not capable of paralleling with ERCOT
  NOIEs submit quarterly reports to ERCOT for DG > 50 kW
Unregistered Distribution Generator (< 1 MW)
  TDSPs submit multiple reports on DG interconnections
    TDSPs submit annual reports to PUC for all interconnections
    TDSPs submit updated ESI ID Profile Codes to ERCOT as DG is installed
    Does not include DG installed at IDR Meter sites (> 700 kW)
  NOIEs submit quarterly reports to ERCOT
    For DG > 50 kW
    Some NOIEs for DG < 50 kW starting in 2020*
                *NPRR891

## Slide 7: Q4 2018 NOIE Distributed Generation Survey
ERCOT surveyed municipalities and co-ops (NOIEs) representing the bulk of the NOIE Load to quantify the amount of DG
  31 of 33 NOIEs surveyed responded
  16 additional NOIEs responded
Solar PV > 50 kW ~70 MW
Wind > 50 kW ~1 MW
Solar PV < 50 kW ~210 MW
Wind <50 kW ~ 1 MW
Total NOIE unregistered DG ~ 282 MW total

## Slide 8: ERCOT Estimated Total DG Growth 2015-2018 (MW)
Note: This estimate includes informal data reporting by many NOIEs and excludes generation data informally reported by investor-owned utilities for generation that would typically be considered backup or emergency generation.
31%
26%
181%

## Slide 9: ERCOT Estimated Total DG Growth 2015-2018 (# Units)
Note: This estimate includes informal data reporting by many NOIEs and excludes generation data informally reported by investor-owned utilities for generation that would typically be considered backup or emergency generation.