## Slide 1
The Ancillary Service Manager
Dave Maggio
May 13, 2019

## Slide 2: Acronyms
Ancillary Service (AS)
Controllable Load Resources (CLRs)
Current Operating Plan (COP)
Day-Ahead Market (DAM)
Emergency Response Service (ERS)
ERCOT Contingency Reserve Service (ECRS)
Fast Frequency Response (FFR)
Nodal Protocol Revision Request (NPRR)
Non-Spinning Reserve (Non-Spin)
Qualified Scheduling Entity (QSE)
Real-Time Co-optimization (RTC)
Real-Time Market (RTM)
Responsive Reserve Service (RRS)
Security Constrained Economic Dispatch (SCED)
Under-Frequency Relay (UFR)

## Slide 3: Does the AS Manager need to change with RTC?
Problem that needs to be addressed:
  The AS Manager displays are:
    Largely driven today by information from the QSEs: real-time telemetry and COP information
    Not designed to recognize that AS awards would be an output of the RTM optimization

## Slide 4: Functions Performed Using the AS Manager Today (and expected under NPRR 863)
The AS Manager is used by ERCOT Operators to manually deploy:
  Non-Spin to off-line Resources
  RRS (and FFR) to Load Resources on a UFR
  ERS
  ECRS to Load Resources that are not Controllable Load Resources
Also used to recall these deployments

## Slide 5: Functions Performed Using the AS Manager Today (and expected under NPRR863)
In populating the list of Resources that can be deployed, the application uses a mix of real-time telemetry, information from the COPs and other sources.
  Largely based on the telemetered, Resource-specific AS responsibilities and schedules.
  COP information is specifically used for off-line Non-Spin where the deployment is occurring in the latter half of an Operating Hour.
  For ERS, the contract information is populated into a database that feeds the display for deployment.
t
t+30
t+60
Operating Hour
Telemetry
COP

## Slide 6: Functionality Under RTC
At a high level, the function of the application stays the same.
  Specifically, the same set of instructions would be sent using the AS Manager.
    This assumes the suite of AS products largely stays the same.
  The source information for the ERS display also stays the same.
The obvious change is the source of information regarding the set of Resources that are providing AS and can be deployed, excluding ERS.
  The telemetry and COP information will be replaced by the AS awards coming out of SCED.
  In some cases, the AS awards coming out of SCED may reflect telemetry from the QSE on their plan to provide AS using a specific Resource.
    This has been discussed for RRS that is scheduled on UFR Load Resources.

## Slide 7: Functionality Under RTC
ERCOT is also evaluating other functionality.
For Non-Spin:
  Relevant to partial deployments, the display currently ranks the Resources based on locational price in the DAM. If similar logic remains, replace the DAM price with RTM prices.
  Depending on the time within the Operating Hour in which the Non-Spin is being deployed, AS Manager currently looks at the awards for the upcoming hour.
  Similarly, current logic automatically redeploys Non-Spin to account for AS responsibility changes at the top of the hour.
For RRS:
  Currently have process for grouping Load Resources providing RRS with a UFR. Looking at doing initial grouping like today but reviewing process for new Resources that get awards.

## Slide 8: Key Takeaways
The AS Manager will perform the same set of primary functions but will be modified to source the Resource-specific AS responsibility/award information as an output from the RTM.
As part of NPRR863, the AS Manager will also be used by ERCOT operators to manually deploy ECRS and FFR that is being provided by Load Resources that are not CLRs.

## Slide 9: Questions