## Slide 1
Update to the Peaker Net Margin Threshold based on Latest Cost of New Entry Information
Aaron Townsend
Supervisor, Market Analysis
Technical Advisory Committee
ERCOT Public
May 22, 2019

## Slide 2: Background Information
The Peaker Net Margin (PNM) threshold is used to determine the point at which the System-Wide Offer Cap (SWCAP) is reset from the High System-Wide Offer Cap (HCAP) of $9,000/MWh to the Low System-Wide Offer Cap (LCAP), which is the greater of $2,000/MWh and 50 times the daily effective Fuel Index Price (FIP).
Per PUCT Substantive Rule 25.505 and Protocol 4.4.11, the PNM threshold is set at 3 times the Cost of New Entry (CONE) for a generation plant, historically a combustion turbine generation plant.
  The PNM threshold in recent years has been $315,000/MW-year
  Implicit CONE is $105,000/MW-year

## Slide 3: Updated Study Information and Proposal
In late December 2018, the latest report on the “Estimation of the Market Equilibrium and Economically Optimal Reserve Margins for the ERCOT Region” (“MERM/EORM study”) was finalized
Within this report, the latest CONE for a combustion turbine generation plant was identified as being $88,500/MW-year
This is lower than the value implicit in the current PNM threshold

## Slide 4: Drivers for the Decrease in CONE
Brattle estimates CONE for PJM and adjusts it to account for locational cost differences in ERCOT
The figure below shows the drivers of recent changes in CONE in PJM
Primary drivers are lower ATWACC (interest rate) and lower corporate tax rates
Image is from Brattle’s 2018 PJM report: https://www.pjm.com/~/media/committees-groups/committees/mic/20180425-special/20180425-pjm-2018-cost-of-new-entry-study.ashx

## Slide 5: Updated Study Information and Proposal
The base case results in the MERM/EORM study used by the PUC to inform the ORDC shift used the $88,500/MWh value
After initial publication Brattle later adjusted the assumed interest rates and corporate tax rates and found that with those new assumptions the CONE would be $91,200/MW-year
ERCOT is proposing to use the $91,200/MW-year CONE and update the PNM threshold from $315,000/MW-year to $273,600/MW-year (3 times $91,200/MW-year)

## Slide 6: Process to Update the PNM Threshold
The PNM threshold is defined as a parameter in Protocol 4.4.11.
An update to the value requires a recommendation from TAC and approval by the ERCOT Board.
The updated value would take effect on the first day of the month following ERCOT Board approval unless otherwise directed by the ERCOT Board.
The change is communicated by ERCOT through a Market Notice and the parameter is administratively updated in the Protocols upon its effectiveness.