## Slide 1
DAM Hub Average Price Calculation
Carrie Bivens
Manager, Forward Markets
June 5, 2019

## Slide 2: Introduction
NPRR931, As Built Hub Average Calculation, was filed on April 16, 2019, and approved by PRS on May 10, 2019
It updates the protocols to reflect the fact that the Day-Ahead Market (DAM) uses the aggregated shift factor method for computing the Hub Average price, rather than a direct simple averaging of the component Hubs’ prices.
Due to necessary Shift Factor cutoffs used during DAM clearing, there can in some cases be a few cents’ difference between these two methods in the current implementation.

## Slide 3: Explanation
Any shift factor that is calculated to be extremely small (Hub cutoff currently set at less than 0.000001) during the DAM Network Security Monitor (NSM) process are not passed on to Network Constrained Unit Commitment (NCUC), in order to reduce the size of constraint data to fit within the existing software restrictions.
Where the hub shift factor cutoff is applied can result in a small price difference if the shadow price of the constraint is very high.
  Note there is an additional parameter being added in a later 2019 release that will have the effect of removing any price difference, however the aggregated shift factor method of calculating prices will continue to be used.

## Slide 4: Simple average of 4 Hub prices

## Slide 5: System implementation
*Simplified example for illustrative purposes