## Slide 1
Follow Up Information Regarding AS Offer Structures
David Maggio
June 7, 2019

## Slide 2: Acronyms
Ancillary Service (AS)
Controllable Load Resource (CLR)
ERCOT Contingency Reserve Service (ECRS)
Nodal Protocol Revision Request (NPRR)
Non-Spinning Reserve Service (Non-Spin)
Primary Frequency Response (PFR)
Qualified Scheduling Entity (QSE)
Quick-Start Generation Resource (QSGR)
Real-Time Co-optimization (RTC)
Regulation Down Service (Reg-Down)
Regulation Up Service (Reg-Up)
Responsive Reserve Service (RRS)
Under-Frequency Relay (UFR)

## Slide 3: Introduction
During previous meetings on the AS Offer structure, there was confusion on how NPRR 863 will affect the current structure.
Given the discussion and identified dependencies, we’re going to pause on development of the RTC principle concepts for AS Offer structure for now.
This material should provide useful context for when the topic is reinitiated later in the year.

## Slide 4: Today’s AS Offer Structure
A set of data applicable to the entire submission:
  QSE short name
  ­Resource ID (includes mode/configuration)
  ­Combined cycle plant name (required for combined cycle Resources only)
  ­Non-Controllable Load flag (true/false indicating UFR or CLR, required for CLR only)
  ­Expiration date/time
One or more sets of data applicable to separate periods of time in the day:
  Start date/hour
  End date/hour
  Up to 5 capacity amounts (in MW) for an AS category (“Online Reserves” - includes RRS, Reg-Up, Online Non-spin; “Regulation-Down”; and “Non-Spin Offline” – Resources must be qualified to provide the AS type, and Load Resources qualified for Non-Spin cannot submit Non-Spin Offline)
  A price associated with each AS type for each capacity amount, if offered for that capacity
  Fixed/variable quantity block indicator, for each capacity amount (only Load Resources can indicate fixed)
  Multi-hour indicator
Source: Market Submission Validation Rules V1.0 (ERCOT MIS Secure Area)

## Slide 5: AS Framework Changes under NPRR 863
Current Framework
FFR
Triggered at 59.85 Hz and full response in 15 cycles
Once deployed, sustain for up to 15 mins. Once recalled, restore within 15 mins
PFR
PFR capable capacity reserved on generators or Controllable Load Resources (CLR)
Minimum 1,150 MW must be provided by resources capable of PFR
Load Resources on UFR
Triggered at 59.70 Hz and full response in 30 cycles
Sustain until recalled. Once recalled, restore within 3 hours
Beyond the minimum PFR, up to 60% of total RRS can come from Load Resources on UFR or FFR.
Generation
Online or offline capacity that can be converted to energy within 10 minutes
Dispatched by SCED
Load Resources (UFR not required)
Up to 50% of ECRS capacity can come from Load Resources with or without UFR
Must respond within 10 minutes. Restoration within 3 hours
Load Resources on UFR
Primary Frequency Response (PFR)
Fast Frequency Response (FFR)
ERCOT Contingency Reserve Service (ECRS)
Load Resources may or may not be on UFR
10 minute ramp
Responsive Reserve Service (RRS)
Primary Frequency Response
Load Resources on Under Frequency Relay (UFR)
10 minute ramp
2,300 to 3,200 MW
No Change
Regulation
Regulation
157 to 687 MW
157 to 687 MW
2,300 to 3,200 MW
508 to 1,644 MW
Responsive Reserve Service
Non-Spin
No protocol changes.
Proposed methodology for Non-Spin Reserve Service quantities in this framework - quantities computed using 2018 A/S Methodology are reduced by ECRS quantities.
967 to 2,361 MW
Quantities are estimates based on historical procurements and projections.
For Discussion Purposes Only. The intent of this slide is to represent NPRR 863 (with STEC comments from 10/1/2018). Protocol language prevails to the extent of any inconsistency with this one page summary.
Overall A/S:
3,807 to 5,958 MW
Overall A/S: 3,807 to 5,958 MW
NPRR 863 (approved by ERCOT Board Feb. 12, 2019)
Non-Spin
0 to 1,180 MW

## Slide 6: AS Offers Structure Change under NPRR 863
Follow today’s linked AS Offer structure to minimize system changes
Change to today’s “Online Reserves” category
  Add ECRS in this category and link it with Reg-Up, RRS and Online Non-Spin
Change to today’s “Non-Spin Offline” category
  Change the category name to “Offline Reserves”
  Add “OFFQS ECRS” in this category and link it with offline Non-Spin
No change to today’s “Regulation-Down” category

## Slide 7: AS Offers for Generation Resources under NPRR 863
“Online Reserves” category
  Reg-Up
    5-minute ramp from online Generation Resources
  RRS
    Capable of providing PFR from online Generation Resources
  ECRS
    10-minute ramp from online Generation Resources
  Online Non-Spin
    30-minute ramp from online Generation Resources
“Regulation-Down” category
  Reg-Down
    5-minute ramp from online Generation Resources
  “Offline Reserves” category
  OFFQS ECRS
    10-minute ramp from offline QSGR
  Offline Non-Spin
    30-minute ramp from offline generation Resources

## Slide 8: AS Offers for Load Resources under NPRR863
“Online Reserves” category
  Reg-Up
    CLR capable of providing PFR
  RRS
    CLR qualified for SCED dispatch and capable of providing PFR
    Load Resource on UFR
  ECRS
    CLR qualified for SCED dispatch and capable of providing PFR
    Load Resource may or may not be on UFR (10-minute ramp)
  Online Non-Spin
    CLR qualified for SCED dispatch
“Regulation-Down” category
  Reg-Down
    CLR capable of providing PFR
  “Offline Reserves” category
  Load Resource can not submit AS offers for “Offline Reserves” category

## Slide 9
Questions