## Slide 1
Planning Guide 5.4.5 – Dynamic and Transient Stability Analysis
ERCOT Transmission Planning
RI Integration Workshop
June 20, 2019

## Slide 2: Background
Planning Guide 5.4.5 (6), based on the approved PGRR054, establishes a process for identifying, proposing, and implementing solutions to stability issues identified during the FIS.
FIS Stability Studies Identify Instability
IE and TSP shall investigate alternative solutions through the proposed GR for ERCOT Review
Feasible?
ERCOT notify TSP and IE. TSP shall investigate a transmission improvement to resolve the instability and report to ERCOT
Feasible?
TSP shall proceed with RPG process
Yes
No
IE shall implement the changes prior to Initial Synchronization
Yes

## Slide 3: PG 5.4.5
(6) If the TSP identifies instability (other than instability identified for extreme events) in the stability portion of the FIS, the following steps will be taken subsequent to the FIS being deemed complete and posted in the Market Information System (MIS) Secure Area in accordance with Section 5.4.8, FIS Study Report and Follow-up:
The IE and TSP shall investigate alternative solutions to resolve the instability through changes to the proposed Generation Resource and report their findings to ERCOT. If changes to the Generation Resource are determined by ERCOT to be feasible, the IE shall implement the changes prior to Initial Synchronization.
  The consideration of alternative solutions include the controller tuning, settings adjustments. No additional hardware or devices will be requested if the proposed GR can meet all the other interconnection requirements.
  The alternative solutions should demonstrate the effectiveness of the alternative solutions and the feasibility of implementing the alternative solutions to resolve the instability prior to the Initial Synchronization.

## Slide 4: PG 5.4.5
(b) If ERCOT determines that changes to the proposed Generation Resource are not feasible to resolve the identified instability, ERCOT shall notify the TSP and IE, and the TSP shall investigate a transmission improvement to resolve the instability and report their findings to ERCOT.
  ERCOT’s review will determine if the transmission improvement is feasible to resolve the instability from stability perspective.
  ERCOT’s review will not determine if the transmission improvement will meet the reliability or economic criteria as defined in the RPG review process.

## Slide 5: PG 5.4.5
(c) If ERCOT determines that a proposed transmission improvement is feasible to resolve the identified instability the TSP shall proceed with implementing the transmission improvement, in accordance with Protocol Section 3.11.4, Regional Planning Group Project Review Process, identified in paragraph (6)(b) above after the requirements of Section 6.9, Addition of Proposed Generation to the Planning Models, have been met for the proposed Generating Resource.
  TSP shall follow the RPG submittal requirement defined in Planning Guide 3.1.2.1.
  If the instability can be resolved through generation re-dispatch, this project is not considered as a reliability project.

## Slide 6: Discussion
If the RPG submittal indicates no reliability or economic need of the identified transmission improvement, ERCOT will conduct comment process only without conducting ERCOT independent review if ERCOT agrees with TSP’s assessment.
If the transmission improvement is not expected to meet reliability and/or economic criteria, should the TSP proceed with RPG process?