## Slide 1
Long SCED intervals and EBP Summary
Market Analysis and Validation
WMWG
June 24th, 2019

## Slide 2: Long SCED intervals, EBP Offset and Price Changes
 | Occurrence Count |  |  | Long SCED duration (in minutes) |  |  | System Lambda Changes ($/MWh) | 
Year | Long SCED Count | Price Correction Count due to long SCED | EBP offset count for long SCED | Maximum duration | Average duration | Minimum duration | Largest Increase | Largest Decrease
2010 | 5 |  | 1 | 36.1 | 19.6 | 12.3 | 0.33 | -0.61
2011 | 28 | 12 | 6 | 120.6 | 27.0 | 10.2 | 319.62 | -8.57
2012 | 5 | 3 |  | 44.2 | 24.6 | 11.8 | 1.08 | -1.22
2013 | 3 | 3 | 1 | 47.7 | 38.1 | 29.3 | -0.37 | -3.96
2014 | 9 | 8 | 2 | 83.8 | 30.6 | 10.1 | 47.52 | -737.41
2015 | 10 | 2 | 2 | 79.5 | 19.4 | 7.7 | 709.33 | -17.21
2016 | 14 | 4 | 2 | 82.9 | 16.7 | 7.7 | 18.86 | -1.62
2017 | 5 | 2 |  | 17.0 | 10.5 | 7.9 | 1.37 | -371.62
2018 | 9 | 5 |  | 27.6 | 13.1 | 7.7 | 0.77 | -85.19
2019 | 2 |  |  | 13.5 | 13.4 | 13.3 | -0.26 | -0.29
Total | 90 | 39 | 14 | 120.6 | 22.1 | 7.7 | 709.33 | -737.41
Note:
The long SCED interval threshold was 10 minute before 2015, and 7.5 minute since 2015 due to EMS logic.
3 Instances in 2018 and 2 instances in 2019 were due to unannounced constant frequency control test.
The System Lambda changes were calculated from original system lambda before price correction.

## Slide 3: Long SCED intervals, EBP Offset and Price Correction
Note:
There were 5 other EBP offset events that are not included in the graphs because they were not related to long SCED intervals. Those include 2 in 2011 and 2012, respectively, and 1 in 2016. EBP offset was entered while SCED was still running.
Chart: Count of Long SCED Intervals/EBP offset and the duration
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019
Long SCED Count | 5 | 28 | 5 | 3 | 9 | 10 | 14 | 5 | 9 | 2
Price Correction Count due to long SCED | 12 | 3 | 3 | 8 | 2 | 4 | 2 | 5
EBP offset event count for long SCED | 1 | 6 | 1 | 2 | 2 | 2

## Slide 4: Duration of Long SCED intervals (Max, Average and Min)
Chart: Long SCED duration in minutes
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019
Max Long SCED duration (minutes) | 36.1 | 120.6 | 44.2 | 47.7 | 83.8 | 79.5 | 82.9 | 17 | 27.6 | 13.5
Average Long SCED duration (minutes) | 19.6 | 27 | 24.6 | 38.1 | 30.6 | 19.4 | 16.7 | 10.5 | 13.1 | 13.4
Min Long SCED duration (minutes) | 12.3 | 10.2 | 11.8 | 29.3 | 10.1 | 7.7 | 7.7 | 7.9 | 7.7 | 13.3

## Slide 5: Count of Price Correction due to Long SCED intervals
Chart: Count of Price Correction related to Long SCED intervals
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019
Count of Price Correction to only RTRMPRs due to long SCED | 0 | 0 | 0 | 2 | 7 | 1 | 2 | 2 | 5 | 0
Count of Price Correction to both SPPs and RTRMPRs due to long SCED | 0 | 12 | 3 | 1 | 1 | 1 | 2 | 0 | 0 | 0
NPRR696 was approved in September 2016, which requires ERCOT holds prices from last good SCED run prior to a failure for 15-minute after the SCED. This rule was applied 3 times since then.

## Slide 6: Questions?