## Slide 1
June 21, 2019
RTCTF Meeting
Nitika Mago
ERCOT Operations
Resource Limit Calculator Under RTC
Telemetry Changes

## Slide 2
Problem Statement
Identify telemetry changes, associated with Resource Limit Calculator (RLC) changes.
Discussion Outline
RLC functional overview
Summary of changes identified and rationale
Discussion and next steps

## Slide 3: RLC Overview
Nodal Protocol Section 6.5.7.2 drives the calculations and monitoring built into RLC today.
RLC uses telemetry from QSEs to compute limits such as HDL, LDL, HASL and LASL. These limits are then sent to MMS/SCED.
RLC receives dispatch data from MMS and sends the same to QSEs.
RLC also hosts calculations related to Generation To Be Dispatched (GTBD), including Predicted Load Ramp Rate (PLDRR) and Predicted Wind Ramp Rate (PWRR).
Resource Limit Calculator
Ancillary Service Calcs.
ex. HASL, LASL
Resource Limit Calcs.
ex. SURAMP, SDRAMP, HDL, LDL
GTBD Calculation
Includes PLDRR, PWRR
Telemetry from QSE via SCADA/ICCP
Dispatch Data from MMS
Operator Initiated Data
SCED BP/LMP Data To QSE via SCADA/ICCP
Calculated and telemetered Data To MMS/SCED
Data For Settlements
Data For Reports and Compliance
Other Calcs./Stuff
Ex. SCED Trigger following RRS release

## Slide 4: Resource Specific Telemetry From/To QSE* - Current
To QSE |  | 
Unit Related |  | A/S Related
Base Point (BP) |  | Non-Spin Deployed (NDPL)
Locational Marginal Price (LMP) |  | RRS Deployed (RDPL) [NCLR]
Curtailment (SBBH) |  | 
SCCT Status (SCCT) |  | 
Updated Desired BP (UDBP) |  | 
From QSE |  |  | 
Unit Related |  |  | A/S Related
High/Low Sustained Limits (HSL, LSL) | AVR Status (AVR) |  | FRRS Up/Down Participation Factor (FUPF, FDPF)
High/Low Emergency Limit (HEL, LEL) | Dynamically Scheduled Resource Schedule (DSRS)[Gen] |  | FRRS Up/Down Responsibility (FURS, FDRS)
Normal Up/Down Ramp Rate (NURR, NDRR) | Lower/Raise Block Status (LBST, RBST) [Gen] |  | Regulation Up/Down Participation Factor (RUPF, RDPF)
Emergency Up/Down Ramp Rates (EURR, EDRR) | PSS Status (PSS) |  | Regulation Up/Down Responsibility (RURS, RDRS)
Net MW/MVAR (MW (aka NPF for CCP), MVAR) | POI kV Measurement/Target (KVM, KVT) |  | Responsive Reserve Responsibility/Schedule (RRRS, RRSC)
Gross MW/MVAR (GMW, GMV) | Scheduled Power Consumption (SPC, SPC2) [CLR] |  | High Set Under Frequency Relay (HSUF) [NCLR]
Resource Status (RST) | Storage Resource Charge/Discharge Data (MXCP, MXDP, MXOD, SOC) |  | Non-Spin Responsibility/Schedule (NSRS, NSSC)
CCP Config No (CCC) | IRR MET Data (DEG, IRAD, MPH, PRES, PTMP, TEMP) |  | 
Non Frequency Responsive Capacity (NFRC) | IRR Turbine/Panel Availability (NTOF, NTON, NTUN) |  | 
Load Resource Breaker Status (LRCB) [NCLR] |  |  | 
Max/Low Power Consumption (MPC, LPC) [CLR, NCLR] |  |  | 
*ERCOT Nodal ICCP Communications Handbook

## Slide 5: RLC Telemetry Changes
Under RTC, Ancillary Services (AS) will be awards will be an output and for Resources that are being economically dispatched by ERCOT, the current practice of pre-reserving portions of their capacity to provide AS through telemetry from the Resource’s QSE will be discontinued.*
  Thus, AS related responsibility and schedule telemetry from QSE are not needed in RTC.
Under RTC, AS will be a resource specific award.
  New telemetry that tracks AS awards at resource level will be available to QSEs.
Under RTC, AS will be awarded to only to those resources qualified to provide the service.
  New telemetry will be created to allow QSEs to telemeter an AS specific maximum capability for a qualified resource.
    Another option being considered is to allow QSE to “opt-out” a qualified resource from getting any specific AS awarded
*Key Principle 1.4 Principle 1

## Slide 6: RLC Telemetry Changes
Under RTC, Regulation instruction from ERCOT will change from QSE portfolio level (remove Participation Factors) to Resource specific.*
  Thus, Regulation related participation factor telemetry from QSE are not needed in RTC.
  New telemetry will be created to send resource level Regulation instructions to QSEs.
Lastly this is not a exhaustive list of telemetry changes. More changes may be identified as discussions on other topics mature.
*Key Principle 1.5 Principle 3

## Slide 7: Resource Specific Telemetry From/To QSE* - RTC
To QSE |  | 
Unit Related |  | A/S Related
Base Point (BP) |  | Non-Spin Deployed (NDPL)
Locational Marginal Price (LMP) |  | RRS Deployed (RDPL) [NCLR]
Curtailment (SBBH) |  | Regulation Up Award, Regulation Down Award
SCCT Status (SCCT) |  | Responsive Reserve Award
Updated Desired BP (UDBP) |  | Non-Spin Award
 |  | Regulation Up Deployment, Regulation Down Deployment
 |  | Updated Desired SP (UDSP)
From QSE |  |  | 
Unit Related |  |  | A/S Related
High/Low Sustained Limits (HSL, LSL) | AVR Status (AVR) |  | FRRS Up/Down Participation Factor (FUPF, FDPF)
High/Low Emergency Limit (HEL, LEL) | Dynamically Scheduled Resource Schedule (DSRS)[Gen] |  | FRRS Up/Down Responsibility (FURS, FDRS)
Normal Up/Down Ramp Rate (NURR, NDRR) | Lower/Raise Block Status (LBST, RBST) [Gen] |  | Regulation Up/Down Participation Factor (RUPF, RDPF)
Emergency Up/Down Ramp Rates (EURR, EDRR) | PSS Status (PSS) |  | Regulation Up/Down Responsibility (RURS, RDRS)
Net MW/MVAR (MW (aka NPF for CCP), MVAR) | POI kV Measurement/Target (KVM, KVT) |  | Responsive Reserve Responsibility/Schedule (RRRS, RRSC)
Gross MW/MVAR (GMW, GMV) | Scheduled Power Consumption (SPC, SPC2) [CLR] |  | High Set Under Frequency Relay (HSUF) [NCLR]
Resource Status (RST) | Storage Resource Charge/Discharge Data (MXCP, MXDP, MXOD, SOC) |  | Non-Spin Responsibility/Schedule (NSRS, NSSC)
CCP Config No (CCC) | IRR MET Data (DEG, IRAD, MPH, PRES, PTMP, TEMP) |  | Regulation Up Max Capability, Regulation Down Max Capability
Non Frequency Responsive Capacity (NFRC) | IRR Turbine/Panel Availability (NTOF, NTON, NTUN) |  | Responsive Reserve Max Capability
Load Resource Breaker Status (LRCB) [NCLR] |  |  | Non-Spin Opt Max Capability
Max/Low Power Consumption (MPC, LPC) [CLR, NCLR] |  |  | 
*ERCOT Nodal ICCP Communications Handbook

## Slide 8
Discussion