## Slide 1: Willing Seller, Willing Buyer DAM AS
Steve Reedy, Potomac Economics
sreedy@potomaceconomics.com
512-225-7139

## Slide 2: AS and Energy in DAM – Current Model
Willing Buyers buy Energy from Willing Sellers
  Hedgers and Arbitrages buying and selling
  No need for physical asset (generator/load)
  No physical obligations incurred
  Imbalance settlement w.r.t. real time market
  Provides hedging opportunity against volatile real time prices
  Provides price signal to inform commitment
ERCOT buys AS to AS plan levels
  As proxy for load
  No matter what offer price
  Only from qualified physical sellers
  Awarded QSEs incur responsibilities to provide AS
Notes: SB408 Effective September 2005

## Slide 3: Why Difference Between DAM Energy and AS?
Currently DAM is the last normal time for ERCOT to procure AS
  Needs to be physical
With advent of RT Co-optimization, ERCOT will get AS in Real-Time
  Enables “energy-like” market for AS in DAM
  Willing Seller, Willing Buyer

## Slide 4: Description of DAM WSWB
ERCOT buys no AS in DAM
Arbitragers or Loads who choose to hedge with DAM AS price put in bids to buy AS quantities/prices
  Bid for Non Spin, ECRS, REG-UP, REG-DN, or RRS
Loads enter self-provision quantities
Arbitragers or Resources who choose to hedge with DAM AS price put in offers to sell AS quantities/prices
  Offer RRS-pfr, RRS-ufr, RRS-ffr, REG-UP conventional, REG-UP ffrs, REG-DN conventional, REG-DN ffrs, ECRS sced, ECRS-lr, Non Spin
  Stand alone offers or current three-part offers

## Slide 5: Description of DAM WBWS
Clearing of market matches bids and offers
  Honors maximum levels of various types of AS (e.g. RRS-ufr)
Sellers receive AS quantity * DAM AS price
  AS = ECRS, Non Spin, RRS, REG-UP, REG-DOWN
  Each have their own price and quantity
Buyers pay AS quantity * DAM AS price
  AS same as for sellers
Real-Time charges are imbalance based
  Charge = (Obligation – Provision) * Real-Time AS price
  Again, AS = ECRS, Non Spin, RRS, REG-UP, REG-DOWN
  Each have their own price and quantity

## Slide 6: FAQs
What About RUCs?
  RUC runs with current schedule
    Basically asks question “Can current COP ON + OFF resources with sufficient start-up time meet load forecast + AS plan?”
    Conceptually similar to today
What about RRS/Loads?
  Only people who have DAM awards for RRS-ufr (or trades with DAM awarded) will be able to offer RRS-ufr into Real-Time
Co-optimized/Linked energy & AS offers?
  Possibly
Load implications
  Loads without DAM awards/self provision will be exposed to Real-Time prices