## Slide 1: Maintaining Participation Factors as an Option
Shams Siddiqi, Ph.D.
(512) 619-3532
shams@crescentpower.net
TAC Meeting
July 24, 2019
Notes: <number>

## Slide 2: Participation Factors (PFs)
July 24, 2019
<number>
NP 6.5.5.2(q) “Reg-Up and Reg-Down participation factors represent how a QSE is planning to deploy the Ancillary Service energy on a percentage basis to specific qualified Resource(s).”
PFs are used solely in real-time monitoring, GREDP, and Base Point Deviation calculations for Resources providing RUS and RDS – they have NO impact on SCED RTC outcomes or LFC deployment instructions.
The award of Ancillary Services every SCED interval by RTC is NOT impacted by using either no PFs or QSE-specified PFs.
In the future, most RUS and RDS will be provided by energy storage.
PFs become very important tools to manage storage levels in deploying RUS and RDS for portfolios with storage resources since LFC has no other mechanism to account for storage levels
Since LFC does NOT take into account congestion or economics in deploying RUS/RDS energy, allowing for PFs results in more economical and efficient RUS/RDS energy deployments
There are NO reliability concerns with current PFs and maintaining PFs
Maintaining PFs as an option allows QSEs to use PFs if required
Notes: <number>

## Slide 3: Maintaining PF as an Option
July 24, 2019
<number>
RTC and LFC would function exactly as described in the ERCOT proposal.
QSEs have the option of telemetering PFs – for all QSEs not exercising this option, there is no change to the ERCOT proposal (this can be implemented as default PFs proportional to awarded quantities).
For QSEs that telemeter PFs, since there is a 8-45 second communication delay in ERCOT accepting telemetered PFs after each RTC run that are aligned with the RTC awards, the first few LFC cycles after each RTC run until aligned PFs are accepted by ERCOT, the QSE resources will be deployed and performance measured based on the exact LFC deployment (as in the ERCOT proposal).
Once the aligned PFs have been accepted by ERCOT after each RTC run and until the next RTC run, real-time resource performance monitoring, GREDP, Base Point Deviation, etc. will all be measured using LFC deployments adjusted for telemetered PFs.
Notes: <number>

## Slide 4: Example of PF Usefulness
July 24, 2019
<number>
Compressed Air Energy Storage (CAES) is registered both as a Generation Resource (GR) and Controllable Load Resource (CLR) and can provide AS both as GR and CLR at the same time – when awarded RUS for both, it’s more efficient to deploy RUS as CLR avoiding roundtrip losses & gas burn – i.e. PF 0.1 on GR and 0.9 on CLR
A QSE portfolio of 2-hour storage resources at various POIs having 2-hr, 1-hr, and 5-min storage levels awarded RUS on all can manage RUS deployment by specifying PFs of say 0.6, 0.3, and 0.1, respectively. For RDS, PFs could be 0.1, 0.3, 0.6, respectively.
PFs allow these resources to manage their storage levels and thereby be able to continuously provide RUS/RDS – otherwise the storage resource with 5-min storage providing RUS for a 5-min RTC interval would likely not be able to provide RUS for the next 5-min RTC interval
Maintaining PFs under RTC as proposed here requires essentially the same real-time resource monitoring, GREDP, and Base Point Deviation calculations as are done today – No LFC performance concerns since LFC is not impacted
Notes: <number>

## Slide 5: Conclusion: Maintain PF under RTC
July 24, 2019
<number>
Maintain PFs as an Option under RTC – maintaining PFs costs close to nothing but, once eliminated, it would be costly to reintroduce PFs
PFs would be optional - default if no PFs are telemetered is exactly deployment amounts coming from LFC
If PFs are not used, then RUS/RDS deployments are exactly what comes from LFC and no design change is needed
With Energy Storage likely to provide the bulk of RUS/RDS capacity, PFs are likely to become vital tools to manage storage levels and continuously provide RUS/RDS
There are many other reasons to maintain PFs including differentials in ramp rates, congestion prices, marginal production costs, etc. and managing through transitions for coal and combined cycle plants
There is no compelling reason to eliminate PFs
Since this is a complex issue that has significant stakeholder support and that may be difficult for TAC to decipher from a short presentation, TAC could direct ERCOT and stakeholders to work on an implementation of this concept acceptable to all
Notes: <number>