## Slide 1: Evaluating Mitigated Offer for RUC Resources
July WMWG discussion

## Slide 2: SCED offer for RUC
Current offer for step 1
  $1500/MWh
Current offer for step 2
  min (step 1 offer, max(step1 LMP, Mitigated offer cap)) if mitigated
Current mitigated offer cap
  Max [
    Generic Incremental fuel price * max( FIP, weighted avg exceptional fuel cost) ,
    (Incremental heat rate* FIP + O&M)* capacity factory multiplier
    ]

## Slide 3: SCED offer for RUC - Issues
RUC offers could replace market based offers and if so could cause price suppression due to the out of market commitment
Prices don’t reflect the real cost of RUCing the resource. Cost of commitment includes
  startup + min energy if RUC committed
  min energy if QSE commitment is extended by RUC

## Slide 4: Real Cost per MWh
Energy obtained
  LSL MWs (avg RUC dispatch) * RUC commitment hours
Cost: Cost of producing energy + cost of commitment
Cost per MWh is ratio of
  Cost of producing energy + cost of commitment
  Total energy obtained
Change to MOC
  Current MOC + (cost of commitment/total energy obtained)
    Current MOC represents cost of energy produced/MW

## Slide 5: Proposal
For all hour which are not RUC Buy-Back Hours of RUC-committed Resources, ERCOT shall change the MOC of the RUC-committed Resource to be used in SCED to greater of
  25 multiplied by FIP
  MOC per 4.4.9.4.1(1) plus
    Max (Resource Category Generic Startup Cost, verifiable Startup Cost, Startup Offer) / (LSL * number of RUC committed hours)
    Max (Resource Category Generic Minimum-Energy Cost, verifiable Minimum-Energy Cost, Minimum-Energy Offer) – MOC at the Midpoint of the Dispatch Range
(I) above is set to zero if RUC commitment is just extending the QSE committed hours

## Slide 6
Questions?