## Slide 1
Evaluating LDF Performance on RT Congestion
Market Analysis and Validation
CMWG
Aug 5th, 2019

## Slide 2: Current LDF Methodology
ERCOT retrieves historical State Estimator load data on all modeled loads in the most recent network models, on the selected proxy day.
The LDF sets are updated regularly to reflect the significant changes in system-wide load patterns, normally every 1~2 months.

## Slide 3: Example A: How LDFs Cause Oversold/RENA
LZ_A
LD1
…..
G
Limit: 100 MVA
DAM LDF: LD1 100MW, total LZ_A 5000MW
DAM awards: 5000 MW PTP Obligation from HB_A to LZ_A
RT: LD1 80MW, total LZ_A 4000MW, the constraint is binding with $400 Shadow Price, which creates price separation of $8 between LZ_A and HB_A, and the SF of LZ_A to the constraint is -2%
Result:
PTP value in RT: 5000*$8
RT Congestion Rent: 100*$400
SF: -100%
RENA: $0
HB_A
Notes: Assumption of current LDF methodology:
With overall load zone wide change, the ratio of individual load is relatively stable. The assumption is still hold in this case.

## Slide 4: Example B: How LDFs Cause Oversold/RENA
LZ_A
LD1
…..
G
Limit: 100 MVA
DAM LDF: LD1 100MW, total LZ_A 5000MW
DAM awards: 5000 MW PTP Obligation from HB_A to LZ_A
RT: LD1 125MW, total LZ_A 5000MW, the constraint is binding with $400 Shadow Price, which creates price separation of $10 between LZ_A and HB_A, and the SF of LZ_A to the constraint is -2.5%
Result:
PTP value in RT: 5000*$10
RT Congestion Rent: 100*$400
SF: -100%
RENA: $100,000
HB_A

## Slide 5: Example C: How LDFs Cause Oversold/RENA
LZ_A
LD1
…..
G
Limit: 100 MVA
DAM LDF: LD1 100MW, total LZ_A 5000MW
DAM awards: 5000 MW PTP Obligation from HB_A to LZ_A
RT: LD1 100MW, total LZ_A 4000MW, the constraint is binding with $400 Shadow Price, which creates price separation of $10 between LZ_A and HB_A, and the SF of LZ_A to the constraint is -2.5%
Result:
PTP value in RT: 5000*$10
RT Congestion Rent: 100*$400
SF: -100%
RENA: $100,000
HB_A

## Slide 6: How LDFs Cause Oversold/RENA
A constraint is binding in RT.
The load ratio in LDF is not matching the actual ratio in RT.
The impact of Load Zone bid/offer on the constraint is not modeled accurately in DAM.

## Slide 7: Using LZ Shift Factor to evaluate LDF performance
To evaluate the accuracy of LDFs to a certain constraint, the old and new LDFs are used to calculated the Load Zone shift factors, which are then compared with the actual RT values.
The LDF-based Load Zone shift factors are calculated from RT electrical bus shift factors, which are all based on the exact same RT topology.
The difference of Load Zone shift factors can only be caused by the different load ratios of LDFs.

## Slide 8: LDF performance on the constraint XWHI58: LON_HILL_381H (OD 1/15/2019)
Chart: LZ_SOUTH SF for constraint XWHI58:LON_HILL_381H

## Slide 9: LDF performance on the constraint XWHI58: LON_HILL_381H (OD 1/15/2019)
Chart: LZ SF (Old LDF vs New LDF) for XWHI58: LON_HILL_381H
| LZ_AEN | LZ_CPS | LZ_HOUSTON | LZ_LCRA | LZ_NORTH | LZ_RAYBN | LZ_SOUTH | LZ_WEST
Average of LZ_SF_prod_recal | 0.017714 | 0.019203 | 0.020012 | 0.016919 | 0.019018 | 0.019048 | -0.092746 | 0.018839
Average of LZ_SF_old | 0.017711 | 0.019217 | 0.020011 | 0.016779 | 0.019022 | 0.019048 | -0.089679 | 0.018837
Average of LZ_SF_new | 0.017714 | 0.019217 | 0.020011 | 0.017018 | 0.019018 | 0.019047 | -0.092404 | 0.018842
Chart: LZ SF Error (Old LDF vs New LDF) for XWHI58: LON_HILL_381H
| LZ_AEN | LZ_CPS | LZ_HOUSTON | LZ_LCRA | LZ_NORTH | LZ_RAYBN | LZ_SOUTH | LZ_WEST
Average of diff_LZ_SF_old | 2.3558e-06 | 1.4686e-05 | 1.4246e-05 | 0.00014244 | 3.7994e-06 | 5.599e-07 | 0.0039942 | 2.0687e-06
Average of diff_LZ_SF_new | 1.2822e-06 | 1.4106e-05 | 6.1679e-06 | 9.9142e-05 | 1.6674e-06 | 1.1589e-06 | 0.0024527 | 2.6643e-06
Notes: 1/15

## Slide 10: LDF performance on the constraint DELMELM5: HILL_MAR_2_1 (OD 2/9/2019)
Chart: LZ_SOUTH SF for constraint DELMELM5:HILL_MAR_2_1

## Slide 11: LDF performance on the constraint DELMELM5: HILL_MAR_2_1 (OD 2/9/2019)
Chart: LZ SF (Old LDF vs New LDF) for DELMELM5:HILL_MAR_2_1
| LZ_AEN | LZ_CPS | LZ_HOUSTON | LZ_LCRA | LZ_NORTH | LZ_RAYBN | LZ_SOUTH | LZ_WEST
Average of LZ_SF_prod_recal | 0.05988 | -0.32427 | 0.04424 | 0.022265 | 0.031589 | 0.030433 | -0.047142 | 0.0029799
Average of LZ_SF_old | 0.060286 | -0.32606 | 0.044257 | 0.025055 | 0.031408 | 0.030406 | -0.046652 | 0.0025969
Average of LZ_SF_new | 0.060083 | -0.32578 | 0.044251 | 0.025167 | 0.031347 | 0.030411 | -0.046499 | 0.0033881
Chart: LZ SF Error (Old LDF vs New LDF) for DELMELM5:HILL_MAR_2_1
| LZ_AEN | LZ_CPS | LZ_HOUSTON | LZ_LCRA | LZ_NORTH | LZ_RAYBN | LZ_SOUTH | LZ_WEST
Average of diff_LZ_SF_old | 0.00040569 | 0.001787 | 1.6417e-05 | 0.002818 | 0.00018085 | 2.9592e-05 | 0.0010829 | 0.00038296
Average of diff_LZ_SF_new | 0.00020816 | 0.0015077 | 1.0615e-05 | 0.0029018 | 0.00024223 | 2.3609e-05 | 0.0010044 | 0.00040826
Notes: 2/9

## Slide 12: LDF performance on the constraint MLOTYUC8 : 16TH_WRD2_1 (OD 2/20/2019)
Chart: LZ_WEST SF for constraint MLOTYUC8: 16TH_WRD2_1

## Slide 13: LDF performance on the constraint MLOTYUC8 : 16TH_WRD2_1 (OD 2/20/2019)
Chart: LZ SF (Old LDF vs New LDF) for MLOTYUC8: 16TH_WRD2_1
| LZ_AEN | LZ_CPS | LZ_HOUSTON | LZ_LCRA | LZ_NORTH | LZ_RAYBN | LZ_SOUTH | LZ_WEST
Average of LZ_SF_prod_recal | 0.0040993 | 0.0048366 | 0.0036341 | 0.0043052 | 0.0026987 | 0.0026246 | 0.0049983 | -0.029994
Average of LZ_SF_old | 0.0040983 | 0.0048375 | 0.0036343 | 0.0042962 | 0.002697 | 0.0026251 | 0.0050152 | -0.028637
Average of LZ_SF_new | 0.0040996 | 0.0048366 | 0.0036341 | 0.0043005 | 0.0026953 | 0.0026218 | 0.0050258 | -0.027327
Chart: LZ SF Error (Old LDF vs New LDF) for MLOTYUC8: 16TH_WRD2_1
| LZ_AEN | LZ_CPS | LZ_HOUSTON | LZ_LCRA | LZ_NORTH | LZ_RAYBN | LZ_SOUTH | LZ_WEST
Average of diff_LZ_SF_old | 1.2038e-06 | 1.0142e-06 | 9.3858e-07 | 1.0576e-05 | 2.7204e-06 | 1.1856e-06 | 3.2927e-05 | 0.0013583
Average of diff_LZ_SF_new | 3.9116e-07 | 4.9704e-07 | 5.0943e-07 | 6.6079e-06 | 3.5696e-06 | 2.7385e-06 | 3.1326e-05 | 0.0026673
Notes: 2/20

## Slide 14: LDF performance on the constraint DDCPJON5: HOOD_DECRDVA_1 (OD 3/13/2019)
Chart: LZ_NORTH SF for constraint DDCPJON5:HOOD_DECRDVA_1
Chart: LZ_West SF for constraint DDCPJON5:HOOD_DECRDVA_1

## Slide 15: LDF performance on the constraint DDCPJON5: HOOD_DECRDVA_1 (OD 3/13/2019)
Chart: LZ SF (Old LDF vs New LDF) for DDCPJON5:HOOD_DECRDVA_1
| LZ_AEN | LZ_CPS | LZ_HOUSTON | LZ_LCRA | LZ_NORTH | LZ_RAYBN | LZ_SOUTH | LZ_WEST
Average of LZ_SF_prod_recal | 0.0025293 | 0.0039044 | -0.0014252 | 0.0038224 | -0.0079044 | -0.00091939 | 0.0026021 | 0.015887
Average of LZ_SF_old | 0.0025404 | 0.003905 | -0.001431 | 0.0038382 | -0.0074587 | -0.00094292 | 0.0026485 | 0.015937
Average of LZ_SF_new | 0.0025383 | 0.0039053 | -0.0014275 | 0.0039913 | -0.0075223 | -0.00085615 | 0.0026543 | 0.015896
Chart: LZ SF Error (Old LDF vs New LDF) for DDCPJON5:HOOD_DECRDVA_1
| LZ_AEN | LZ_CPS | LZ_HOUSTON | LZ_LCRA | LZ_NORTH | LZ_RAYBN | LZ_SOUTH | LZ_WEST
Average of diff_LZ_SF_old | 1.1191e-05 | 2.0423e-06 | 6.1087e-06 | 4.3941e-05 | 0.00044576 | 2.8743e-05 | 4.6423e-05 | 5.0182e-05
Average of diff_LZ_SF_new | 9.0248e-06 | 1.1474e-06 | 2.4375e-06 | 0.00016889 | 0.0003821 | 6.3856e-05 | 5.2171e-05 | 1.5678e-05

## Slide 16: Overall Load Zone SF Comparison for 5 Selected Days
Chart: Average SF error for 5 selected Days
| LZ_AEN | LZ_CPS | LZ_HOUSTON | LZ_LCRA | LZ_NORTH | LZ_RAYBN | LZ_SOUTH | LZ_WEST
Average of diff_LZ_SF_old | 0.00020639 | 0.00018641 | 0.00011402 | 0.00053901 | 8.6802e-05 | 0.00012427 | 0.00077473 | 0.0003727
Average of diff_LZ_SF_new | 9.336e-05 | 0.00013938 | 5.4859e-05 | 0.00055739 | 8.5701e-05 | 8.8886e-05 | 0.00047988 | 0.00055358

## Slide 17: Conclusion
By comparing LDF-based LZ shift factors, we can better understand the accuracy of LDFs on the existing RT congestions, and estimate the potential impact to RENA.
With new dynamic LDFs, the improvements have been observed in most of cases, such as LZ_SOUTH and LZ_HOUSTON. But its performance on LZ_WEST is below the expectation.
More studies will be performed to track and compare the performance of new dynamic LDFs.