## Slide 1
KP 1.3
Examples:
Clarification of Telemetered Ramp Rates For All Generation Resources
Expected Outcomes For Combined Cycle Generation Resources (CCGR) Considering Frequency Responsive Capacity
Sai Moorty
Principal, Market Design and Analysis
July 12, 2019

## Slide 2: ERRATA: June 21st Posting of two files (KP1.3)
KP1.3 PowerPoint presentation and KP1.3 Word document corrected and reposted to June 21st RTCTF meeting page
http://www.ercot.com/content/wcm/key_documents_lists/180301/5._RTC_constraints_KP1.3_062119_corrected_v2.pptx
http://www.ercot.com/content/wcm/key_documents_lists/180301/5._RTC_constraints_KP1.3_062119_corrected_v2.docx

## Slide 3: Agenda
Review examples:
Clarification of Telemetered Ramp Rates for all Generation Resources
Expected Outcomes For Combined Cycle Generation Resources (CCGR) Considering Frequency Responsive Capacity

## Slide 4: Clarification of Telemetered Ramp Rates for all Generation Resources
Ramp Rate (Up/Down):
Represent the total capacity (in MW) that the Resource can change from its current actual generation or consumption within the next five minutes divided by five.
This is what is expected today and does not change under RTC
Telem. MW
output
Normal Ramp Rate Up/Down
(MW/min)
30
5
275
350
Tel. MW output | NRRUp (MW/min) | NRRDn (MW/min)
200 | 17.5 | 30
225 | 13.33 | 30
250 | 9.17 | 30
275 | 5 | 30
310 | 5 | 5

## Slide 5: Next: Combined Cycle Generation Resource (CCGR) Constraint Examples
Purpose of the examples is to illustrate the use of the proposed CCGR specific conditional constraints
The intent of these CCGR specific conditional constraints is to economically account for the frequency responsive capacity of the CCGR when awarding energy (Base Point), Regulation and RRS-PFR.
  Given the prices, the awards for energy, Regulation, RRS provides the best economic outcome for the CCGR
  In addition, these awards will be physically feasible
  Allows the QSE to telemeter data to ERCOT-RTC that reflects the frequency responsive capability in Real-Time
Homework:
Please review examples
Provide additional scenarios
Does this proposal for accounting for frequency responsive capacity of CCGR address concerns for awarding of energy, Regulation, RRS under RTC?

## Slide 6: ERCOT Proposal: Conditional Constraints For CCGR
LSL
HSL
Tel. MW
LDL
HDL
BP
RespFactor*BP
LowRespLim
HiRespLim
Frequency Responsive Capacity
CCGR Capacity e.g. 2x1 configuration
(1-RespFactor)*BP
Lo
Hi
Non Frequency Responsive Capacity
Key constraints for ALL GR
HDL-BP-RegUp>=0
HSL-BP-RegUp-RRS
-ECRS-NSPIN>=0
BP-RegDn-LDL>=0
RegUp and RRS only provided by
frequency responsive capacity
Optimization engine does not
differentiate between
frequency and non frequency capacity
RegUp
RRS
Cond. Constraint 1
If (RegUp+RRS) > 0 then
HiRespLim - RespFactor*BP-RegUp-RRS >=0
RegDn
Cond. Constraint 2
If (RegDn > 0 then
RespFactor*BP-RegDn-LowRespLim >=0

## Slide 7: Scenario Setup For Combined Cycle Generation Resource (CCGR)
.
ST3 with 25MW
duct burner
CT1
CT2
CC component | LSL | HSL
CT1 | 75 | 100
CT2 | 75 | 100
ST3 including 25 MW Duct Burner | 50 | 150
2x1 CC configuration | 200 | 350
Telem. MW
output
Normal Ramp Rate Up/Down
(MW/min)
30
5
275
350
MW
Energy Offer Curve $/MWh
21 $/MWh
60 $/MWh
325
350

## Slide 8: Scenario Setup For Combined Cycle Generation Resource (CCGR) – cont’d
AS Offer for 2x1 CCGR
  20 MW RegUp @ $12/MW/h
  60 MW RRS-PFR @ $10/MW/h
  350 MW ECRS @ $1500/MW/h  set high to ensure 0 MW awarded for simplicity
  350 MW NSPIN @ $1500/MW/h  set high to ensure 0 MW awarded for simplicity
Note that ScalingFactorUp and ScalingFactorDn is set to 1 for the examples – i.e. no ramp sharing between energy and Regulation
Just like today, RTC will model CCGR (2x1 configuration) as a single Resource in the optimization engine
Regulation Up/Down and RRS-PFR can only be provided by the 2x1 configuration’s frequency responsive capacity
  i.e. the CT1+CT2 capacity = 200 MW
CCGR specific constraints to ensuring awards for RegUp, RegDn and RRS-PFR are feasible

## Slide 9: Scenario Setup For Combined Cycle Generation Resource (CCGR) – cont’d
: Proportion of the Base Point provided by the frequency responsive capacity of the Combined Cycle Generation Resource
  In the examples presented:
: Minimum amount of the total Base Point provided by the frequency responsive capacity of the Combined Cycle Generation Resource
  In the examples presented:
: Maximum amount of the total Base Point provided by the frequency responsive capacity of the Combined Cycle Generation Resource
  In the examples presented:
   Capacity of CT1+CT2

## Slide 10: Scenario Setup For Combined Cycle Generation Resource (CCGR) – cont’d
Apart from standard Generation Resource constraints, enforce these additional constraints if following conditions satisfied:
  Conditional constraint 1: If (RegUp+RRS-PFR) awards greater than zero
  Conditional constraint 2: If RegDn award is greater than zero

## Slide 11: Scenario Setup For Combined Cycle Generation Resource (CCGR) – cont’d
.
CT1 and CT2 capacity is frequency responsive
Example of CT1+CT2 (frequency responsive capacity) vs Steamer output
2x1 MW output | CT1+ CT2 MW | ST3 MW | HDL 2x1 | LDL 2x1 | Resp Factor | Lo Resp Lim | Hi Resp Lim
200 | 150 | 50 | 287.5 | 200 | 0.75 | 150 | 200
250 | 166 | 84 | 295.8 | 200 | 0.664 | 132.8 | 200
275 | 174 | 101 | 300 | 200 | 0.6327 | 126.5 | 200
300 | 182 | 118 | 325 | 275 | 0.6067 | 166.8 | 200
310 | 188 | 122 | 335 | 285 | 0.6065 | 172.8 | 200
325 | 200 | 125 | 350 | 300 | 0.62 | 185.7 | 200
2x1 MW output | CT1+ CT2 MW | ST3 MW | HDL 2x1 | LDL 2x1 |  | Lo Resp Lim | Hi Resp Lim
200 | 150 | 50 | 287.5 | 200 | 0.75 | 150 | 200
250 | 166 | 84 | 295.8 | 200 | 0.664 | 132.8 | 200
275 | 174 | 101 | 300 | 200 | 0.6327 | 126.5 | 200
300 | 182 | 118 | 325 | 275 | 0.6067 | 166.8 | 200
310 | 188 | 122 | 335 | 285 | 0.6065 | 172.8 | 200
325 | 200 | 125 | 350 | 300 | 0.62 | 185.7 | 200
CT1+CT2 MW output
ST3 MW output
150
200
50
125
150
Duct
Burner

## Slide 12: Example 1
Optimum solution is BP=295.83 MW, RegUp=0 MW, RRS=0 MW
Based on prices, energy is more profitable than RegUp and RRS
2x1 Telem (MW) | RespFactor | LDL (MW) | HDL (MW) | LoRespLim=RespFactor*LDL (MW) | HiRespLim (MW)
250 | 0.664 | 200 | 295.83 | 132.8 | 200
2x1 Telem (MW) |  | LDL (MW) | HDL (MW) | LoRespLim=RespFactor*LDL (MW) | HiRespLim (MW)
250 | 0.664 | 200 | 295.83 | 132.8 | 200
EOC/ LMP ($/MWh) | AS Offer/MCPC | 
 | RegUp ($/MW/h) | RRS ($/MW/h)
21/25 | 12/12 | 10/10
EnergyAward (Base Point) 2x1 MW | CT1+CT2 MW (RespFac*BP) | ST3 MW | RegUp Award (MW) | RRS Award (MW) | Revenue -OfferCost ($)
295.83 | 196.43 | 99.4 | 0 | 0 | 1183.32

## Slide 13: Example 2
Optimum solution is BP=295.83 MW, RegUp=0 MW, RRS=3.57 MW
Based on prices, RegUp and RRS more profitable than energy
However the maximum revenue to 2x1 CCGR occurs when Energy Award (Base Point)=HDL and RegUp award is zero
  RRS award limited by the HiRespLim constraint (200-(BP+RegUp+RRS )>=0)
2x1 Telem (MW) | RespFactor | LDL (MW) | HDL (MW) | LoRespLim=RespFactor*LDL (MW) | HiRespLim (MW)
250 | 0.664 | 200 | 295.83 | 132.8 | 200
2x1 Telem (MW) |  | LDL (MW) | HDL (MW) | LoRespLim=RespFactor*LDL (MW) | HiRespLim (MW)
250 | 0.664 | 200 | 295.83 | 132.8 | 200
EOC/ LMP ($/MWh) | AS Offer/MCPC | 
 | RegUp ($/MW/h) | RRS ($/MW/h)
21/25 | 12/17 | 10/15
EnergyAward (Base Point) 2x1 MW | CT1+CT2 MW (RespFac*BP) | ST3 MW | RegUp Award (MW) | RRS Award (MW) | Revenue -OfferCost ($)
295.83 | 196.43 | 99.4 | 0 | 3.57 | 1201.17
290.83 | 193.11 | 97.72 | 0 | 6.89 | 1197.77
280.83 | 186.47 | 94.36 | 10 | 3.53 | 1190.97

## Slide 14: Example 3
Optimum solution is BP=200 MW, RegUp=67.2 MW, RRS=0 MW
Based on prices, RegUp is most profitable followed by RRS and then energy
2x1 Telem (MW) | RespFactor | LDL (MW) | HDL (MW) | LoRespLim=RespFactor*LDL (MW) | HiRespLim (MW)
250 | 0.664 | 200 | 295.83 | 132.8 | 200
2x1 Telem (MW) |  | LDL (MW) | HDL (MW) | LoRespLim=RespFactor*LDL (MW) | HiRespLim (MW)
250 | 0.664 | 200 | 295.83 | 132.8 | 200
EOC/ LMP ($/MWh) | AS Offer/MCPC | 
 | RegUp ($/MW/h) | RRS ($/MW/h)
21/25 | 12/19 | 10/15
EnergyAward (Base Point) 2x1 MW | CT1+CT2 MW (RespFac*BP) | ST3 MW | RegUp Award (MW) | RRS Award (MW) | Revenue -OfferCost ($)
200 | 132.8 | 67.2 | 67.2 | 0 | 1270.4
271.1 | 180 | 91.1 | 20 | 0 | 1224.4
295.83 | 196.43 | 99.4 | 0 | 3.57 | 1201.17
280.83 | 186.47 | 94.35 | 10 | 3.53 | 1210.97
180.72 | 120 | 60.72 | 20 | 60 | 1162.89

## Slide 15: Example 4
Optimum solution is BP=325 MW, RegUp=0 MW, RRS=0 MW
Based on prices, energy is more profitable than RegUp and RRS
Energy award (Base Point) is 325 MW as the cost is $60/MWh above this level
2x1 Telem (MW) | RespFactor | LDL (MW) | HDL (MW) | LoRespLim=RespFactor*LDL (MW) | HiRespLim (MW)
310 | 0.6065 | 285 | 335 | 172.84 | 200
2x1 Telem (MW) |  | LDL (MW) | HDL (MW) | LoRespLim=RespFactor*LDL (MW) | HiRespLim (MW)
310 | 0.6065 | 285 | 335 | 172.84 | 200
EOC/ LMP ($/MWh) | AS Offer/MCPC | 
 | RegUp ($/MW/h) | RRS ($/MW/h)
21/25 | 12/12 | 10/10
EnergyAward (Base Point) 2x1 MW | CT1+CT2 MW (RespFac*BP) | ST3 MW | RegUp Award (MW) | RRS Award (MW) | Revenue -OfferCost ($)
325 | 197.1 | 127.9 | 0 | 0 | 1300

## Slide 16: Example 5
Optimum solution is BP=325 MW, RegUp=1.45 MW, RRS=1.45 MW
Based on prices, RegUp and RRS more profitable than energy
Energy award (Base Point) is 325 MW as the cost is $60/MWh above this level
2x1 Telem (MW) | RespFactor | LDL (MW) | HDL (MW) | LoRespLim=RespFactor*LDL (MW) | HiRespLim (MW)
310 | 0.6065 | 285 | 335 | 172.84 | 200
2x1 Telem (MW) |  | LDL (MW) | HDL (MW) | LoRespLim=RespFactor*LDL (MW) | HiRespLim (MW)
310 | 0.6065 | 285 | 335 | 172.84 | 200
EOC/ LMP ($/MWh) | AS Offer/MCPC | 
 | RegUp ($/MW/h) | RRS ($/MW/h)
21/25 | 12/17 | 10/15
EnergyAward (Base Point) 2x1 MW | CT1+CT2 MW (RespFac*BP) | ST3 MW | RegUp Award (MW) | RRS Award (MW) | Revenue -OfferCost ($)
325 | 197.1 | 127.9 | 1.45 | 1.45 | 1314.52
290 | 175.87 | 114.13 | 10 | 14.13 | 1280.65

## Slide 17: Example 6
Optimum solution is BP=285 MW, RegUp=27.16 MW, RRS=0 MW
Based on prices, RegUp and RRS more profitable than energy
2x1 Telem (MW) | RespFactor | LDL (MW) | HDL (MW) | LoRespLim=RespFactor*LDL (MW) | HiRespLim (MW)
310 | 0.6065 | 285 | 335 | 172.84 | 200
2x1 Telem (MW) |  | LDL (MW) | HDL (MW) | LoRespLim=RespFactor*LDL (MW) | HiRespLim (MW)
310 | 0.6065 | 285 | 335 | 172.84 | 200
EOC/ LMP ($/MWh) | AS Offer/MCPC | 
 | RegUp ($/MW/h) | RRS ($/MW/h)
21/25 | 12/19 | 10/15
EnergyAward (Base Point) 2x1 MW | CT1+CT2 MW (RespFac*BP) | ST3 MW | RegUp Award (MW) | RRS Award (MW) | Revenue -OfferCost ($)
285=LDL | 172.84 | 112.16 | 27.16 | 0 | 1330.13
296.8 | 179.99 | 116.8 | 20 | 0 | 1327.24
290 | 175.87 | 114.13 | 20 | 4.13 | 1320.65
325=HDL | 197.1 | 127.9 | 2.9 | 0 | 1320.32

## Slide 18
Discussion

## Slide 19
Appendix

## Slide 20: Recap: On-Line Generation Resource Constraints (ALL)
Other constraints that limit AS awards based on new telemetry, qualified MW, ramp rates (if applicable)
LDL/LSL constraints to ensure energy and RegDn awards are feasible

## Slide 21: Recap: On-Line Generation Resource Constraints (ALL) – cont’d
HDL constraint to ensure energy and RegUp awards are feasible
HSL constraint to ensure energy and RegUp,RRS (PFR), ECRS and NSPIN awards are feasible