## Slide 1
Item 3a – Ancillary Service Demand Curves for Real-Time Co-Optimization
Dan Jones
August 9, 2019

## Slide 2: Objective and Approach
For RTC, produce individual ancillary service demand curves (ASDCs) that are, in aggregate, as consistent as possible with anticipated pricing outcomes for the ORDC methodology that will be effective March 1, 2020
Already specified by the PUCT:
  NPRR 863 AS Products (Reg-Up, RRS, ECRS, NSRS)
  VOLL = $9,000/MWh
  SWOC = $2,000/MWh
  Maximum ASDC value = $9,000/MWh (cover 0 to 2,000 MW of reserves)
  Maximum Energy Price (exclusive of congestion) capped at $9,000/MWh
This presentation addresses the approach for:
  Developing an aggregate, single curve representation for the 2020 ORDC as a function of total online and offline reserves; and
  II. Dividing the single aggregate 2020 ORDC into individual ASDCs for Reg Up, RRS, ECRS and NSRS that vary by hour depending on the minimum AS requirements
Separately, also need to develop a Reg-Down demand curve

## Slide 3
I. Developing an aggregate, single curve representation for the 2020 ORDC

## Slide 4: Developing a Single 2020 ORDC
Time period considered
  Jun 1, 2014 through Dec 31, 2018
Data considered at SCED granularity
  RTOLCAP
  RTOFFCAP
  X = 2,000 MW
  2020 mu () substituted for production mu
  2020 sigma () substituted for production sigma
Composite LOLP calculation used

## Slide 5: Capacity levels < 10,000 MW
  Composite Price ($/MWh)
  ~90k SCED intervals out of ~480k intervals examined where
  A locally estimated scatterplot smoothing (LOESS) regression curve was added to the data to create a smooth composite LOLP curve
*System lambda is limited to $2,000 to be consistent with the maximum marginal cost of energy under RTC

## Slide 6: Capacity levels < 10,000 MW
To extend the curve to 2,000 MW of total reserves due to the absence of historical data points
Used a system lambda of $493 which was the average system lambda for data points less than 4,000 MW of total reserves
Assumed
  This is in alignment with the existing process of setting RTOFFCAP = 0 once EEA Level 1 is initiated
Extended
Section

## Slide 7
II. Dividing the single aggregate 2020 ORDC into individual ASDCs

## Slide 8: Dividing the Aggregate ORDC into ASDCs: Approach
Current scarcity pricing consists of the combination of ORDC and PBPC
PBPC is a proxy for a Reg-Up demand curve in the current design
Can use the PBPC to inform where to “drop” AS MW into the Aggregate ORDC curve
Chart: Power Balance Penalty Curve
| 0 | 5 | 5 | 10 | 10 | 20 | 20 | 30 | 30 | 40 | 40 | 50 | 50 | 100 | 100 | 150 | 150 | 200 | 200 | 220
 | 250 | 250 | 300 | 300 | 400 | 400 | 500 | 500 | 1000 | 1000 | 2250 | 2250 | 4500 | 4500 | 6000 | 6000 | 7500 | 7500 | 9001 | 9001

## Slide 9: Dividing the Aggregate ORDC into ASDCs
Step 1: Reserve 100 MW each of Reg-Up and RRS on aggregate ORDC consistent with PBPC pricing
Reg-Up RRS ECRS NSRS
175 2300 1268 107
Jul-19 HE22
NPRR 863 Requirements

## Slide 10: Dividing the Aggregate ORDC into ASDCs
Step 2: Place at highest priced open MWs on the aggregate ORDC
Reg-Up RRS ECRS NSRS
175 2300 1268 107
Jul-19 HE22
NPRR 863 Requirements

## Slide 11: Dividing the Aggregate ORDC into ASDCs
Step 3: Place at highest priced open MWs on the aggregate ORDC
Reg-Up RRS ECRS NSRS
175 2300 1268 107
Jul-19 HE22
NPRR 863 Requirements

## Slide 12: Dividing the Aggregate ORDC into ASDCs
Step 4: Place ECRS Requirement at highest priced open MWs on the aggregate ORDC
Reg-Up RRS ECRS NSRS
175 2300 1268 107
Jul-19 HE22
NPRR 863 Requirements

## Slide 13: Dividing the Aggregate ORDC into ASDCs
Step 5: Place NSRS Requirement at highest priced open MWs on the aggregate ORDC
Reg-Up RRS ECRS NSRS
175 2300 1268 107
Jul-19 HE22
NPRR 863 Requirements

## Slide 14: Dividing the Aggregate ORDC into ASDCs
Step 6: Fill remaining MWs on the aggregate ORDC priced at >= $0.01 as NSRS
ORDC reserves today are most similar to NSRS, so it seems appropriate to assign the remainder of the aggregate curve to that product (I.e., assigning it to other services would be more restrictive than the ORDC)
Reg-Up RRS ECRS NSRS
175 2300 1268 107
Jul-19 HE22
NPRR 863 Requirements

## Slide 15: Resulting ASDCs: July-19 HE22
Reg-Up RRS ECRS NSRS
175 2300 1268 107
Jul-19 HE22
NPRR 863 Requirements

## Slide 16: Resulting ASDCs: Feb-19 HE7
Reg-Up RRS ECRS NSRS
623 2840 690 1442
Feb-19 HE7
NPRR 863 Requirements
While the underlying composite curve would remain unchanged, the individual ASDCs would adjust hourly to reflect the change in AS requirements

## Slide 17: Resulting ASDCs: Feb-19 HE7
Non-Spin Requirement
Reg-Up RRS ECRS NSRS
623 2840 690 1442
Feb-19 HE7
NPRR 863 Requirements

## Slide 18: Comparison of the Two Example Hours
Feb-19 HE7
Jul-19 HE22

## Slide 19: Comparison of the Two Example Hours

## Slide 20: Questions and Additional Discussion