## Slide 1
MTLF Overview
Calvin Opheim
Load Forecasting & Analysis
WMWG
August 19, 2019

## Slide 2: Outline of Today’s Presentation
MTLF Models
Input Variables
Forecast Horizons
Questions

## Slide 3
MTLF Models

## Slide 4: MTLF Models
7 models are currently available
  5 are internally developed
  Named E, E1, E2, E3, and M
  2 are legacy “black box” models from GE
  Named A3 and A6

## Slide 5: MTLF Models
A3 Notes
  Uses recent history to update the model coefficients
  Prone to significantly over-forecast summer demands on very hot days
  Prone to significantly over-forecast winter demands on very cold days

## Slide 6: MTLF Models
A6 Notes
  Uses recent history to update the model coefficients
  Only uses one weather station per weather zone
  Prone to significantly over-forecast summer demands on very hot days
  Prone to significantly over-forecast winter demands on very cold days

## Slide 7: MTLF Models
E Notes
  Considered to be the overall best model for Day Ahead
  Slow to change during shorter forecast horizons (1 – 4 hours ahead)
  Calibrated based on most recent historical days (look back at the last 7 – 14 days)
  Tuned based on forecast performance during the current day (look back at the last 3 hours)

## Slide 8: MTLF Models
E1 Notes
  Designed to be the most responsive model to changing conditions
  Designed to perform well on very hot and very cold days
  Does not do well on mild days
  Can result in a jagged forecast shape
  Tuned based on forecast performance from the last hour

## Slide 9: MTLF Models
E2 Notes
  Looks more at rain and cloud cover
  More reliant on the weather forecast for the next 14 hours
  Best at capturing Winter/Spring/Fall rain type and cloud cover patterns
  Tendency to under forecast very hot conditions
  Calibrated based on most recent historical days (look back at the last 7 – 14 days)
  Tuned based on forecast performance during the current day (look back at the last 3 hours)

## Slide 10: MTLF Models
E3 Notes
  Provides more weight on weather for shorter term forecasts
  Relatively slow to change
  Input from additional weather stations
  Calibrated based on most recent historical days (look back at the last 7 – 14 days)
  Tuned based on forecast performance during the current day (look back at the last 3 hours)

## Slide 11: MTLF Models
M Notes
  The average of the 6 other models
  Historically has shown to be the best Day Ahead forecast
  Provides a good benchmark for other models

## Slide 12: MTLF Models
Chart: Day Ahead MAPE
| 2015 | 2016 | 2017 | 2018 | 2019
Active Forecast | 0.028598 | 0.026318 | 0.025622 | 0.023521 | 0.026
M | 0.019842 | 0.020662 | 0.024411

## Slide 13
Input Variables

## Slide 14: Weather Zones
Notes: WEST peak was in July

## Slide 15: Original Weather Stations

## Slide 16: Current Weather Stations

## Slide 17: Variables
Model | Day Of Week | Holiday | Daylight Savings | Season | Dry Bulb | Dew Point | Cloud Cover | Wind Speed | Heat Index
E | X | X | X | X | X | X | X | X | X
E1 | X | X | X |  | X | X |  | X | 
E2 | X | X | X | X | X | X | X | X | X
E3 | X | X | X | X | X | X | X | X | X
A3 | X | X | X |  | X | X | X | X | X
A6 | X | X | X |  | X | X |  |  | 
Model | Wind Chill | Wetbulb | Sunshine Minutes | Solar Irradiance | Relative Humidity | Precipitation | HDD | CDD
E | X | X |  | X | X |  | *E | *E
E1 |  |  |  |  |  |  |  | 
E2 | X | X |  | X |  | X | *E | *E
E3 | X | X |  | X | X |  | *E | *E
A3 | X | X | X |  | X |  |  | 
A6 |  |  | X |  | X |  |  | 
Note *E indicates used in energy model only

## Slide 18: Previous Load Values
Use previous observed load values
  Examples: to predict the load at 5 pm, use the actual load from
  4 pm
Referred to as an autoregressive model

## Slide 19
Forecast Horizons

## Slide 20: Forecast Horizons
Mid-Term Load Forecast (MTLF)
  Hourly forecast for the next 7 days
Hour Ahead/Real Time Forecast
Day Ahead Forecast

## Slide 21: Flowchart
Blended Forecast
Backcast Adjustment
Hour Ahead Models
(autoregressive)
Day Ahead Models
(non autoregressive)
Tuning Adjustment
Final Forecast

## Slide 22: Real Time / Hour Ahead Forecast
Created every hour
  Hourly forecast for the next 7 days beginning with the next hour
Hour Ahead models include lagged load values
  The actual load from the previous hour is the most significant variable to predict the load for the current hour.
  Example: to predict the load at 5 pm, use the actual load from
  4 pm
Referred to as an autoregressive model

## Slide 23: Day Ahead Forecast
Created at 2 pm every day
  Hourly forecast for the next 7 days beginning tomorrow
Day Ahead models do not include any lagged load values
  The last actual load value would be for 1 pm today. This is not a significant variable for predict the load for tomorrow

## Slide 24: Summary
The E, E2, and E3 models consist of two different forecasting models (hour ahead and day ahead)
E1 only uses day ahead models
A3 and A6 only use a single model. They do not have a backcast feature. They recalculate the model coefficients based on recent performance. This is not the same as the tuning feature mentioned on the previous slide.

## Slide 25: Summary
The hour ahead models are used to forecast the next few hours (1 to 4 hours). Then the day ahead models are used.
Day ahead models can incorporate adjustments based on performance from prior days (backcast)
The hour ahead and day ahead models can be blended together
The forecast can be adjusted based on the most recent forecast performance (tuning)

## Slide 26: Questions?