## Slide 1
Ancillary Services Settlement Under RTC - Examples
Pamela Shaw
May 13, 2019

## Slide 2: Agenda
  Review principle language
  Review formula
  Settlement discussion – unit trip carrying AS
  Examples:
    System requirements change under 3 conditions:
      DAM AS = RTC AS
      RTC AS > DAM AS
      RTC AS < DAM AS
    Scenarios:
    QSE with resource w/Self Arranged
    QSE with resource w/AS Trades
    QSE with resource w/DAM award and resource trip
    QSE with resource w/RTM award > DAM award
    QSE with Resource that has a trade
    QSE with Load obligation that changes between DAM and RTM

## Slide 3: Principle Language
Note: The following principles are not impacted by any change to the DAM framework currently being considered at the PUCT.
  1.6 The current AS imbalance settlement processes for ORDC will be replaced with a new process in RTC.
    1.6.1 This process will not create new sources of uplift or make-whole for Load Serving Entities (LSEs).
    1.6.2 There will be a separate AS imbalance calculation for each AS product.
    1.6.3 Non-zero net AS imbalance amounts will be charged or paid to QSEs on a Load Ratio Share (LRS) basis. If the DAM award plus self-arrangement MW amounts are exactly balanced with the RTM award MW amounts, there will be no LRS-based charges or payment (i.e., AS imbalance charges and payments will be exchanges between AS suppliers).
    1.6.4 The basis for the approach to the new AS imbalance calculation is the current process for energy imbalance payments and charges.
    1.6.5 The RTM obligation for a QSE is equal to the RTM LRS multiplied by sum of all RTM awards (i.e., there is no portfolio self-arrangement for the RTM).

## Slide 4: Example Formulas: Regulation Up Service with RTC
  In the DAM Settlement for each hour:
  Equation #1:
  Regulation Up Service Payment;
  PCRUAMT q = (-1) * MCPCRU DAM * PCRU q
  Equation #2:
  Regulation Up Service Charge;
  DARUAMT q = DARUPR * DARUQ q
  In the RTM Settlement:
  Equation #3:
  DARTPCRUAMTq= ((DARUOBL'q – DARUSA1 )* MCPCRU DAM) – DARUAMTq
  Where: DARUOBL'q = (DAM AS Plan) * HLRSq
  1. Correction to previous presented slides

## Slide 5: Example Formulas: Regulation Up Service with RTC
  In the RTM Settlement:
  Equation #4:
  RTRUIMBAMTq =
  (-1) * (.25) * { ∑ r [(RTRUAWDr * RTRUMCPCRPr) - (DARUAWDr * RTRUMCPC)] -
  (DARUSA * RTRUMCPC) + (RUTP - RUTS) * RTRUMCPC }
  Equation #5:
  LARTRUIMBAMTq =
  -1 * ∑q RTRUIMBAMT * LRSq
Pink = RTC Award * RTC Resource Specific Price
Blue = DAM Award * RTC SCED weighted price
Purple = DAM Self Arranged * RTC SCED weighted price
Green = RU Trades * RTC SCED weighted price

## Slide 6: Unit Trip Carrying AS
  Unit X awarded AS @13:05
  Unit X trips offline @13:06:30
  Two possible outcomes:
    Frequency Event
      If certain system conditions exist and the unit trip causes the frequency to dip to 59.91, RRS will be triggered and RTC will run again.
      The RTC awards Unit Y the AS
      The RTC does not award Unit X and there are no financial impacts (unless carrying a DAM award)
    No Frequency Event
      Unit X communicates to ERCOT that the unit has tripped off and can’t provide AS
      Next RTC at 13:10, Unit Y is awarded AS
      The RTC does not award Unit X and there are no financial impacts (unless carrying a DAM award)

## Slide 7: Settlement Example1
      15-minute settlement interval
      DAM AS = RTC AS
        Supply side:
        QSE 1 Resource trips offline in 2nd RTC
        QSE 2 has a trade sale
        QSE 3 Self arranged and trade purchase plus RTC AS award that makes up for tripped unit
        Demand side:
        QSE 3 and QSE 4 have OBL change in DAM and RTM
        QSE 5 has DAM OBL but no RTM OBL

## Slide 8: Settlement example 1

## Slide 9: Settlement Example 2
      15-minute settlement interval
      RTC AS > DAM AS
        Supply side:
        QSE 1 Resource awarded in DAM & RTC
        QSE 2 Resource awarded in DAM & RTC
        QSE 3 Resource awarded in one SCED interval for additional AS above plan
        Demand side:
        QSE 3 - QSE 5 OBL and OBL' same as example 1
        QSE 3 - QSE 4 charged additional AS per LRS

## Slide 10: Settlement Example 2

## Slide 11: Settlement Example 3
      15-minute settlement interval
      Prices increase in DAM and RTC
      RTC AS < DAM AS
        Supply side:
        QSE 1 Resource awarded in DAM & RTC award is less than DAM award
        QSE 2 Resource awarded in DAM & RTC
        QSE 3 Not awarded DAM or RTC
        Demand side:
        QSE 3 - QSE 5 OBL and OBL' change from DAM to RTM
        QSE 3 - QSE 5 charged additional AS per LRS

## Slide 12: Settlement Example 3

## Slide 13: Next Steps
  Post Ancillary Service Imbalance Settlement Principle document for comments
  ?