## Slide 1
Potential Impacts of Intra-Hour Energy Offer Curve Submissions on SCED Performance
ERCOT Staff
WMWG
August 19, 2019

## Slide 2: SCED data reads: How it works today
Some data is static for the full Operating Day
  Example: Resource parameters
Some data changes by the hour
  Energy Offer Curves
  Mitigated Offer Cap Curves & Offer Floor

## Slide 3: SCED data reads: How it works today
Some data changes in real time, with every SCED run. For example:
  Resource status
  MW
  LDL/HDL
  Transmission constraints
Normally:
  SCED run at top of HE 01 takes the longest
  SCED run at top of each hour is second-longest
  Intra-hour SCED runs are the fastest

## Slide 4: 2019 SCED timestamps
Jan. 1 thru July 10, 2019 SCED average run times :
SCED Type | No. of runs | Mean (seconds)
1st of Day | 191 | 18.3
1st of Hour | 4,751 | 16.0
Others | 54,534 | 12.2
This data indicates that intra-hour SCED runs that include reads of new EOCs should increase run time by less than 4 seconds, on average
ERCOT cautions that this is only an estimate; results after actual implementation could vary

## Slide 5: Cautionary notes
Intra-hour EOCs for storage resources should not be implemented without first developing mitigation rules for storage
There will be system impacts, magnitude currently unknown:
  Settlements
  Market Management System
  MIS Reports
  Others….