## Slide 1
Key Principle 5 –
Day-Ahead Market
Carrie Bivens
August 27, 2019

## Slide 2: Introduction
Since the PUCT has provided direction on the scope of DAM changes to consider for RTC, it is appropriate for the task force to go ahead and move forward with discussions on three items from Key Principle 5 on the tracking spreadsheet:
  Ancillary Service Demand Curves (ASDCs) in the DAM;
  Changes to the current DAM AS insufficiency process; and
  Impacts on AS Obligation process for Load-Serving Entities (LSEs) if ASDCs in the DAM

## Slide 3: Current AS Plan Procurement
In current DAM implementation, the last MW of each Ancillary Service is just as “important” to the optimization as the first
  AS Plan is modeled as constraints with very high penalty costs
    This is analogous to having vertical AS demand functions, and the optimization will take any necessary step to procure every single MW in the AS plan.
  Example of OD 2/6/13:
    DAM cleared $3k prices for all AS for Hour 1 due to a shortage in available Non-Spin offers. A small quantity, 4.4 MWs, was struck at $3k and set the clearing price.

## Slide 4: Setting MCPCs when Insufficient
In the current implementation, if DAM does not have sufficient offers to clear the entire AS plan:
  First, it will use the DAM optimization penalty costs for purposes of prioritizing each of the Ancillary Services and ensuring that any resource necessary to provide the service would be available to Unit Commitment
    Reg-Up and Reg-Dn = $3M
    RRS = $2M
    Non-Spin = $1M
  Then, if the penalty costs end up setting any of the MCPCs, the DAM operator will do a “pricing run” prior to publishing
    The pricing run relaxes the AS constraint such that the penalty costs are removed from the published MCPCs.
Protocol reference: Section 4.5.2, Ancillary Service Insufficiency

## Slide 5: ASDCs in DAM
Under RTC, prices will be established for each AS that reflect the lost reserve value in the case of a shortage in real-time.
If an AS shortage exists in DAM, large or small, then ASDCs should determine how much clears and at what price, rather than the current process.
  Refines the quantity of procurement to reflect the fact that the first MW is more valuable than the last
  Clearing prices become more reflective of the actual scarcity
Outcomes should be consistent with real-time.
  Helps ensure that DAM will continue to be the primary source for forward procurement of AS capacity, rather than relying on RUC, by aligning the day-ahead and real-time
Therefore, DAM should use the same ASDCs as SCED.

## Slide 6: Simplified Examples
  DAM example with no ASDC (current implementation) when short AS (illustrative only)
    All examples here are simplified with only one AS product, no energy offer shortage, no resource or transmission constraints, no curves
 | MW | Price
Energy Bid | 200 | $125
G1 energy offer | 100 | $30
G1 RRS offer | 45 | $40
G2 energy offer | 150 | $50
Awards | MW
G1 energy | 55
G2 energy | 145
G1 RRS | 45
RRS Plan = 50 MW
Prices | 
System lambda | $50
MCPC | $60*
* reflects $20 opportunity cost of energy for G1

## Slide 7: Simplified Examples
  DAM example with basic ASDC when short AS (illustrative only)
 | MW | Price
Energy Bid | 200 | $125
G1 energy offer | 100 | $30
G1 RRS offer | 45 | $40
G2 energy offer | 150 | $50
Awards | MW
G1 energy | 55
G2 energy | 145
G1 RRS | 45
RRS Plan = 50 MW
Prices | 
System lambda | $50
MCPC | $100*
* reflects RRS demand curve price

## Slide 8: Simplified Examples
  DAM example with basic ASDC when offer is higher than lowest portion of ASDC (illustrative only)
 | MW | Price
Energy Bid | 200 | $125
G1 energy offer | 100 | $30
G1 RRS offer | 45 | $120
G2 energy offer | 150 | $50
Awards | MW
G1 energy | 60
G2 energy | 140
G1 RRS | 40**
RRS Plan = 50 MW
Prices | 
System lambda | $50
MCPC | $140*
** Constrained by RRS demand curve
* reflects $20 opportunity cost of energy for G1

## Slide 9: AS Obligation Changes
Ancillary Services Obligation will continue to be published by 6 am in the day-ahead.
  This will become an advisory number based on the AS Plan
  It will be used for Self-Arranged AS transaction validation (e.g., for RRS when determining allowable UFR MWs per QSE.)
Minimum AS Obligation quantity will be 0.1 MW.
After DAM is complete, an updated AS Obligation will be published based on actual AS procurement quantities, if different.
  With ASDCS in DAM, fewer MWs could be procured than the AS Plan for any service, and more MWs could be procured for any service with a curve that extends past the AS Plan quantity.
ERCOT will use this updated quantity for DAM AS settlement for QSEs with load ratio shares.
Protocol reference: Section 4.2.1.2, Obligation Assignment and Notice

## Slide 10: Draft Key Principle Concepts
KP5
  ASDCs will be added to the DAM optimization.
  The same ASDCs in SCED will be used in DAM.
  Eliminate the current DAM AS insufficiency process
    Remove process of reopening submission window for more offers
    Remove current pricing run
  AS Obligation quantities will be updated for settlement based on actual DAM AS quantities procured, if different from the AS Plan quantities.

## Slide 11: Additional Discussion
Open question
  Due to the fact that there is no power balance penalty curve in DAM (Energy Bids provide a similar function when energy is scarce), does the offer cap for DAM need to be different than real-time?

## Slide 12: Questions?