## Slide 1
Item 3c –Key Principle 1.3
Ancillary Service Awarding and Imbalance Discussion and Examples
RTCTF
August 27, 2019

## Slide 2: Acronyms
Ancillary Service (AS)
Day-Ahead Market (DAM)
ERCOT Contingency Reserve Service (ECRS)
Key Principle (KP)
High Sustained Limit (HSL)
Max Power Consumption (MPC)
Market Clearing Price for Capacity (MCPC)
Net Power Flow (NPF)
Non-Spinning Reserve Service (Non-Spin)
Physical Responsive Capability (PRC)
Primary Frequency Response (PFR)
Qualified Scheduling Entity (QSE)
Real-Time Co-optimization (RTC)
Real-Time Co-optimization Task Force (RTCTF)
Regulation Up Service (Reg-Up)

## Slide 3: ERCOT’s KP1.3 Comments
ERCOT posted comments to KP1.3 on August 20, 2019 changing the previously drafted shared principle concepts.
ERCOT had previously proposed that Load Resources providing UFR-type AS would continue to get awarded the same amount of AS, even after being manually deployed for the AS and no longer consuming energy.
The latest comments amend that treatment to state that, once a Load Resource providing UFR-type AS has been deployed, RTC will attempt to procure that AS from Resources that are shown to be available to provide that AS during the subsequent executions.
The general intent of RTC is to take a fresh look at the system during each execution to see what Resources are currently available for awarding of AS and energy.

## Slide 4: ERCOT’s KP1.3 Comments cont.
With additional discussion and in thinking about the current design, we identified issues with what we proposed at the August 9, 2019 RTCTF:
  The treatment for Load Resource that are manually deployed for UFR-type AS was different than the treatment in other cases (e.g., other methods of deployment and other Resource types) and this difference did not seem warranted.
  This different treatment would reduce AS Imbalance charges to Load Resources and, in doing so, create additional cost to Load relative to today’s design.
  Having RTC think the UFR-type RRS can be awarded and is still available for deployment can create operational issues, specifically during an EEA.

## Slide 5: Example of EEA Operation
System Condition is going from EEA Level 1 into EEA Level 2
UFR RRS is deployed during EEA Level 2
Scenario Setup
  68,000 MW of frequency responsive generation capacity (FR Gen)
    EOC of $25/MWh
    AS Offer of $0/MW for URS, RRS, ECRS
  2,000 MW of non-frequency responsive generation capacity (NFRC Gen)
    EOC of $40/MWh
    AS Offer of $0/MW for ECRS
  Reg-Up Demand Curve is one block of 200 MW @ $9,000/MW
  RRS Demand Curve is two blocks, 1,800MW @ $9,000/MW and 500 MW @ $6,000/MW – assume the UFR RRS limit is 1,150 MW
  ECRS Demand Curve is one block of 1,500 MW @ $2,000/MW
  1,150 MW of UFR RRS awarded in the DAM (50% limit on RRS)
$9,000
200
Reg-Up
1800
$9,000
2300
$6,000
RRS
1500
$2,000
ECRS

## Slide 6: Example of EEA Operation cont.
RTC Awards, UFR RRS Deployed during EEA Level 2
EEA Level | FR Gen HSL | NFRC Gen HSL | Load | LRS RRS Award | Gen Reg-Up Award | Gen RRS Award | Gen ECRS Award |  | FR Gen BP | NFRC Gen BP |  | PRC
1 | 68,000 | 2,000 | 69,000 | 1,150 | 100 | 900 | 0 |  | 67,000 | 2,000 |  | 2,150
1 | 68,000 | 2,000 | 69,400 | 1,150 | 60 | 540 | 0 |  | 67,400 | 2,000 |  | 1,750
Current Proposal |  |  |  | Intervals after EEA2 UFR deployment with no RRS award to already deployed UFR |  |  |  |  |  |  |  | 
2 | 68,000 | 2,000 | 68,250 | 0 | 175 | 1,575 | 0 |  | 66,250 | 2,000 |  | 1,750
2 | 68,000 | 2,000 | 67,500 | 0 | 200 | 2,300 | 0 |  | 65,500 | 2,000 |  | 2,500
Original Proposal |  |  |  | Intervals after EEA2 UFR deployment with continued RRS award to already deployed UFR |  |  |  |  |  |  |  | 
2 | 68,000 | 2,000 | 68,250 | 1,150 | 200 | 1,150 | 400 |  | 66,650 | 1,600 |  | 1,350
2 | 68,000 | 2,000 | 67,500 | 1,150 | 200 | 1,150 | 1,150 |  | 66,650 | 850 |  | 1,350
Original Proposal:
RTC optimization continues to assume that the RRS is being provided by the deployed Load Resources
Therefore, it only attempts to procure the remaining 1150 MW RRS and awards cheaper frequency responsive capacity for energy and backs down non-frequency responsive capability.
This leads to PRC decreasing as opposed to improving, delaying the exit from EEA 2.
Current Proposal:
RTC optimization uses actual system conditions and recognizes lack of available RRS in system and attempts to procure based on the RRS Demand Curve.
This leads to continued energy awards to non-frequency responsive capacity and PRC improving, thus allowing for quicker exit from EEA 2.

## Slide 7: Example of EEA Operation cont.
Key points from the example:
  Leading up to the event, the optimization is trying to reserve frequency responsive capability, even if that means using more expensive energy.
  When UFR Load Resources providing RRS have been manually deployed in EEA 2, this creates additional headroom on Generation Resources to provide AS.
  If the optimization continues to assume that the RRS is being provided by the deployed Load Resources, it may think there is sufficient frequency responsive capability on the system and dispatch frequency responsive capacity for energy while keeping headroom on available non-frequency responsive capability. This leads to PRC decreasing as opposed to improving.
  However, if the optimization treats this deployment like other cases and attempts to procure the full RRS amount from other available Resources, non-frequency responsive capability will be utilized for energy and PRC should be able to recover more quickly.

## Slide 8: Settlement in the EEA Operation
DAM Results
Total Load MW | LMP $/MWh | Reg-Up MCPC $/MW | RRS MCPC $/MW | ECRS MCPC $/MW
67,150 | 2040 | 2015 | 2015 | 2000
Total Load MW | Rest Of System Load | UFR Load Resource |  | FR Gen |  |  |  | NFRC Gen | 
 | Energy Award MW |  |  |  |  |  |  |  | 
 |  | Energy Award MW | RRS Award MW | Energy Award MW | Reg-Up Award MW | RRS Award MW | ECRS Award MW | Energy Award MW | ECRS Award MW
67,150 | 66,000 | 1,150 | 1,150 | 66,500 | 200 | 1150 | 0 | 500 | 1500

## Slide 9: Settlement in the EEA Operation cont.
System Condition: EEA Level 1, Results for two intervals
UFR Load Resource not deployed and normal RTC run
Prices
RT Imbalance Settlements
EEA Level | Total Load | LMP | Reg-Up MCPC | RRS MCPC | ECRS MCPC
1 | 69000 | 6025 | 6000 | 6000 | 5985
1 | 69400 | 9000 | 8975 | 8975 | 5960
EEA Level | FR Gen |  |  | NFRC Gen |  |  | UFR LR |  |  |  | Rest Of System Load |  | 
 | $ Energy Imb. | $ AS Imb. | $ Total Imb. | $ Energy Imb. | $ AS Imb. | $ Total Imb. | $ Energy Imb. | $ AS Imb. | $ RT LA AS Imb. | $ Total Imb. | $ Energy Imb. | $ RT LA AS Imb. | $ Total Imb.
1 | (175,729) | 175,000 | (729) | (753,125) | 748,125 | (5,000) | 0 | 0 | (15,385) | (15,385) | 928,854 | (907,740) | 21,115
1 | (562,500) | 560,938 | (1,563) | (1,125,000) | 745,000 | (380,000) | 0 | 0 | (21,640) | (21,640) | 1,687,500 | (1,284,297) | 403,203

## Slide 10: Settlement in the EEA Operation cont.
System Condition: EEA Level 2, Results for two intervals
UFR Load Resource deployed: RTC dispatch and Pricing run
Prices
  Same under both proposals
RT Imbalance Settlements: Current Proposal
RT Imbalance Settlements: Original Proposal
EEA Level | Total Load | LMP | Reg-Up MCPC | RRS MCPC | ECRS MCPC
2 | 68250 | 9000 | 8975 | 8975 | 5960
2 | 67500 | 6025 | 6000 | 6000 | 5985
EEA Level | FR Gen |  |  | NFRC Gen |  |  | UFR LR |  |  |  | Rest Of System Load |  | 
 | $ Energy Imb. | $ AS Imb. | $ Total Imb. | $ Energy Imb. | $ AS Imb. | $ Total Imb. | $ Energy Imb. | $ AS Imb. | $ RT LA AS Imb. | $ Total Imb. | $ Energy Imb. | $ RT LA AS Imb. | $ Total Imb.
2 | 300,000 | (299,166) | 833 | (1,125,000) | 745,000 | (380,000) | (862,500) | 860,104 | 0 | (2,396) | 1,687,500 | (1,305,937) | 381,562
2 | 577,396 | (575,000) | 2,396 | (753125) | 748125 | (5,000) | (577,396) | 575,000 | 0 | (2,396) | 753,125 | (748,125) | 5,000
EEA Level | FR Gen |  |  | NFRC Gen |  |  | UFR LR |  |  |  | Rest Of System Load |  | 
 | $ Energy Imb. | $ AS Imb. | $ Total Imb. | $ Energy Imb. | $ AS Imb. | $ Total Imb. | $ Energy Imb. | $ AS Imb. | $ RT LA AS Imb. | $ Total Imb. | $ Energy Imb. | $ RT LA AS Imb. | $ Total Imb.
2 | 0 | 0 | 0 | (825,000) | 546,333 | (278,667) | (862,500) | 0 | 0 | (862,500) | 1,687,500 | (546,333) | 1,141,167
2 | 0 | 0 | 0 | (175,729) | 174,562 | (1,167) | (577,396) | 0 | 0 | (577,396) | 753,125 | (174,562) | 578,562

## Slide 11: Settlement in the EEA Operation cont.
Under today’s design, when a Load Resource providing UFR-type AS is deployed:
  That Resource is no longer consuming and is not available for another deployment, so there is an AS Imbalance charge with the price based on the ORDC price adder.
  With the Load Resource no longer consuming, it also avoids the cost of buying energy.
    If there was an energy purchase for what the Load Resource had been consuming (e.g., in the DAM), an Energy Imbalance would also be created and there would be a payment to the Load Resource’s QSE.
  The money collected from the AS Imbalance charges go to QSEs that are long on their AS Imbalance. Under scarcity conditions when AS is being used, this generally results in an AS Imbalance payment to Load.

## Slide 12: Settlement in the EEA Operation cont.
Under the last comments, RTC would work very similarly.
  That Resource is no longer consuming and available for another deployment, RTC will take a fresh at awarding that AS to other Resources and there is an AS Imbalance charge with the price based on the real-time MCPC for that AS.
  With the Load Resource no longer consuming, it also avoids the cost of buying energy.
    If there was an energy purchase for what the Load Resource had been consuming (e.g., in the DAM), an Energy Imbalance would also be created and there would be a payment to the Load Resource’s QSE.
  The money collected from the AS Imbalance charges go to QSEs that are long on their AS Imbalance. Under scarcity conditions when AS is being used, this generally results in an AS Imbalance payment to Load.
Assuming that the deployed Load Resource should continue to be awarded means that, in addition to avoiding the energy cost, there is not an AS Imbalance charge for the Load Resources and there would be less dollars allocated to Load, relative to today.

## Slide 13: Examples of how this process would work under RTC with various types of Resources and AS products Based on the ERCOT August 20, 2019 comments

## Slide 14: Example – Generation Resource Providing PFR-type RRS
Time
RTC 0
RTC 5
RTC 10
RTC 15
HSL
DAM
RRS Award
Output
Base Point
Case A
Generation Resource responds to frequency and is able to back down to the RTC 0 Base Point when RTC 5 and 10 are executed
No AS Imbalance
Area under the green line is paid for energy
Time
RTC 0
RTC 5
RTC 10
RTC 15
HSL
DAM
RRS Award
Case B
Generation Resource responds to frequency and is not able to back down to the RTC 0 Base Point when RTC 5 is executed
Some AS Imbalance for RTC 5 only. RTC looks for RRS elsewhere for RTC 5
Area under the green line is paid for energy
RTC RRS Award
Output
Base Point
RTC RRS Award
Similar examples would also apply for Reg-Up

## Slide 15: Example – Generation Resource Providing PFR-type RRS cont.
Time
RTC 0
RTC 5
RTC 10
RTC 15
HSL
DAM
RRS Award
Output
Base Point
Case C
Generation Resource trips between RTC 0 and RTC 5 and is not available to provide RRS in RTC 5 or 10
AS Imbalance for all RRS for RTC 5 and 10 and no AS Imbalance for RTC 0. RTC looks for RRS elsewhere for RTC 5 and 10
Area under the green line is paid for energy
RTC RRS Award
Similar examples would also apply to Reg-Up

## Slide 16: Example – Load Resource Providing UFR-type RRS
Time
RTC 0
RTC 5
RTC 10
RTC 15
HSL
DAM
RRS Award
NPF
Case D
Load Resource trips due to a frequency event between RTC 0 and RTC 5 and is not able to provide RRS again for RTC 5 or 10
AS Imbalance for all RRS for RTC 5 and 10 and no AS Imbalance for RTC 0. RTC looks for RRS elsewhere for RTC 5 and 10
Area under the green line is charged for energy
Time
RTC 0
RTC 5
RTC 10
RTC 15
HSL
DAM
RRS Award
Case E
Load Resource is manually deployed by ERCOT between RTC 0 and RTC 5 and is not able to provide RRS again for RTC 10
AS Imbalance for all RRS for RTC 10 and no AS Imbalance for RTC 0 and 5. RTC looks for RRS elsewhere for RTC 10
Area under the green line is charged for energy
RTC RRS Award
NPF
RTC RRS Award

## Slide 17: Example – Load Resource Providing UFR-type RRS cont.
Time
RTC 0
RTC 5
RTC 10
RTC 15
HSL
DAM
RRS Award
Case F
Load Resource trips because of Resource issue between RTC 0 and RTC 5 and is not available to provide RRS in RTC 5, but hypothetically resumes consumption by RTC 10
AS Imbalance for all RRS for RTC 5 and no AS Imbalance for RTC 0 and 10. RTC looks for RRS elsewhere for RTC 5
Area under the green line is charged for energy
NPF
RTC RRS Award
Self-provisioned RRS could also have been moved to another Load Resource within the QSE

## Slide 18: Example – Generation Resource Providing Off-line Non-Spin
Time
RTC 0
RTC 5
RTC 10
RTC 15
HSL
DAM
Non-Spin Award
Output
Base Point
Case G
Generation Resource gets deployed for off-line Non-Spin by ERCOT between RTC 0 and RTC 5
AS Imbalance for some Non-Spin for RTC 5 and 10 and no AS Imbalance for RTC 0. RTC looks for Non-Spin elsewhere for RTC 5 and 10
Area under the green line is paid for energy
RTC Non-Spin Award
Time
RTC 0
RTC 5
RTC 10
RTC 15
HSL
DAM
Non-Spin Award
Output
Base Point
Case H
Generation Resource gets deployed for off-line Non-Spin by ERCOT between RTC 0 and RTC 5 and trips during start up
AS Imbalance for Non-Spin for RTC 5 and 10 and no AS Imbalance for RTC 0. RTC looks for Non-Spin elsewhere for RTC 5 and 10
Area under the green line is paid for energy
RTC Non-Spin Award

## Slide 19: Example – Generation Resource Providing Off-line ECRS
Time
RTC 0
RTC 5
RTC 10
RTC 15
HSL
DAM ECRS Award
Output
Base Point
Case I
Generation Resource gets deployed for off-line ECRS between RTC 0 and RTC 5
AS Imbalance for ECRS for RTC 5 and 10 and no AS Imbalance for RTC 0. RTC looks for ECRS elsewhere for RTC 5 and 10
Area under the green line is paid for energy
RTC ECRS Award

## Slide 20: Example – On-line Generation Resource Providing ECRS
Time
RTC 0
RTC 5
RTC 10
RTC 15
HSL
DAM
ECRS Award
Output
Base Point
Case J
ECRS awards for the Generation Resource change because of economics
AS Imbalance for ECRS for RTC 5 and 10 and no AS Imbalance for RTC 0. RTC looks for ECRS elsewhere for RTC 5 and 10
Area under the green line is paid for energy
RTC ECRS Award
Similar examples would also apply to on-line Non-Spin

## Slide 21: Questions