## Slide 1
Item 3a –Key Principle 1.1
Updated Ramp Constraint Illustration
RTCTF
September 19, 2019

## Slide 2: Acronyms
Ancillary Service (AS)
Ancillary Service Demand Curves (ASDC)
ERCOT Contingency Reserve Service (ECRS)
Generation-to-be-Dispatched (GTBD)
High Ancillary Service Limit (HASL)
High Dispatch Limit (HDL)
High Sustained Limit (HSL)
Operating Reserve Demand Curve (ORDC)
Non-Spinning Reserve Service (Non-Spin)
Power Balance Penalty Curve (PBPC)
Real-Time Co-optimization (RTC)
Real-Time Co-optimization Task Force (RTCTF)
Regulation Up Service (Reg-Up)
Responsive Reserve Service (RRS)
Security-Constrained Economic Dispatch (SCED)
Security-Constrained Economic Dispatch Up Ramp Rate (SURAMP)

## Slide 3: Introduction
During the August 27, 2019 RTCTF discussion on Real-Time ASDCs, there was a desire to look at the same illustrative examples under a system-wide scarcity condition.
  This was is addition to the ramp-constrained system condition that was presented.
The group also wanted to discuss the pros and cons of the two approach
  The approach of basing a portion of the Reg-Up and RRS ASDCs on the current PBPC.
  The approach of stacking all Reg-Up ahead of RRS, all RRS ahead of ECRS, and all ECRS ahead of Non-Spin

## Slide 4: Example Setup
This presentation again uses a simplified example to illustrate how a system would behave under:
  RTC where the ASDC for Reg-Up is placed within an aggregate ORDC based on a PBPC; and
  RTC where the ASDC for Reg-Up is placed at the highest price points of the aggregate ORDC without consideration of the PBPC.
The system:
  Resources - One generator (Resource A) that has an HSL of 100 MW and a ramp rate of 1 MW/min
  AS - There are two AS products: Reg-Up and ECRS, both with an AS plan of 3 MW
Chart: PBPC
| 0 | 1.5 | 1.5 | 3
 | 2000 | 2000 | 9000 | 9000

## Slide 5: RTC Examples
Chart: Aggregate ORDC
| 0 | 2.5 | 2.5 | 4 | 4 | 6
ORDC | 9000 | 9000 | 2000 | 2000 | 1000 | 1000
Chart: ASDCs - Example A
| 0 | 1.5 | 1.5 | 3
Reg-Up | 9000 | 9000 | 2000 | 2000
ECRS | 9000 | 9000 | 1000 | 1000
Chart: ASDCs - Example B
| 0 | 2.5 | 2.5 | 3
Reg-Up | 9000 | 9000 | 2000 | 2000
ECRS | 2000 | 2000 | 1000 | 1000
Reg-Up is set exactly equal to the inverse of the PBPC
All Reg-Up is placed at price points on the aggregate ORDC ahead of ECRS

## Slide 6: RTC – Example A
Key points:
  In interval 2, start seeing scarcity pricing driven by ASDCs
    Initially only “short” on ECRS
  For interval 3, we now see shortages in both Reg-Up and ECRS, but neither are fully exhausted
  For interval 3, the ASDCs set the AS prices at $9,000/MWh
    Note: ERCOT’s KP 1.1 proposal does not price any ECRS or Non-Spin at $9,000/MWh
Real-Time Interval | GTBD/ Demand | Resource A |  |  |  | 
 |  | Reg-Up Award | ECRS Award | HSL/ HASL | HDL (Physical Ramp) | Base Point
1 | 94 | 3 | 3 | 100/na | 96.5 | 94
2 | 96 | 3 | 1 | 100/na | 99 | 96
3 | 98 | 1.2 | 0.8 | 100/na | 100 | 98
4 | 96 | 3 | 1 | 100/na | 100 | 96
Chart: ASDCs - Example A
| 0 | 1.5 | 1.5 | 3
Reg-Up | 9000 | 9000 | 2000 | 2000
ECRS | 9000 | 9000 | 1000 | 1000
Ramp constraint:
HDL = Output + (1MW/min * 5min) = Output + 5MW
Base Point + (50% * Reg-Up Award) <= HDL

## Slide 7: RTC – Example B
Key points:
  In interval 2, start seeing scarcity pricing driven by ASDCs
    Initially only “short” on ECRS
  For interval 3, we now see shortages in both Reg-Up and ECRS, but more Reg-Up awarded compared to example A since ECRS is now fully exhausted
  For interval 3, the Reg-Up price is at $9,000/MWh and the ECRS price is at $2,000/MWh
Real-Time Interval | GTBD/ Demand | Resource A |  |  |  | 
 |  | Reg-Up Award | ECRS Award | HSL/ HASL | HDL (Physical Ramp) | Base Point
1 | 94 | 3 | 3 | 100/na | 96.5 | 94
2 | 96 | 3 | 1 | 100/na | 99 | 96
3 | 98 | 2 | 0 | 100/na | 100 | 98
4 | 96 | 3 | 1 | 100/na | 100 | 96
Ramp constraint:
HDL = Output + (1MW/min * 5min) = Output + 5MW
Base Point + (50% * Reg-Up Award) <= HDL
Chart: ASDCs - Example B
| 0 | 2.5 | 2.5 | 3
Reg-Up | 9000 | 9000 | 2000 | 2000
ECRS | 2000 | 2000 | 1000 | 1000

## Slide 8: High-Level Pros/Cons of the Approaches
RTC where the ASDC for Reg-Up is placed within an aggregate ORDC based on a PBPC
  In a ramp-constrained system condition, you will avoid system-wide capacity scarcity pricing for minor ramp scarcity conditions.
  However, in a system-wide capacity scarcity condition, Reg-Up would only be given partial priority over the other AS products.
RTC where the ASDC for Reg-Up is placed at the highest price points of the aggregate ORDC without consideration of the PBPC
  In a ramp-constrained system condition, you may see system-wide capacity scarcity pricing for even minor ramp scarcity conditions.
  However, in a system-wide capacity scarcity condition, Reg-Up would be given complete priority over the other AS products.

## Slide 9: Appendix
Material presented at the August 27, 2019 RTCTF Meeting

## Slide 10: Introduction
During the 8/9/19 RTCTF discussion on Real-Time ASDCs, there was a need for an example looking at pricing outcomes during a ramp-constrained system condition.
Questions that were posed:
  What are the theoretical effects of basing the Reg-Up ASDC on the PBPC as opposed to having all Reg-Up placed at the highest price points of the aggregate ORDC?
  If the ASDC prices points are higher for one AS product than another AS product, it is guaranteed that the latter AS product is fully exhausted before being short on the first AS product?

## Slide 11: Example Setup
This presentation uses a simplified example to illustrate how a ramp-constrained system would behave under:
  Today’s market design;
  RTC where the ASDC for Reg-Up is placed within an aggregate ORDC based on a PBPC; and
  RTC where the ASDC for Reg-Up is placed at the highest price points of the aggregate ORDC without consideration of the PBPC.

## Slide 12: Example Setup
A ramp-constrained system condition is referring to a case where there is sufficient supply capacity on the system relative to demand, but there is not sufficient ramp capability that is available for the horizon of the 5-minute dispatch interval.
The system:
  Resources - One generator (Resource A) that has an HSL of 100 MW and a ramp rate of 1 MW/min
  AS - There are two AS products: Reg-Up and ECRS, both with an AS plan of 3 MW
  Assume 50% ramp sharing between energy and Reg-Up

## Slide 13: Today’s Market
Key points:
  AS responsibilities can’t be moved.
  For interval 3, the ramp limitations result in going 0.5 MW into the PBPC.
    Accordingly, price goes to $2,000/MWh based on the PBPC.
  Theoretically, Reg-Up is deployed to account for the missing energy.
Chart: PBPC
| 0 | 1.5 | 1.5 | 3
 | 2000 | 2000 | 9000 | 9000
Real-Time Interval | GTBD/ Demand | Resource A |  |  |  | 
 |  | Reg-Up Responsibility | ECRS Responsibility | HSL/ HASL | HDL (SURAMP -Based) | Base Point
1 | 70 | 3 | 3 | 100/94 | 71 | 70
2 | 73 | 3 | 3 | 100/94 | 73.5 | 73
3 | 77 | 3 | 3 | 100/94 | 76.5 | 76.5
4 | 79 | 3 | 3 | 100/94 | 80 | 79
Ramp constraint:
SURAMP = 1MW/min – ((3/5)*50%) = 0.7MW/min
HDL = Output + (0.7MW/min * 5min) = Output + 3.5MW

## Slide 14: RTC Examples
Chart: Aggregate ORDC
| 0 | 2.5 | 2.5 | 4 | 4 | 6
ORDC | 9000 | 9000 | 2000 | 2000 | 1000 | 1000
Chart: ASDCs - Example A
| 0 | 1.5 | 1.5 | 3
Reg-Up | 9000 | 9000 | 2000 | 2000
ECRS | 9000 | 9000 | 1000 | 1000
Chart: ASDCs - Example B
| 0 | 2.5 | 2.5 | 3
Reg-Up | 9000 | 9000 | 2000 | 2000
ECRS | 2000 | 2000 | 1000 | 1000
Reg-Up is set exactly equal to the inverse of the PBPC
All Reg-Up is placed at price points on the aggregate ORDC ahead of ECRS

## Slide 15: RTC – Example A
Key points:
  AS awards can now change.
  For the entire window there is sufficient 10-minute ramp and capacity for energy and all AS, so no ECRS shortages regardless of the ASDC
  For interval 3, the ramp limitations result in being 1 MW short on Reg-Up.
    Accordingly, price goes to $2,000/MWh based on the ASDC.
Real-Time Interval | GTBD/ Demand | Resource A |  |  |  | 
 |  | Reg-Up Award | ECRS Award | HSL/ HASL | HDL (Physical Ramp) | Base Point
1 | 70 | 3 | 3 | 100/na | 72.5 | 70
2 | 73 | 3 | 3 | 100/na | 75 | 73
3 | 77 | 2 | 3 | 100/na | 78 | 77
4 | 79 | 3 | 3 | 100/na | 81.5 | 79
Chart: ASDCs - Example A
| 0 | 1.5 | 1.5 | 3
Reg-Up | 9000 | 9000 | 2000 | 2000
ECRS | 9000 | 9000 | 1000 | 1000
Ramp constraint:
HDL = Output + (1MW/min * 5min) = Output + 5MW
Base Point + (50% * Reg-Up Award) <= HDL

## Slide 16: RTC – Example B
Key points:
  AS awards and base points are the same as in example A.
  With the same shortage for interval 3, the Reg-Up ASDC sets the price at $9,000/MWh.
  This value is higher than any point on the ECRS ASDC, but there is not an ECRS shortage
Ramp constraint:
HDL = Output + (1MW/min * 5min) = Output + 5MW
Base Point + (50% * Reg-Up Award) <= HDL
Chart: ASDCs - Example B
| 0 | 2.5 | 2.5 | 3
Reg-Up | 9000 | 9000 | 2000 | 2000
ECRS | 2000 | 2000 | 1000 | 1000
Real-Time Interval | GTBD/ Demand | Resource A |  |  |  | 
 |  | Reg-Up Award | ECRS Award | HSL/ HASL | HDL (Physical Ramp) | Base Point
1 | 70 | 3 | 3 | 100/na | 72.5 | 70
2 | 73 | 3 | 3 | 100/na | 75 | 73
3 | 77 | 2 | 3 | 100/na | 78 | 77
4 | 79 | 3 | 3 | 100/na | 81.5 | 79

## Slide 17: Conclusions
Questions:
  What are the theoretical effects of basing the Reg-Up ASDC on the PBPC as opposed to having all Reg-Up placed at the highest price points of the aggregate ORDC?
  With a Reg-Up ASDC where Reg-Up is placed at the highest price points of the aggregate ORDC:
    In a ramp-constrained system condition, you may see system-wide capacity scarcity pricing for even a minor ramp scarcity condition.
    However, in a system-wide capacity scarcity condition, Reg-Up would be given priority over the AS products.
  If the ASDC prices points are higher for one AS product than another AS product, it is guaranteed that the latter AS product is fully exhausted before being short on the first AS product?
  No, this is not guaranteed. One reason for this is the fact that the individual AS products all have different definitions, like time for the Resource to respond (e.g., 5 min vs. 10 min).

## Slide 18: Questions