## Slide 1
Item 3a –Key Principle 1.1
Rationale for ASDCs stacked in Order of Reliability Value
Shams Siddiqi, PhD
Crescent Power, Inc.
RTCTF
September 19, 2019

## Slide 2: Introduction
During the August 27, 2019 RTCTF discussion on Real-Time ASDCs, there was a desire to look at the same illustrative examples under a system-wide scarcity condition.
  This was is addition to the ramp-constrained system condition that was presented.
The group also wanted to discuss the pros and cons of the two approach
  The approach of basing a portion of the Reg-Up and RRS ASDCs on the current PBPC.
  The approach of stacking all Reg-Up ahead of RRS, all RRS ahead of ECRS, and all ECRS ahead of Non-Spin

## Slide 3: Example Setup
This presentation again uses a simplified example to illustrate how a system would behave under:
  RTC where the ASDC for Reg-Up is placed within an aggregate ORDC based on a PBPC; and
  RTC where the ASDC for Reg-Up is placed at the highest price points of the aggregate ORDC without consideration of the PBPC.
The system:
  Resources - One generator (Resource A) that has an HSL of 100 MW and a ramp rate of 1 MW/min with Energy Offer of $20/MWh
  AS - There are two AS products: Reg-Up and ECRS, both with an AS plan of 3 MW with Reg-Up offer at $10/MW/hr and ECRS offer at 0.
Chart: PBPC
| 0 | 1.5 | 1.5 | 3
 | 2000 | 2000 | 9000 | 9000

## Slide 4: RTC Examples
Chart: Aggregate ORDC
| 0 | 2.5 | 2.5 | 4 | 4 | 6
ORDC | 9000 | 9000 | 2000 | 2000 | 1000 | 1000
Chart: ASDCs - Example A
| 0 | 1.5 | 1.5 | 3
Reg-Up | 9000 | 9000 | 2000 | 2000
ECRS | 9000 | 9000 | 1000 | 1000
Chart: ASDCs - Example B
| 0 | 2.5 | 2.5 | 3
Reg-Up | 9000 | 9000 | 2000 | 2000
ECRS | 2000 | 2000 | 1000 | 1000
Reg-Up is set exactly equal to the inverse of the PBPC
All Reg-Up is placed at price points on the aggregate ORDC ahead of ECRS

## Slide 5: RTC – Example A
Key points:
  ECRS is only exchanged for energy in SCED – not deployed by LFC
  Reg-Up is deployed by LFC and thus provides valuable reliability between SCED cycles
  Yet in intervals 2,3,4 ECRS awards are given priority over Reg-Up awards – reducing system reliability
  Note: red highlighted prices would be capped at $9,000 under my proposal
Real-Time Interval | GTBD=Base Point | Resource A |  |  |  | 
 |  | Reg-Up Award | ECRS Award | SPP ($/MWh) | Reg-Up MCPC ($/MW/hr) | ECRS MCPC ($/MW/hr)
1 | 94.1 | 3 | 2.9 | $1,520 | $1,510 | $1,500
2 | 96.1 | 2.9 | 1.0 | $2,010 | $2,000 | $1,990
3 | 98.1 | 0.9 | 1.0 | $9,010 | $9,000 | $8,990
4 | 99.1 | 0 | 0.9 | $9,020 | $9,010 | $9,000
Chart: ASDCs - Example A
| 0 | 1.5 | 1.5 | 3
Reg-Up | 9000 | 9000 | 2000 | 2000
ECRS | 9000 | 9000 | 1000 | 1000
Ramp constraint:
HDL = Output + (1MW/min * 5min) = Output + 5MW
Base Point + (50% * Reg-Up Award) <= HDL

## Slide 6: RTC – Example B
Key points:
  ECRS is only exchanged for energy in SCED – not deployed by LFC
  Reg-Up is deployed by LFC and thus provides valuable reliability between SCED cycles
  In all intervals Reg-Up awards are given priority over ECRS awards – increased system reliability
  ECRS prices are appropriately lower for those buying back DAM awards
  Note: red highlighted prices would be capped at $9,000 under my proposal
Real-Time Interval | GTBD=Base Point | Resource A |  |  |  | 
 |  | Reg-Up Award | ECRS Award | SPP ($/MWh) | Reg-Up MCPC ($/MW/hr) | ECRS MCPC ($/MW/hr)
1 | 94.1 | 3.0 | 2.9 | $1,520 | $1,510 | $1,500
2 | 96.1 | 3.0 | 0.9 | $2,020 | $2,010 | $2,000
3 | 98.1 | 1.9 | 0 | $9,010 | $9,000 | $2,000
4 | 99.1 | 0.9 | 0 | $9,010 | $9,000 | $2,000
Ramp constraint:
HDL = Output + (1MW/min * 5min) = Output + 5MW
Base Point + (50% * Reg-Up Award) <= HDL
Chart: ASDCs - Example B
| 0 | 2.5 | 2.5 | 3
Reg-Up | 9000 | 9000 | 2000 | 2000
ECRS | 2000 | 2000 | 1000 | 1000

## Slide 7: High-Level Pros/Cons of the Approaches
RTC where the ASDC for Reg-Up is placed within an aggregate ORDC based on a PBPC
  Since the entire capacity providing RRS and ECRS (over 3,000MW) under RTC will be available to SCED for energy ramping needs (unlike today where that capacity is not available to SCED and held behind HASL), there is very little to no chance of the system experiencing ramp scarcity conditions.
  Lower value AS may have higher MCPC than higher value AS
  In a system-wide capacity scarcity condition, Reg-Up would only be given partial priority over the other AS products thereby reducing reliability
RTC where the ASDC for Reg-Up is placed at the highest price points of the aggregate ORDC without consideration of the PBPC
  In a system-wide capacity scarcity condition, Reg-Up would be given complete priority over the other AS products
  Reflects the definition of demand curves – i.e. curves should reflect the reliability value of the service (and Reg-Up is definitely more valuable than Non-Spin and ECRS) – results in rational award and pricing outcomes

## Slide 8: Ramp-Constrained System Conditions

## Slide 9: Example Setup
A ramp-constrained system condition is referring to a case where there is sufficient supply capacity on the system relative to demand, but there is not sufficient ramp capability that is available for the horizon of the 5-minute dispatch interval.
The system (ERCOT’s example of One generator is unrealistic and highly tailored to make their case when there’s about 3,000MW of RRS/ECRS and only 200MW of Reg-Up):
  Resources - Two generator (Resource A and B) that each has an HSL of 50 MW and a ramp rate of 1 MW/min and energy offers of $10/MWh and $20/MWh
  AS - There are two AS products: Reg-Up and ECRS, both with an AS plan of 3 MW: RA: $10/MW Reg-Up offer, $0/MW ECRS offer; RB: $15/MW Reg-Up offer, $12/MW ECRS offer
  Assume 50% ramp sharing between energy and Reg-Up

## Slide 10: Today’s Market
Key points:
  AS responsibilities can’t be moved.
  For interval 3, the ramp limitations result in going 0.5 MW into the PBPC.
    Accordingly, price goes to $2,000/MWh based on the PBPC.
  Theoretically, Reg-Up is deployed to account for the missing energy.
Chart: PBPC
| 0 | 1.5 | 1.5 | 3
 | 2000 | 2000 | 9000 | 9000
Ramp constraint:
SURAMP = 1MW/min – ((3/5)*50%) = 0.7MW/min
HDL = Output + (0.7MW/min * 5min) = Output + 3.5MW

## Slide 11: RTC Examples
Chart: Aggregate ORDC
| 0 | 2.5 | 2.5 | 4 | 4 | 6
ORDC | 9000 | 9000 | 2000 | 2000 | 1000 | 1000
Chart: ASDCs - Example A
| 0 | 1.5 | 1.5 | 3
Reg-Up | 9000 | 9000 | 2000 | 2000
ECRS | 9000 | 9000 | 1000 | 1000
Chart: ASDCs - Example B
| 0 | 2.5 | 2.5 | 3
Reg-Up | 9000 | 9000 | 2000 | 2000
ECRS | 2000 | 2000 | 1000 | 1000
Reg-Up is set exactly equal to the inverse of the PBPC
All Reg-Up is placed at price points on the aggregate ORDC ahead of ECRS

## Slide 12: RTC – Example A
Key points:
  AS awards can now change.
  For the entire window there is sufficient 10-minute ramp and capacity for energy and all AS, so no ECRS shortages regardless of the ASDC
  For interval 3, the ramp limitations result in being 1 MW of Reg-Up being moved to Resource B
  Ramp only an issue when capacity scarcity
Ramp constraint:
HDL = Output + (1MW/min * 5min) = Output + 5MW
Base Point + (50% * Reg-Up Award) <= HDL
Chart: ASDCs - Example A
| 0 | 1.5 | 1.5 | 3
Reg-Up | 9000 | 9000 | 2000 | 2000
ECRS | 9000 | 9000 | 1000 | 1000

## Slide 13: RTC – Example A (Capacity Scarcity)
Key points:
  Change Resource A HSL to 30MW.
  Now Reg-Up is not awarded while less valuable ECRS is awarded.
  Less reliable operation.
  Can result in Reg-Up prices being lower than ECRS prices.
Ramp constraint:
HDL = Output + (1MW/min * 5min) = Output + 5MW
Base Point + (50% * Reg-Up Award) <= HDL
Chart: ASDCs - Example A
| 0 | 1.5 | 1.5 | 3
Reg-Up | 9000 | 9000 | 2000 | 2000
ECRS | 9000 | 9000 | 1000 | 1000

## Slide 14: RTC – Example B
Key points:
  AS awards and base points are the same as in example A.
  Pricing outcomes will also be identical.
Ramp constraint:
HDL = Output + (1MW/min * 5min) = Output + 5MW
Base Point + (50% * Reg-Up Award) <= HDL
Chart: ASDCs - Example B
| 0 | 2.5 | 2.5 | 3
Reg-Up | 9000 | 9000 | 2000 | 2000
ECRS | 2000 | 2000 | 1000 | 1000

## Slide 15: RTC – Example B (Capacity Scarcity)
Key points:
  Change Resource A HSL to 30MW.
  Now Reg-Up is awarded while less valuable ECRS is not awarded.
  More reliable operation.
  Reg-Up prices always higher than ECRS prices.
Ramp constraint:
HDL = Output + (1MW/min * 5min) = Output + 5MW
Base Point + (50% * Reg-Up Award) <= HDL
Chart: ASDCs - Example B
| 0 | 2.5 | 2.5 | 3
Reg-Up | 9000 | 9000 | 2000 | 2000
ECRS | 2000 | 2000 | 1000 | 1000

## Slide 16: Conclusions
Ramp-constrained operation is addressed by RTC by moving and ultimately awarding less of lower value AS - capacity providing RRS and ECRS (over 3,000MW) under RTC will be available to SCED for energy ramping needs (unlike today), there is very little to no chance of the system experiencing ramp scarcity conditions.
RTC where the ASDC for Reg-Up is placed within an aggregate ORDC based on a PBPC
  Lower value AS may be priced higher than higher value AS
  In a system-wide capacity scarcity condition, Reg-Up would only be given partial priority over the other AS products thereby reducing reliability
RTC where the ASDC for Reg-Up is placed at the highest price points of the aggregate ORDC without consideration of the PBPC
  In a system-wide capacity scarcity condition, Reg-Up would be given complete priority over the other AS products and so higher prices
  Reflects the definition of demand curves – i.e. curves should reflect the reliability value of the service (and Reg-Up is definitely more valuable than Non-Spin and ECRS) – results in rational award and pricing outcomes