## Slide 1
Storage:
SCED Dispatch of Controllable Load Resources (CLRs)
ERCOT Staff
WMWG
September 16, 2019

## Slide 2: Background
In order to participate in SCED and/or Ancillary Services today, storage devices must register as both a Generation Resource (GR) and a Controllable Load Resource (CLR)
  This system will be in place for the foreseeable future
CLR participation in SCED was enabled by NPRR 555, approved by the ERCOT Board Sept. 2013
NPRR 555 allows CLRs to participate in SCED by submitting Bids to buy ‘up to’ their specified price

## Slide 3: Background
Initial candidates for Loads in SCED were residential aggregations with air conditioners under direct load control
  Other Binding Document: ‘Requirements for Aggregate Load Resource (ALR) Participation’
The NPRR and OBD contemplated that SCED participation would come from ALRs scattered across a Load Zone
Batteries are well-suited to SCED dispatch on both the GR and CLR sides

## Slide 4: How SCED dispatches CLRs
Nodal Protocols 6.5.7.3 (1):
  ‘The SCED process is designed to simultaneously manage energy, the system power balance and network congestion through Resource Base Points and calculation of LMPs every five minutes. The SCED process uses a two-step methodology that applies mitigation prospectively to resolve Non-Competitive Constraints for the current Operating Hour. The SCED process evaluates Energy Offer Curves, Output Schedules and Real-Time Market (RTM) Energy Bids to determine Resource Dispatch Instructions by maximizing bid-based revenues minus offer-based costs, subject to power balance and network constraints. The SCED process uses the Resource Status provided by SCADA telemetry under Section 6.5.5.2, Operational Data Requirements, and validated by the Real-Time Sequence, instead of the Resource Status provided by the COP. An RTM Energy Bid represents the bid for energy distributed across all nodes in the Load Zone in which the Controllable Load Resource is located.’
Result: The ERCOT system is designed to dispatch all CLRs – including CLR-Storage – based on the Load Zone shift factor
  This is appropriate for an ALR but not for a single-site CLR-Storage receiving Wholesale Storage Load (WSL) treatment
  (NOTE: To date, no CLRs-Storage have participated in SCED)

## Slide 5: Change needed for storage CLRs in SCED
CLR-Storage receiving WSL treatment today is currently settled using nodal pricing -- but the system implementation would incorrectly dispatch CLR-Storage based on the Load Zone shift factor if a Bid to Buy is submitted
An RTM Energy Bid from a single-site CLR-Storage receiving WSL treatment should be specific to the single-site CLR-Storage, and the CLR should be dispatched and settled based on the nodal price at that location
Correcting this will require system changes

## Slide 6: Additional Protocol change for clarification
Nodal Protocols 3.6.1 (5):
  ‘The Settlement Point for a Controllable Load Resource with a Real-Time Market (RTM) Energy Bid is its Load Zone Settlement Point.’
This provision should not apply to a CLR-Storage receiving Wholesale Storage Load treatment, which is settled at the nodal price at its location. This language should be revised to acknowledge the exception.

## Slide 7: Looking ahead
Today’s presentation is just a heads-up
ERCOT will address this issue and others in forthcoming NPRRs

## Slide 8
Questions?