## Slide 1: SPP Operating Reserve Market Overview
Gary Cate
Manager, Market Design

## Slide 2: Section header slide optional
Use this if you need to divide your presentation into sections

## Slide 3: OPERATING REGION
Service territory: 546,000 square miles
Population served: 17.5 million
Generating plants: 818*
Substations: 5,054*
* In SPP’s reliability coordination footprint

## Slide 4: 2018 Energy Production by Fuel Type: 275,887 GWh total
Chart: 
| Coal (42.4%) | Wind (23.5%) | Gas (23.4%) | Nuclear (5.4%) | Hydro (4.8%) | Fuel Oil (0.2%) | Solar (0.2%) | Other (0.1%)
Energy Consumption | 42.4 | 23.5 | 23.4 | 5.4 | 4.8 | 0.2 | 0.2 | 0.1
Chart: 
| Natural Gas (23.4%) | Coal (42.4%) | Wind (23.5%) | Nuclear (5.4%) | Fuel Oil (0.2%) | Hydro (4.8%) | Solar (0.2%) | Other (0.1%)
Energy Consumption | 0.234 | 0.424 | 0.235 | 0.054 | 0.002 | 0.048 | 0.002 | 0.001
Notes: The energy consumption number represents the summed hourly average of the amount of energy used by retail customers in the market footprint.

## Slide 5: MIN AND MAX PERCENT OF GENERATION MIX BY FUEL TYPE
Chart: 
| Coal | Wind | Gas | Nuclear | Hydro
High | 0.688 | 0.627 | 0.507 | 0.099 | 0.093
Low | 0.141 | 0.004 | 0.062 | 0.026 | 0.012
Average | 0.399 | 0.246 | 0.24 | 0.062 | 0.05
June 2018 – June 2019
Max
Min

## Slide 6: Market Facts
225 market participants
757 generating resources
2018 marketplace settlements = $20.5 billion
50,662 MW coincident peak load (8/19/19)
  Winter peak: 43,584 MW (1/17/18)
16,972 MW Wind Peak (9/11/2019)
67.3% Wind Penetration Peak (4/27/2019)

## Slide 7: SPP Integrated Marketplace overview
“Day-2” Market Implemented March 1, 2014
Replaced Energy Imbalance Service (EIS) Market launched in 2007
SPP consolidated all EIS member Balancing Authorities (BA) into one SPP BA
• Day-Ahead Market, Reliability Unit Commitment, Real-Time Balancing, and Transmission Congestion Rights (CRR’s in ERCOT)
Products: Energy, Regulation UP, Regulation DN, Spinning, Supplemental

## Slide 8: SPP Integrated Marketplace Overview (Key Differences from ERCOT)
Day Ahead Must Offer
  Must offer enough generation to cover Load and Operating Reserve (Regulation, Spinning and Supplemental) obligations
High Participation in Day Ahead Market
  Average of 99% of Real Time Load bid into Day Ahead
Day Ahead Market Commitments are binding
  Over 95% of all commitments come from Day Ahead
  Non-instructed deviation from Day Ahead Commitment Plan allocated portions of Make Whole Payment
Less aggressive shortage pricing

## Slide 9: SPP Operating Reserve Products
Regulation UP
Procured in both DA and RT
Resources cleared in DA may be different than resources in Real Time
Regulation Selection process occurs 30 minutes prior to top of hour
No virtual offers. Physical supply offers only.
Chart: REGUP Requirements 2018
| January | February | March | April | May | June | July | August | September | October | November | December
REGUP | 357.3777 | 342.0238 | 316.2567 | 310.9528 | 347.1667 | 389.8458 | 368.8669 | 367.5753 | 330.7569 | 304.9839 | 313.7792 | 329.4315

## Slide 10: SPP Operating Reserve Products
Regulation DN
Procured in both DA and RT
Resources cleared in DA may be different than resources in Real Time
Regulation Selection process occurs 30 minutes prior to top of hour
No virtual offers. Physical supply offers only.
Chart: REGDN Requirements 2018
| January | February | March | April | May | June | July | August | September | October | November | December
REGDN | 357.2245 | 343.2946 | 316.4946 | 312.2833 | 345.8454 | 391.4708 | 369.1169 | 369.0887 | 330.9833 | 305.5806 | 314.2861 | 330.1962

## Slide 11: SPP Operating Reserve Products
Spinning Reserve
Procured in both DA and RT
Resources cleared in DA may be different than resources in Real Time
Covers trip of largest unit plus ½ of second largest unit
SPP typically employs a 50/50 split between Spinning and Supplemental
No virtual offers. Physical supply offers only.
Chart: Spinning Requirements 2018
| January | February | March | April | May | June | July | August | September | October | November | December
SPIN | 795.8105 | 753.625 | 743.1499 | 592.4944 | 675.1526 | 730.4097 | 733.5766 | 735 | 741 | 748.4348 | 741.7417 | 748.5081

## Slide 12: SPP Operating Reserve Products
Supplemental Reserve
Procured in both DA and RT
Resources cleared in DA may be different than resources in Real Time
Covers trip of largest unit plus ½ of second largest unit
SPP typically employs a 50/50 split between Spinning and Supplemental
Can be offline or online
No virtual offers. Physical supply offers only.
Chart: Supplemental Requirements 2018
| January | February | March | April | May | June | July | August | September | October | November | December
SUPP | 717.6169 | 753.625 | 743.1499 | 592.4944 | 675.1526 | 730.4097 | 733.5766 | 735 | 741 | 748.4348 | 741.7417 | 748.5081

## Slide 13: SPP Product Offer Caps (FERC Mandated)
Regulation- $500
Contingency Reserves- $100
Energy- $1000 (absent FERC Order 831)
  Regulation
    $600
    Contingency Reserve Cap + Regulation Offer Cap ($100+$500)
  Operating Reserves
    $1100
    Energy Offer Cap + Contingency Reserve Offer Cap ($1000+$100)
SPP Scarcity Price Caps
(FERC Approved, not Mandated)
SPP Operating reserve and product offer caps

## Slide 14: Regulating Reserve Demand Curves
  Regulation Base Demand Curve
  C
    ] * Min Run Time
Notes: Base Curve calculated monthly. Regions are based on historical results.

## Slide 15: Contingency Reserve Demand Curves
The regions specified for Contingency Reserve scarcity are based on the excess CR SPP carries relative to the largest resource contingency, as required by NERC
  Currently SPP carries Contingency Reserves protecting the largest resource contingency and half of the second largest in SPP
The regions may be adjusted as system conditions change
  Whenever the largest or next largest contingencies change
0.5 * Second Largest Gen Online (881MW)

## Slide 16: Biggest Lesson Learned
Regulation Deliverability
  SPP employs Reserve Zones to ensure deliverability of Reserves
  SPP clearing engine does not account for the deployment of cleared reserves on Operating Constraints
  Study is not granular enough to account for some real time system conditions
  When system is congested, resources that have an adverse effect on a constraint are pushed downwards
  This makes those resources prime candidates for clearing up Regulation UP
  Deployment of that regulation then acerbates the loading on the Operating Constraints
SPP had to make system changes to address inequities associated with this process
  Removed the buy back obligation for Resources that were manually removed from regulation by the SPP Operators

## Slide 17: Integrated Marketplace Implementation
Official Start in 2011
  Consolidated Balancing Authority, Congestion Rights Market, Day Ahead and Real Time Market, 5 minutes Settlements
  Budget was approximately $100 Million
    Approximately 2/3 of cost were Software and Systems
    Additional costs for program management and support
  Go-Live March 2014
    Reached $1 billion in savings in late 2016

## Slide 18: Integrated Marketplace Implementation
Official Start in 2011
  Consolidated Balancing Authority, Congestion Rights Market, Day Ahead and Real Time Market, 5 minutes Settlements
  Budget was approximately $100 Million
    Approximately 2/3 of cost were Software and Systems
    Additional costs for program management and support
  Go-Live March 2014
    Reached $1 billion in savings in late 2016
    Reduced overall regulation requirement for SPP by 20%

## Slide 19: Integrated Marketplace Implementation
Significant Stakeholder involvement
  Bi-weekly meetings to design and write tariff and protocols
  Co-optimization was one of primary goals
    Most efficient way to clear
    Provides opportunities for participants and savings for ratepayers

## Slide 20: Integrated Marketplace Scope/Readiness/Go-lIVE Issues
Scope
  Clearing Regulation Up and Regulation Dn as separate products initially created issues
    Mainly from commitment perspective
    Real Time market had less performance issues
Readiness
  Understanding economics of clearing particular product becomes more difficult. Significant learning opportunities for participants and staff.
Go-Live
  Previously discussed deliverability issues
  Majority of our issues were from a commitment perspective and not really related to co-optimization

## Slide 21: Tips/Tricks
Managing deliverability
  Constraint impacts
Ramp Rate interaction
  Ensuring appropriate ramp is available for all products
  Ramp Sharing
  Product Substitution
  Ramping Capability Product

## Slide 22: Questions?

## Slide 23
Gary Cate
Manager, Market Design
Please feel free to contact me at gcate@spp.org