## Slide 1
Item 4a – KP1.1 and KP3
RUC Items and the Reliability Deployment Pricing Run
Aaron Townsend
October 9, 2019

## Slide 2: Topics
Process for determining the amount of individual AS products that can be provided by a Resource for RUC
Potential floors for AS Offers on Resources committed through the RUC process
Continuation of the Reliability Deployment Price Adder process
QSEs instructed to be committed by RUC may elect to forgo RUC Settlement (i.e., continuation of opt out)

## Slide 3: AS Provision in RUC Studies

## Slide 4: AS Provision in RUC
With the RUC engine also co-optimizing energy and AS when analyzing future system conditions, it will need as input the amount of individual AS products that can be provided by a Resource
As part of KP3, TAC has already approved the following language:
  “Proxy AS Offers will be used in RUC in determining a co-optimized solution where AS Offers have not been submitted.”
Related to this, looking to discuss additional detail on the AS Offers and changes to information provided in the COPs

## Slide 5: Offers for AS Provision in RUC
ERCOT is proposing to use the same proxy methodology for AS offers in RUC as in Real-Time
  Proxy methodology for Real-Time is still under discussion, but the final determination for Real-Time will also be used in RUC
  This is most likely to result in the most accurate prediction of Real-Time outcomes
ERCOT is also proposing that RUC use the same scaling for AS offers that is currently applied to energy offers (=1/1000)
  The scaling would be applied to both submitted and proxy AS offers

## Slide 6: Additional COP Information for RUC
In addition to submitted and proxy AS Offers, RUC will also use COP information to determine how much capability for each AS product each Resource will be capable of providing in each hour of the RUC study period
Proposing change to the data elements in the COP where Resource AS Responsibilities are replaced with Resource AS Capabilities
  This new information will help limit the amount of AS that RUC can put on a Resource to values below the qualified amounts when the Resource is expected to have physical limitations in Real-Time
  RUC will also consider information like COP Resource Status when determining dispatch and placement of AS

## Slide 7: Offer Floors for ONRUC Resources in SCED and the Reliability Deployment Price Adder Process

## Slide 8: Addressing the Impacts Reliability Deployments
As part of KP1.1, RTCTF has discussed the following principle concept:
  “2) The existing process of having a pricing run to capture the effects of reliability deployments will continue. However, the pricing run will be modified to also co-optimize energy and AS. To account for the co-optimization in the pricing run, the following modifications will be made to the inputs:
  a. AS offers from Reliability Unit Commitment (RUC) instructed Resources, including RMR Resources, will be removed for the pricing run or be assigned a pre-defined high AS offer price .
Looking to discuss additional detail about the Reliability Deployment Price Adder process and the treatment of ONRUC Resources in both the dispatch and pricing runs

## Slide 9: Energy and AS Offer Floors for ONRUC Resources
Under RTC, RUC-instructed Resources may have been committed to help meet overall system-capacity needs, including AS needs
Today, ONRUC capacity has an energy offer floor of $1,500/MWh
Under RTC, ONRUC capacity will have the same energy offer floor
Under RTC, ONRUC capacity will be eligible for AS awards, subject to qualification, capability, and offer
ERCOT is proposing that the AS Offer floor for ONRUC capacity be $1,500/MWh, or the ASDC value at the AS Plan quantity, whichever is lower
  Applied in both the dispatch and pricing runs

## Slide 10: Example AS Offers of ONRUC Resource
Reg-Up Example
Reg-Up Offer floor for a RUC-instructed Resource able to provide Reg-Up:
  Minimum of $9,000/MWh and $1,500/MWh = $1,500/MWh
Chart: Reserves (MW)
| 0 | 250 | 250 | 250 | 250 | 250 | 250 | 250 | 250 | 250
REGUP | 9000 | 9000 | 9000 | 9000 | 9000 | 9000 | 9000 | 9000 | 9000 | 0
Price is $9,000/MWh at MW level equal to the AS Plan

## Slide 11: Example AS Offers of ONRUC Resource
RRS Example
RRS Offer floor for a RUC-instructed Resource able to provide RRS:
  Minimum of $4,800/MWh and $1,500/MWh = $1,500/MWh
Chart: Reserves (MW)
| 0 | 1750 | 1830 | 1910 | 1990 | 2070 | 2150 | 2230 | 2300 | 2300
RRS | 9000 | 9000 | 6379 | 6127 | 5866 | 5597 | 5322 | 5044 | 4799 | 0
Price is ~$4,800/MWh at MW level equal to the AS Plan

## Slide 12: Example AS Offers of ONRUC Resource
ECRS Example
ECRS Offer floor for a RUC-instructed Resource able to provide ECRS:
  Minimum of $1,100/MWh and $1,500/MWh = $1,100/MWh
Chart: Reserves (MW)
| 0 | 175 | 350 | 525 | 700 | 875 | 1050 | 1200 | 1350 | 1350
ECRS | 4188 | 4188 | 3591 | 3037 | 2518 | 2064 | 1666 | 1372 | 1118 | 0
Price is ~$1,100/MWh at MW level equal to the AS Plan

## Slide 13: Example AS Offers of ONRUC Resource
Non-Spin Example
Note: ASDC for Non-Spin goes beyond the AS Plan amount
Non-Spin Offer floor for a RUC-instructed Resource able to provide Non-Spin:
  Minimum of $415/MWh and $1,500/MWh = $415/MWh
Chart: Reserves (MW)
| 0 | 50 | 150 | 350 | 650 | 1050 | 1550 | 2250 | 3100 | 3100
NSPIN | 1044 | 1044 | 906 | 673 | 419 | 210 | 79 | 16 | 2 | 0
Price is ~$415/MWh at MW level equal to the AS Plan
AS Plan for Non-Spin
$1,500/MWh would not allow any Non-Spin to be awarded to the Resource

## Slide 14: Application of AS Offer Floors
Note that the AS Plan quantities vary by hour so under this proposal different hours will have different offer floors
ERCOT systems will apply the offer floors if the QSE-submitted offer is below the applicable floor
  This is the same as the energy offer floor today

## Slide 15: The Relevant Outputs the Reliability Deployment Price Adder Process will Change with RTC
Individual price adders will apply to energy as well as each AS product
  Energy price adder
  Regulation Up price adder
  Regulation Down price adder
  RRS price adder
  ECRS price adder
  NSRS price adder
AS price adders will be based on positive increase in MCPCs between dispatch and pricing runs

## Slide 16: Ability to Opt Out of RUC Settlement

## Slide 17: RTC and Opting Out of RUC Settlement
RTC will not affect the ability for QSEs to opt out of RUC settlement

## Slide 18: Proposed Principle Concepts – KP1
KP1.1
  The Reliability Deployment Price Adder process will apply to both energy and AS, and the adder for each AS product will be the positive increase in MCPC between the dispatch and pricing run

## Slide 19: Proposed Principle Concepts – KP3
KP3
  The RUC engine will use the same proxy methodology for AS as Real-Time
  The RUC engine will use the same scaling for AS offers as energy offers
  RUC will use new information contained in the COP to determine how much capability for each AS product each Resource will be capable of providing

## Slide 20: Proposed Principle Concepts – KP3, continued
KP3
  The Energy Offer Floor for RUC-instructed Resources which have not opted out of RUC settlement will be $1,500/MWh for both the dispatching and pricing run
  AS Offer Floors for RUC-instructed Resources which have not opted out of RUC settlement will be $1,500/MWh, or the ASDC value at the AS Plan quantity, whichever is lower, for both the dispatch and pricing runs
  RTC will not affect the ability for QSEs to opt out of RUC settlement

## Slide 21: Questions