## Slide 1
Item 3e – KP1.3 and 1.4
Resource Statuses and Telemetered AS Limitations
Sai Moorty
Principal, Market Design and Analysis
October 9, 2019

## Slide 2: Topics
AS Market Participation Matrix by Resource Type
Resource Statuses
QSE Telemetry for Temporary Restrictions on AS Awards

## Slide 3: AS Market Participation Matrix by Resource Type
 | RegUp |  | RegDn |  | RRS |  |  | ECRS |  | NSPIN
 | Conventional | FRRS Up | Conventional | FRRS Dn | PFR | UFR | FFR | Dispatchable | Blocky | 
GR | X |  | X |  | X |  |  | X |  | X
CLR | X |  | X |  | X |  |  | X |  | X
Battery Resource | X | X | X | X | X |  | X | X |  | X
Rapid-LR (UFR) |  |  |  |  |  | X |  |  | X | 
Rapid-LR (FFR) |  |  |  |  |  |  | X |  | X | 
Basic-LR |  |  |  |  |  |  |  |  | X | 

## Slide 4: RTC: Generation Resource Statuses
Resource Status | COP | Telemetry | Proposed use of Generation Resource Status under RTC
ON | Y | Y | Available for energy and AS awards
ONOPTOUT | Y | Y | Considered to be same as ON
ONRUC | Y | Y | Considered to be same as ON (specific rules for EOC and AS Offer)
ONOS | Y | Y | Applying current rules for output schedules, available for energy and AS awards this should no long be needed. Can’t have AS awards as to deploy them would move off the OS schedule. Also can not be in PRC
ONDSR | Y | Y | Applying current rules for DSR, available for energy and AS awards Needs more discussion
OFFQS | Y | Y | Considered to be same as ON for energy, ECRS and NSPIN. Cannot be awarded Regulation or Responsive Reserve If these units can not regulate, then how can they respond to a Setpoint from ERCOT that also moves around
OFF | Y | Y | Not available to for energy, RegUp, RegDn, RRS, or ECRS awards Available for NSPIN if qualified
ONTEST | Y | Y | Energy participation same as today. Not eligible for AS award Can unit be in PRC
ONEMR | Y | Y | Considered to be same as ON, Not eligible for AS award QSE may appropriately set LSL and HSL to reflect operating limits Can ths be in PRC
STARTUP |  | Y | Energy participation same as today. Cannot be awarded AS (BP=telMW+5*RRup) Exception is when OFF Resource deployed for Non-Spin and OFFQS awarded BP>0
SHUTDOWN |  | Y | Energy participation same as today. Cannot be awarded AS (BP=telMW-5*RRdn)

## Slide 5: RTC: Generation Resource Statuses
Resource Status | COP | Telemetry | Proposed use of Generation Resource Status under RTC
ONSC | Y | Y | (New Resource Status to replace ONRR, ONECRS) Hydro in Synchronous Condenser mode. BP=TelMW. Available for RRS, ECRS and NSPIN (?) awards AS deployed by frequency trigger or ERCOT Manual deployment If manually deployed, how is BP set?
ONHOLD |  | Y | (New Resource Status) Indicates unavailability to be moved up or down. BP=telMW Not eligible for AS award Example usage scenario: Combined Cycle Configuration transition, Boiler feed pump start, etc. Does this count in PRC
OUT | Y | Y | Not available for energy or AS awards
EMR | Y | Y | Not available for energy or AS awards How is BP set when on-line?
EMRSWGR | Y | Y | Not available for energy or AS awards How is BP set when on-line?

## Slide 6: RTC: Generation Resource Statuses Not Used
Resource Status | Generation Resource Status Not Used under RTC
ONREG | Status no longer needed
FRRSUP | Status no longer needed
ONOSREG | Status no longer needed
ONDSRREG | Status no longer needed
ONRR | Status no longer needed
ONECRS | Status no longer needed
ONFFRRRS | Status no longer needed
OFFNS | Status no longer needed
As a general rule, if AS is not available for any reason, then LDL=Act Gen=HDL. Is it counted in PRC?
Resource Statuses for Battery Resources will be a subset of that used for Generation Resources.
  Will be discussed later

## Slide 7: RTC: Load Resource Statuses
Resource Status | COP | Telemetry | Proposed use of Load Resource Status under RTC
ONL | Y | Y | (New Resource Status to replace ONRGL, ONCLR, ONRL,ONECL,ONFRRSL,FRRSDN,FRRSUP) I’m still not convinced this is the best solution for operating in the EEA?
OUTL | Y | Y | Not available for energy or AS awards
Resource Status | Load Resource Status Not Used under RTC
ONRGL | Status no longer needed
FRRSUP | Status no longer needed
FRRSDN | Status no longer needed
ONCLR | Status no longer needed
ONRL | Status no longer needed
ONECL | Status no longer needed
ONFFRRRSL | Status no longer needed

## Slide 8: RTC: QSE Telemetry for Temporary Restrictions on AS Awards
KP1.3 (Status: Under discussion at RTCTF)
  QSEs will have ability in Real-Time to indicate whether a Resource is temporarily unable to provide AS due to operational constraints. This should be a status bit indicating a particular AS is not available, ERCOT must be the enity that calculateds the amount of AS by type based on HSL-Act Gen.
KP1.4 (Status: Under discussion at RTCTF)
  Under RTC, there will be new telemetry types to be submitted by QSEs with respect to AS-specific maximum capability for any AS-qualified Resource. I do not think this will work as QSEs setting capability numbers asynchronously from when SCED runs. ERCOT needs to do this calculation. ERCOT must do this calculation to assure that sum of AS on a unit is not greater than HSL-act Gen.
  To better understand ramp capability for determining ECRS and Non-Spin awards, the following new telemetry points will be needed for Resources providing those services:
    A blended 10-minute Emergency Ramp Rate Up for the Resources that will be used to check the feasibility of ECRS awards. This value will be the 10-minute output change capability of the Resource divided by 10 (positive change for Resources injecting into the grid and negative change for Resources withdrawing from the grid).
    A blended 30-minute Normal Ramp Rate Up for the Resources that will be used to check the feasibility of Non-Spin awards. This value will be the 30-minute output change capability of the Resource divided by 30 (positive change for Resources injecting into the grid and negative change for Resources withdrawing from the grid).

## Slide 9: Feedback On Allowing Resource Telemetry Indicating Temporary Inability To Provide AS
Need to ensure that RTC has a check that estimation calculation of PRC using HSLs and Act Gen from available AS Offers is greater than the actual PRCAS Awards, otherwise RTC dispatch is invalid – related to AS participation rules/Proxy AS Offer

## Slide 10: Feedback On Allowing Resource Telemetry Indicating Temporary Inability To Provide AS
Consider use of existing status telemetry of Raise Block Status (RBST) and Lower Block Status (LBST) in RTC to limit Base Point and AS awards
  Currently, used only in LFC for the intra 5 minute period to freeze UDBP
Options under RTC:
  Option1: Discontinue the use of these status telemetry in all ERCOT systems
  Option2:
  Continue to use these two telemetry status indicators for purposes of intra 5 minute freeze of UDSP and Regulation.
  ERCOT systems will NOT include applicable Resource capacity in the determination of PRC if either of RBST or LBST is set
  Monitor duration of time when either RBST or LBST is set and raise alarm if it exceeds threshold
  If RBST, and/or LBST is set at time of RTC run,
    Resource ineligible for AS awards by RTC in that run
    If RBST is set, HDL=TelemMW; BasePoint cannot exceed Telemetered MW
    If LBST is set LDL=TelemMW; BasePoint cannot be less than Telemetered MW

## Slide 11: Feedback On Allowing Resource Telemetry Indicating Temporary Inability To Provide AS
On proposed new telemetry to limit AS awards by RTC, are all of them required?
    Why would a QSE provide a Resource specific telemetry limiting awards for ECRS but the HDL for Resource indicates it can receive a Base Point higher than its current output level?

## Slide 12: RTC: Generation Resource Telemetry for Temporary Restrictions on Regulation Awards
Resource RegUp Award
Option 1: Keep both telemetered quantities, note Limited Duration Resource will require both quantities
Option 2: For Generation Resources, only use NRRUp, as this is already used for HDL calculation
Telemetered Normal Ramp Rate (MW/Min) reflecting 5 minute capability
Telemetry (MW value) to indicate maximum RegUp MW capability
Both these telemetered quantities (MW, MW/min) are submitted by QSEs for each Resource.
Is having QSE submit both telemetered quantities necessary?
Same question applies for RegDn

## Slide 13: RTC: Generation Resource Telemetry for Temporary Restrictions on ECRS Awards
Resource ECRS Awards
Option 1: Keep both telemetered quantities, justification?
Option 2: Only use TelMxECRS; the QSE shall use ERRUp10 concept in determining the telemetered maximum ECRS MW capability
Telemetered Emergency Ramp Rate (MW/Min) reflecting 10 minute capability
Telemetry (MW value) to indicate maximum ECRS MW capability
Both these telemetered quantities (MW, MW/min) are submitted by QSEs for each Resource.
Is having QSE submit both telemetered quantities necessary?

## Slide 14: RTC: Generation Resource Telemetry for Temporary Restrictions on NSPIN Awards
Resource NSPIN Awards
Option 1: Keep both telemetered quantities, justification?
Option 2: Only use TelMxNSPIN; the QSE shall use NRRUp30 concept in determining the telemetered maximum NSPIN MW capability
Telemetered Normal Ramp Rate (MW/Min) reflecting 30 minute capability
Telemetry (MW value) to indicate maximum NSPIN MW capability
Both these telemetered quantities (MW, MW/min) are submitted by QSEs for each Resource.
Is having QSE submit both telemetered quantities necessary?

## Slide 15
Discussion