## Slide 1: Summary of NPRR826
Summary of latest comments (6/27/19 Reliant) below.
NPRR826 establishes a methodology to set the Mitigated Offer Cap (MOC) for RMR Resources based on a “last in line” concept.
The objective is to minimize the impact of an RMR Resource (out of market action) on competitive market outcomes.
NPRR826 includes criteria that must be met before the methodology will be used. If all of the criteria is not met, the RMR Resource will be mitigated based on cost.

## Slide 2: Summary of NPRR826
The RMR MOC methodology in NPRR826 will only be applied to an active constraint when all 3 conditions are true:
  The RMR Resource has a 2% or more unloading shift factor on the transmission facility;
  The RMR Resource has a 5% unloading impact* on the transmission facility; and
  At least one other non-RMR Resource has a 5% or more unloading shift factor on the transmission facility.
*Unloading impact is reduction of flow on the transmission facility and is used in ERCOT’s evaluation of whether the unit would be an effective RMR Resource.

## Slide 3: Summary of NPRR826
The RMR MOC methodology in NPRR826 works as follows (i.e. to create the line):
  Identify all non-RMR Resources that have a 2%* or more unloading shift factor on the transmission facility;
  Collect the highest energy offer point (mitigated if applicable) for each Resource in step 1 and convert to a shadow price equivalent;
  Select the highest value from step 2 and ensure it is less than the shadow price cap for the constraint by $1;
  Add $0.01 to the value from step 3, multiply by the shift factor of the RMR Resource to convert back to an energy offer equivalent, and set as the RMR MOC; and
  If there are multiple constraints, use the lowest value from step 4.
*2% is set as a default value and can be updated by TAC.

## Slide 4: Suggested Next Steps
Approve NPRR826 with 10/10/19 PRS desk edits (language clarifying use of mitigated offers on top of 6/27/19 Reliant comments).
Consider IA at November PRS meeting.
Table at TAC until PUCT Project 49788 (Rulemaking to Amend 16 TAC § 25.502) is complete.