## Slide 1
Energy Storage Resources
Nodal pricing
Nodal dispatch
Bids to buy
Paul Wattles
ERCOT Staff
BESTFORCE
Oct. 18, 2019

## Slide 2: Principle Market Design Framework for Storage Resources
An Energy Storage Resource (ESR*) should be settled at a nodal price when either charging (withdrawing) or discharging (injecting)
An ESR should be active in SCED for both charging and discharging
SCED should dispatch an ESR on its nodal shift factor when either charging or discharging
* ESR terminology as set forth in NPRR 957, endorsed by PRS 9/12/19, IA endorsed by PRS 10/10/19

## Slide 3: Current and future scenarios
Until mid-2024, an ESR will continue to be modelled as both a Generation Resource (GR) and a Controllable Load Resource (CLR)
  ‘Combo model’ approach
The principle framework (previous slide) will be a reality when the single model approach is implemented in 2024. An ESR:
  Will be settled at a nodal price whether it is charging or discharging
  Will charge based on the equivalent of a Real-Time Energy Bid in SCED
  Will be dispatched by SCED on a nodal shift factor in both charge and discharge mode
ERCOT is proposing to implement these concepts for the rest of the combo model era

## Slide 4: Background: Nodal vs. zonal pricing
Under current Protocols, CLRs can participate in SCED by submitting RTM Energy Bids to buy power ‘up to’ their specified price
  Enabled by NPRR 555, Load Resource Participation in SCED, approved by the ERCOT Board Sept. 2013 and implemented in 2014
Nodal Protocols 3.6.1 (5):
  ‘The Settlement Point for a Controllable Load Resource with a Real-Time Market (RTM) Energy Bid is its Load Zone Settlement Point.’

## Slide 5: Background: SCED participation
Battery ESRs are well-suited to SCED dispatch on both the discharging (GR) and charging (CLR) sides
  ESR-GRs routinely participate in SCED with Energy Offer Curves
  SCED qualification for the CLR side of an ESR should not be a challenge
To date, no ESRs have sought SCED qualification for the CLR side
  Instead of charging based on a Bid to buy, ESRs are changing status to OUTL and charging outside of SCED
  This will not be an option under the single model approach

## Slide 6: Background: SCED dispatch
Nodal Protocols 6.5.7.3 (1):
  ‘The SCED process is designed to simultaneously manage energy, the system power balance and network congestion through Resource Base Points and calculation of LMPs every five minutes. The SCED process uses a two-step methodology that applies mitigation prospectively to resolve Non-Competitive Constraints for the current Operating Hour. The SCED process evaluates Energy Offer Curves, Output Schedules and Real-Time Market (RTM) Energy Bids to determine Resource Dispatch Instructions by maximizing bid-based revenues minus offer-based costs, subject to power balance and network constraints. The SCED process uses the Resource Status provided by SCADA telemetry under Section 6.5.5.2, Operational Data Requirements, and validated by the Real-Time Sequence, instead of the Resource Status provided by the COP. An RTM Energy Bid represents the bid for energy distributed across all nodes in the Load Zone in which the Controllable Load Resource is located.’
Result: The ERCOT system today is designed to dispatch all CLRs – including ESR CLRs – based on the Load Zone shift factor
  This is appropriate for an Aggregated Load Resource, but not for an ESR

## Slide 7: ERCOT’s Proposal
Require ESRs to be settled at a nodal price whether discharging (injecting) or charging (withdrawing)
Require ESRs to charge based on SCED dispatch on an RTM Energy Bid to buy
  This will align their behavior today with other SCED-dispatched Resources
  It will prepare them for the single model era, when SCED dispatch will be mandatory
  It will also provide ERCOT with operational visibility that it does not have today
Clarify that an ESR will be dispatched by SCED on its nodal shift factor whether charging or discharging

## Slide 8: Footnote: Wholesale Storage Load
Withdrawals would be settled at a nodal price regardless of whether the ESR is receiving Wholesale Storage Load (WSL) treatment
  Existing ESRs with WSL treatment* would continue to receive WSL, but they would also:
    be required to submit RTM Bids,
    be dispatched on their nodal shift factor, and
    receive base point weighted pricing (when charging)
  WSL would remain an option for future ESRs with ERCOT-approved metering configurations
* All ESRs today are receiving WSL treatment.

## Slide 9: Footnote: Settlement Only Storage
This proposal would apply only to ESRs, but the concept is also appropriate for Settlement Only storage
  Settlement Only treatment will be addressed under different Key Concepts
  Settlement Only storage terminology expected to be introduced in a future RTF NPRR

## Slide 10
Questions?