## Slide 1
KP1.5 - RTC Emergency Settlement
Austin Rosel
October 9, 2019

## Slide 2: SCED Failure under RTC
Under KP1.5, RTCTF has discussed how the SCED failure process would work under RTC.
  QSEs may need to “hold” an issued basepoint for a period of time longer than a normal SCED run under certain conditions.
  With SCED level AS awards under RTC, QSEs may need to similarly “hold” their AS awards.

## Slide 3: SCED Failure under RTC
Depending on length of the failure and grid conditions, QSEs may be issued Emergency Base Points due to an Emergency Condition or Watch.
There is no corresponding emergency AS award under RTC.
To keep RTC processes in alignment with today’s processes and avoid unneeded complication, the proposal is to have Emergency Base Points factor in the last good set of AS awards
  Non-AS capacity on Resources would be utilized ahead of AS capacity

## Slide 4: Emergency Settlements
QSEs with held Base Points and Emergency Base Points are considered for additional compensation if the RTSPP is less than the price on the QSE’s EOC (capped by the MOC) at the “held” or Emergency Base Point.
  This ensures that QSE is not receiving a price and Base Point combination that forces the QSE to operate at less than cost.
There are no proposed changes to this settlement under RTC, this treatment will continue.

## Slide 5: Emergency Settlements
ERCOT is not proposing any new settlement calculations for AS awards under RTC for held awards.
  In the event of a “hold”, the AS price and award for a QSE will be extended and considered in the AS Imbalance Settlement until new awards and prices are created in a subsequent SCED run.
  There is no equivalent mitigated cost curve associated with AS offers that the QSE would need to be made whole to.
  Utilizing non-AS capacity ahead of AS capacity for Emergency Base Points allows system to maintain the AS, should result in a smoother transition when SCED runs again, and minimizes the need for any settlement changes.

## Slide 6: Proposed Principle Concepts
As part of determining Emergency Base Points, RTC systems will consider the AS award from the most recent SCED execution. AS awarded capacity will be prioritized ahead of non-AS awarded capacity and Regulation and RRS will be prioritized ahead of ECRS and Non-Spin.
No new settlement calculations will be needed to address the case where there is a SCED failure.