## Slide 1
NPRR970 Reliability Unit Commitment (RUC) Fuel Dispute Process Clarification
&
VCMRR026 Related to NPRR970, Reliability Unit Commitment (RUC) Fuel Dispute Process Clarification
Ino González
WMWG
October 21, 2019

## Slide 2: NPRR617 Energy Offer Flexibility
NPRR617 allows generators to submit SUO and MEO up to 200% of costs in DAM.
Before Implementation of NPRR617
SUO and MEO were capped at costs (both in DAM and RUC)
RUC Cost Guarantee (RUCG)
RUCG = SUO + MEO* Min (LSL, RTMG)
Where,
SUO = Startup Offer
MEO = Min Energy Offer
RTMG = Real-Time Metered Generation (MWh)

## Slide 3: NPRR617 Energy Offer Flexibility
After Implementation of NPRR617
The SUO and MEO are capped at 200% of costs (in DAM only)
RUC Cost Guarantee (RUCG)
RUCG = Min (SUO1, SUCAP) + Min(MEO1, MECAP) * Min (LSL, RTMG)
Where,
SUCAP = Startup Cap
MECAP = Min Energy Cap
1 SUO and MEO can exceed their respective costs

## Slide 4: RUC Fuel Dispute Process
Before Implementation of NPRR617
RUC Cost Guarantee (RUCG)
RUCG = SUO + MEO* Min (LSL, RTMG)
ERCOT had no way of knowing how the Offers were constructed and as such, there was no way to know exactly how fuel purchases impacted Offers.
Appendix 8 in the VC Manual included a procedure for estimating the change to the SUO and MEO as a result of higher fuel costs.

## Slide 5: Other Changes
After Implementation of NPRR617
RUC Cost Guarantee (RUCG)
RUCG = Min (SUO, SUCAP)1 + Min(MEO, MECAP)1* Min (LSL, RTMG)
Offers can exceed costs
SUCAP and MECAP can be calculated with updated fuel costs
RUC fuel disputes are now processed by modifying the SUCAP and MECAP.
Example:
SUCAP = Startup fuel * (FIP + Fuel Adder) + O&M
Where, (FIP + Fuel Adder) is replaced by actual fuel costs

## Slide 6: Other Proposed Changes
Clarify that the Fuel Index Price (FIP) and Fuel Oil Price (FOP) are adjusted by the proxy fuel adder, X, as defined in the Verifiable Cost Manual.

## Slide 7
Questions?