## Slide 1
NPRR971 Changing Energy Offer Curve Caps for Make-Whole Calculation Purposes and Replacing the Real-Time Average Incremental Energy Cost
Ino González
WMWG
October 21, 2019

## Slide 2: NPRR971 Objectives
Part 1: Replace the Real-Time Average Incremental Energy Cost with Energy Offer Curve Caps
Part 2: Update Energy Offer Curve Caps (EOCPRCAP) for Make-Whole Calculation Purposes

## Slide 3: Part 1: Average Incremental Energy Cost (AIEC)
AIEC = Area under curve
(RTMG*4-LSL)
$/MWh
MW
RTMG*4
LSL
EOCPRCAP = Heat Rate * FIP
Average cost for supplying energy from the LSL to the RTMG*4

## Slide 4: Part 1: AIEC in RUC Make-Whole Payment Calculation
Energy Offer Curves for RUC-Committed Resources have a $1500 floor price
Calculate Resource Revenues
  Per QSE
  Per Resource
  Per Operating Day with RUC Commitment
$/MWh
MW
LSL
Costs
(AIEC)
SPP
RTMG * 4
Energy Offer Curve
EOCPRCAP
Revenues
$1500
HSL
Revenue Less Cost Above LSL During RUC-Committed Hours
Notes: The next piece we need to calculate is the Revenue less costs above the LSL during RUC-Committed hours. In this calculation, the energy cost is derived from the Resource’s Energy Offer Curve or proxy Energy Offer Curve as applicable. Just as with the Day-Ahead Make Whole settlement, ERCOT will calculate the Average Incremental Energy Cost (AIEC) from the Energy Offer Curve, limited by the same Make-Whole Cap. The difference with the Real-Time AIEC is that we now use RTMG*4 as the cleared MW value.
This calculation is calculated per QSE, per Resource, per Operating Day for all the RUC-Committed Hours in that Operating Day.

## Slide 5: Part 1: AIEC Used in other Calculations
DAM Make-Whole Payment – Not proposing a change
HDL Override – proposing a change
Voltage Support – proposing a change
Notes: The next piece we need to calculate is the Revenue less costs above the LSL during RUC-Committed hours. In this calculation, the energy cost is derived from the Resource’s Energy Offer Curve or proxy Energy Offer Curve as applicable. Just as with the Day-Ahead Make Whole settlement, ERCOT will calculate the Average Incremental Energy Cost (AIEC) from the Energy Offer Curve, limited by the same Make-Whole Cap. The difference with the Real-Time AIEC is that we now use RTMG*4 as the cleared MW value.
This calculation is calculated per QSE, per Resource, per Operating Day for all the RUC-Committed Hours in that Operating Day.

## Slide 6: Part 2: Update Energy Offer Curve Caps (EOCPRCAP)
Some Existing Caps
4.4.9.3.3 Energy Offer Curve Caps for Make-Whole Calculation Purposes
Coal and Lignite = $18.00/MWh;
Combined Cycle greater than 90 MW = 9 MMBtu/MWh * ((Percentage of FIP * FIP) + (Percentage of FOP * FOP))/100, as specified in the Energy Offer Curve;
Hydro = $10.00/MWh;
(l) Other = SWCAP;

## Slide 7: Part 2: Update Energy Offer Curve Caps (EOCPRCAP)
Updated Caps for Some Resource Categories
4.4.9.3.3 Energy Offer Curve Caps for Make-Whole Calculation Purposes
Coal and Lignite = 12.80 MMBtu/MWh * ((Percentage of FIP * FIP) + (Percentage of FOP * FOP))/100, as specified in the Energy Offer Curve;
Combined Cycle greater than 90 MW = 10.4 MMBtu/MWh * ((Percentage of FIP * FIP) + (Percentage of FOP * FOP))/100, as specified in the Energy Offer Curve;
(l) Other = $53.00/MWh;

## Slide 8
Questions?