## Slide 1
Discussion on proposed Solar PV Growth Projection using an S-curve Model
Supply Analysis Working Group
September 27, 2019

## Slide 2: S-Curve Growth Projections
Initial Methodology Proposed at April 12, 2019 SAWG Meeting
  http://www.ercot.com/calendar/2019/4/12/172702-SAWG
Chart: Installed Cumulative MW at end of Year
| 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029
 | 500.0003 | 809.4202 | 1379.8149 | 2190.7544 | 3001.6939 | 3572.0886 | 3881.5085 | 4026.0933 | 4088.9298 | 4115.3745 | 4126.3527 | 4130.8843

## Slide 3: S-Curve Major Variables
“Fixed” Variables
  Total potential: 18,433 MW, is based on Table 4.3 of the AWS Truepower report, "Solar Site Screening and Hourly Generation Profiles," prepared for ERCOT representing development for the four major metropolitan areas in ERCOT (DFW, Houston, San Antonio, Austin)
    Link: http://www.ercot.com/content/wcm/lists/114800/ERCOT_Solar_SiteScreenHrlyProfiles_Jan2017.pdf
  Base year and Value: 500 MW for 2018 based on ERCOT data presented at April 12, 2019 SAWG meeting.
    http://www.ercot.com/content/wcm/key_documents_lists/172703/SAWG__Meeting_4-12-2019_DistGenData.pptx
  Baseline MW calibration factor: TBD (Adjusted so that 2018 = 500 MW)

## Slide 4: S-Curve Major Variables
Variables for discussion
  Additional Capacity Potential outside 4 major cities: 10% selected
        The larger the number, the greater the final installed MW
        ERCOT will have UL look at non-metropolitan solar PV potential next year
  Market Saturation: 20% selected
        The larger the number, the greater the final installed MW.
  Start of Fast Growth: 2019 (selected for ITC Credit rampdown)
  Takeover Time (Years): 4 (Selected for more geometric growth)
        The larger the number, the slower the growth
  Smoothing parameter: 35 (selected to provide a geometric growth)
        Must be greater than 15 to solve

## Slide 5: Effects of Variable changes
Chart: Installed Cumulative MW
| 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029
 | 500 | 656.8545 | 858.5433 | 1108.8421 | 1406.1417 | 1741.4189 | 2098.1107 | 2454.8025 | 2790.0798 | 3087.3793 | 3337.6781 | 3539.367
Smoothing changed to 100
Takeover time changed to 10
Chart: Installed Cumulative MW
| 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029
 | 499.9995 | 822.8419 | 1417.9802 | 2264.0982 | 3110.2161 | 3705.3544 | 4028.1969 | 4179.0537 | 4244.6161 | 4272.2079 | 4283.6623 | 4288.3905
Chart: Installed Cumulative MW
| 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029
 | 500 | 744.3488 | 1349.9685 | 2403.2942 | 3456.6199 | 4062.2397 | 4306.5884 | 4390.7437 | 4418.111 | 4426.8431 | 4429.6122 | 4430.4887
Takeover time 4
Smoothing 35
Start of growth 2019
Chart: Installed Cumulative MW
| 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029
 | 500 | 565.5624 | 716.4193 | 1039.2617 | 1634.4 | 2480.5179 | 3326.6359 | 3921.7742 | 4244.6166 | 4395.4735 | 4461.0359 | 4488.6277
Start of Growth changed to 2021