## Slide 1: Offer Floors for ONRUC Resources in SCED (KP 1.3) and the Reliability Deployment Price Adder Process (KP 1.1) – Luminant Comments

## Slide 2: RUC/RMR Treatments: Today vs. RTC
Today’s RUC treatment:
  Energy price impact is mitigated via energy offer floor of $1500/MWh and RDPA run
  Scarcity price impact is mitigated via removal of RUC/RMR capacity from ORDC adder calculations
Under RTC:
  ERCOT’s initial proposal covers the energy price impact (energy offer floor of $1500/MWh and RDPA run)
  Real-time AS and scarcity pricing are inextricably linked under RTC, however, so need to make two separate but coordinated policy cuts
    Scarcity pricing impact: not currently addressed in Key Principles
    AS offer floor: depends on how scarcity pricing impact is addressed
Goal: ensure that RUC AS offer floors and scarcity pricing treatment are coordinated and consistent with current treatment

## Slide 3: RUC Scarcity Pricing Options
Option #1: Another pricing run with RUC capacity assigned to AS removed (should result in scarcity pricing by moving further up ASDC), and assign through another adder
Option #2: Utilize existing ORDC calculations to estimate value of removing RUC/RMR capacity from aggregate ASDC, then assign through another adder
Option #3: Right-shift the aggregate ASDC by the HSL of the RUC/RMR resource, allocate to individual ASDCs (could base on minimum AS requirement share, aggregate ASDC share, or some other allocation scheme)
Option #4: Proxy RUC scarcity pricing impact correction via RUC AS offer floors (may require use of AS proxy floors if the required offer floor exceeds SWOC)
  Set RUC AS offer/proxy floor to 75th percentile of ASDCmax
  Set RUC AS offer/proxy floor to MAX($1500, ASDC value at the AS Plan quantity)
  Set RUC AS offer/proxy floor at flat figure (e.g., $1500, $2000, possibly higher)

## Slide 4: Conceptual Example – Option #1
Chart: Reserves (MW)
| 0 | 50 | 150 | 350 | 650 | 1050 | 1550 | 2250 | 3100 | 3100
NSPIN | 1044 | 1044 | 906 | 673 | 419 | 210 | 79 | 16 | 2 | 0
AS Plan for Non-Spin
(1) Assume NSRS clears at 2,250 MW ($16) but includes 700 MW of RUC’d capacity
(2) 700 MW RUC adjustment  corrected ASDC price should be based on 1,550 MW point on ASDC ($79)  Adder = $79 - $16 = $63/MWh
Note: NOT suggesting that a unit should be RUC’d for NSRS, only illustrating potential scarcity pricing impact

## Slide 5: Conceptual Example – Option #2
Chart: Reserves (MW)
(1) Assume NSRS clears at 2,250 MW ($16) but includes 700 MW of RUC’d capacity
Same 700 MW RUC adjustment if reserves ~6,500 MW would be the difference between the ORDC price at 6,500 MW and at 5,800 MW  Adder = ~$107 - ~$47 = ~$60/MWh

## Slide 6: Conceptual Example – Option #3
Chart: Reserves (MW)
| 0 | 50 | 150 | 350 | 650 | 1050 | 1550 | 2250 | 3100 | 3100
NSPIN | 1044 | 1044 | 906 | 673 | 419 | 210 | 79 | 16 | 2 | 0
Chart: 
| 0 | 50 | 150 | 350 | 650 | 1050 | 1550 | 2250 | 3100 | 3100
NSPIN | 1044 | 1044 | 906 | 673 | 419 | 210 | 79 | 16 | 2 | 0
AS Plan for Non-Spin
(1) Assume NSRS clears at 2,250 MW but includes 700 MW of RUC’d capacity
(2) 700 MW RUC shift to ASDC  new ASDC price at 2,250 MW point on ASDC ($79)  Adder = $79 - $16 = $63/MWh
Note: NOT suggesting that a unit should be RUC’d for NSRS, only illustrating potential scarcity pricing impact
Shifted ASDC

## Slide 7: Proposed Principle Concepts
KP 1.1(7)
  Effect of the existing policy of removing RUC and RMR capacity from the calculation of the ORDC adder will be preserved as faithfully as possible
    Option #1 or #3 would be the most consistent with RTC trend of internalizing costs and adders to LMPs; Option #2 would be most consistent with today’s treatment
    Option #4 permutations not mutually exclusive to Options #1-3 (still need a RUC AS offer floor) but more pressing if Options #1-3 are not workable
KP 3(17)
  Depending on approach taken re: KP 1.1(7) above, may or may not need adjustment (but adjustment may be desired regardless)
  At a minimum, seems safe to say that RUC AS offer floors should be “the same” for both the dispatch and pricing runs.
  Need to consider AS offer floor impacts on ability for SCED to use RUC’d capacity for AS