## Slide 1
Single Model Settlement Changes
Austin Rosel
ERCOT
BESTF Meeting
11/4/2019

## Slide 2: Single Model Settlements
This presentation covers settlement changes necessary to support migration to single model ESR under Real-Time Co-optimization, listed under KTC-7.
This presentation does not discuss item number 4 under KTC-7, the settlement of SODG and SOTG at Nodal pricing for both charging and discharging. That conversation is tentatively scheduled for February 2020.

## Slide 3: DAM
Day-Ahead Energy Charge – No change, negative awards will be settled as Day Ahead Energy Purchases at Resource Node SPP.
Day-Ahead Make-Whole Payment– No change, ESRs will not require a DAM Make-Whole. With $0 startup, $0 minimum energy and no temporal constraints DAM awards will not be inconsistent with offer.
DAM CRR Settlement Changes –
  Need a minimum and maximum resource price used in deration calculations for ESR type. Currently use “other” (-$20/Mwh, $100/Mwh).

## Slide 4: DAM
Day-Ahead Energy Payment – No change
Day-Ahead Make-Whole Charge – No change
PTP Obligations – No change
Ancillary Service Payments – No Change
Ancillary Service Charges – No Change

## Slide 5: RTM
RUC Make Whole Payment/ Clawback Charge– No change, ESRs will not be RUC committed.
RUC Decommitment Payment – No change, with $0 startup, no payment will be required.
RUC Capacity Short Charge –
  Possible change, needs more discussion.
  Currently for batteries, the Load Resource capacity is not considered in capacity short calculations.
  The Capacity Short Charge under RTC needs to properly account for capacity and AS Responsibility of the new single ESR.

## Slide 6: RTM
Real-Time Energy Imbalance – Change, ESR load will be charged a Base Point Weighted Nodal price in Real-Time. Currently non-WSL load is charged a zonal price, and WSL load is charged a load weighted Nodal price.
Base Point Deviation – New BPD calculation to measure performance for the single resource that considers both positive and negative base points and both and generation and load for the ESR.
Emergency Energy – Extend current rules to negative Base Points. If the negative Base Points for an ESR are inconsistent with Real-Time Settlement Point Prices the QSE will be considered for additional compensation similar to how conventional generation is considered today.

## Slide 7: RTM
All Load allocated payment/charges – No policy change, load for an ESR that is not Wholesale Storage Load will still be incorporated into load allocated charges.
Real-Time DC Tie Import / Block Load Transfer – No change
Real-Time HDL Override Payment – No change
Real-Time Congestion Payment – No change
Voltage Support Payment – No change
Black Start Payment – No change
RTM Ancillary Services – No change
RMR/MRA – No Change

## Slide 8: Questions?