## Slide 1
KTC-7: Base Point Deviation Charges for Energy Storage Resources- Single Model
Magie Shanks
ERCOT
BESTF Meeting
11/04/2019

## Slide 2: Overview
Create a new Base Point Deviation (BPD) Settlement for the Single Model Energy Storage Resource (ESR).
Incorporate proposal for tiered deviation tolerances for ESRs.

## Slide 3: Base Point Deviation Settlement
The ESR:
  Will be registered as a single Resource.
  Can receive both positive and negative SCED base points.
  Will telemeter generation/consumption as a single value, either positive or negative, for the Resource.
BPD for ESR will mimic both the current BPD settlement for Generation Resources and Generation and Controllable Load Resource (GCLR) Group (proposed in NPRR963).

## Slide 4: Base Point Deviation Settlement
Chart: Settlement Intervals
| 1 | 2 | 3
Tolerance | 3.0833 | 2.0833 | -4.0833
AABP in MWh | 2.3333 | 1.3333 | -3.3333
AABP | 2.3333 | 1.3333 | -3.3333
Chart: 
| 1 | 2 | 3
AABP in MWh | 2.3333 | 1.3333 | -3.3333
Gen/Cons | 8.3333 | 1.6667 | -6.1667
UNDER
OVER
Tolerance
Tolerance
Tolerance

## Slide 5: Deviation Tolerances
Tiered Approach based on AABP for ESR
  AABP = AVGBP + AVGREG
Proposed ESR Tolerances:
  ABS(AABP) ≤ 10 MW
    3 MW or 3% of AABP
  ABS(AABP) > 10MW
    5 MW or 5% of AABP

## Slide 6: Questions?