## Slide 1
AS Trades in RTC
Carrie Bivens
October 30, 2019

## Slide 2: Current AS Trade Submission Process
The Buying and Selling QSE each submit a trade containing the following:
  Buying QSE name
  Selling QSE name
  AS Type: RegUp, RegDn, RRSGN, RRSLD, RRSNC, or NSRS
  MW quantity
MMS performs essentially no validation on trades, other than to ensure the fields are filled out and valid.

## Slide 3: AS Trades: Today’s Process
If the trades match, they are “Confirmed”, and used in the AS Responsibility Check.
For each QSE and AS type, the AS Responsibility Check balances:
  If a QSE is short overall on a particular AS, then the AS Responsibility Check will send a message detailing the shortage.
    If not resolved, there is a failure to provide and the operator will open a SASM if needed.
    Other than this limited SASM interplay, the trade quantities have no market impacts.
Self-arranged AS
DAM AS Awards
AS Trades as Seller
Against
AS in COPs
AS Trades as Buyer

## Slide 4: AS Trades: Current Process in RTC Design
AS trade quantities for Load Resources providing RRS or ECRS will be used to determine the self-provision cap per QSE.
  Self-provision cap:
      1 Self-Arranged AS is limited by AS obligation and the any constraints on sub-types.
      2 DAM AS Awards are also constrained by the sub-type constraints.
This process might result in a case where one QSE’s excess trade volume results in pro-rations for all QSEs in RTC.
  Only applies to AS types with self-provision caps
Self-Arranged AS1
DAM AS Awards2
AS Trades as Seller
Against
AS Trades as Buyer

## Slide 5: Simplified Example: Current RTC design
150 MW
36
27
Assume RRS plan = 150 MW. RRS limit from NCLR is set to 60%; NCLR limit is 90 MW
QSE A has an AS Obligation of 50 MW. Self-arranged NCLR is limited to 30 MW. QSE A self-arranges 30 MW of NCLR.
QSE B is awarded 30 MW of RRSNC in the DAM.
QSE C has an AS Obligation of 50 MW. They trade to buy 40 MW of NCLR, but their NCLR limit is 30 MW.
Total NCLR of 100 MW exceeds 90 MW limit. All NCLRs pro-rated down to 90% to reach 90MW.
QSE C exceeding their NCLR limit causes QSE A and QSE B to lose 3 MW each of NCLR.
30
30
NCLR 60% limit
90 MW
27
NCLR 60%
limit
All NCLRs pro-rated to under the 60% cap
3(B)
3(A)
4(C)
NCLR
over limit
NCLR
reductions
40
RRS Plan

## Slide 6: Example Scenario - Forward Bilateral
QSE B - Buying QSE (Has a load ratio share (LRS))
QSE S - Selling QSE (Has a Load Resource)
QSE B and QSE S enter into a bilateral agreement for RRS of RRSNC subtype (non-controllable load resource) for 50 MW (using pre-NPRR863 MMSUI terminology)
QSE B
QSE S
50 MW
RRSNC

## Slide 7: Example Scenario – Morning of the Day-Ahead
QSE B ends up with an RRS Obligation of 75 MW, based on their LRS
  They are restricted to self-arranging 60% of their RRS Obligation from NCLRs
  Therefore, they self-arrange 45 MW (75 MW * 60%) of RRSNC
In DAM, the total self-arranged NCLR MWs are subtracted first from the 60% total NCLR limit.
  If there's any remaining room, RRS will be awarded to additional Load Resources up to the 60% cap
QSE B
RRS Obl.=75
RRSNC=45
QSE S
50 MW
RRSNC

## Slide 8: Example Scenario – 1430 in the day-ahead
QSE B submits a 50 MW trade to ERCOT, for RRSNC subtype, with QSE B as the buying QSE and QSE S as the selling QSE
QSE S submits a 50 MW trade to ERCOT, for RRSNC subtype, with QSE B as the buying QSE and QSE S as the selling QSE
They match, and are therefore "confirmed"
QSE B
RRS Obl.=75
RRSNC=45
QSE S
50 MW
RRSNC

## Slide 9: Example Scenario – Issue Based on Current Design
A pre-process will calculate QSE S's self-provision cap.
The cap consists of their DAM RRS award (if any), plus their self-arrangement for RRSNC (if any), plus their net sell MWs for RRSNC.
  In this case, it is 50 MW (assume no other trades, awards, etc.)
When all the self-provision MWs are added up, system-wide ERCOT is 5 MW over.
To maintain the limit, all Load Resources NCLR quantity will be reduced pro-rata by a total of 5 MW to get under the limit.
NCLR
reductions
NCLR 60%
limit

## Slide 10: AS Trades: Proposal
Net trade
+15 MW
Net trade
+35 MW
Net trade
+75 MW
Net trade
+100 MW
If QSEs with LRS have confirmed trades in excess of their self-arrangement maximum, then ERCOT will inform them of the overage quantity and give some time to resolve with the selling QSE.
  If it is not resolved by 1800 in the day-ahead, then ERCOT will cancel the buying QSE side of trades on a last-in, first-out basis to the extent necessary to get under the limit.
    A firm time is being proposed since there are two parties involved that need to know their net trade position w/r/t ERCOT systems going into the Operating Day.
  They will have another opportunity to submit new matching trades until the end of the adjustment period, as long as the net quantities stay under the limit.
50 MW
RRSNC
90
20 MW
RRSNC
25
65 MW
25 MW
75 MW

## Slide 11: AS Trades: Add Evaluation in RTC
RRSNC
25
RRSNC
90
RRSNC
90
Each circle represents a different QSE, some with Load Ratio Share (LRS). RRSNC number is the 60% limit of LRS.
Each arrow represents an RRSNC AS trade. MWs can be traded multiple times.
Only analyze QSEs with LRS>0 to narrow.
Net trade
+100 MW
Net trade
+100 MW
Net trade
+35 MW
50 MW
100 MW
RRSNC
75
35 MW
45 MW
20 MW
40 MW
RRSNC
25
65 MW
25 MW
RRSNC
40
60 MW
75 MW
100 MW
RRSNC
45
Net trade
+35 MW
Net trade
+75 MW
Net trade
+45 MW
Net trade
+40 MW

## Slide 12: Example Scenario – New Proposal
Right after DRUC closes (~1430 in the day-ahead)
Run a process that checks whether anyone has over-purchased RRSNC
Send a message to QSE B that they have 5 MW too many
Possible Outcome #1
QSE B calls QSE S and they resolve the discrepancy, they both resubmit their trade with a quantity of 45 MW prior to 1800
Now everything is in alignment – no RUC short, no RT pro-ration
QSE S is able to get awarded an extra 5 MWs in SCED, if desired, in case there is room freed up elsewhere within the RRSNC limit
50 MW
RRSNC
45
50 MW
RRSNC
QSE B
RRS Obl.=75
RRSNC=45
QSE S

## Slide 13: Example Scenario – New Proposal
Possible Outcome #2
QSE B does nothing
At 1800 in the day-ahead, ERCOT cancels/rejects their trade (only QSE B's trade is canceled, but because there is no longer a match this will not be a confirmed trade)
    This may cause a RUC capacity short for the buying QSE
QSE S is able to offer those 50 MWs in SCED, if desired.
50 MW
RRSNC
QSE B
RRS Obl.=75
RRSNC=45
QSE S

## Slide 14: Example Scenario – New Proposal
Possible Outcome #3
QSE B does nothing at first
At 1800 in the day-ahead, ERCOT cancels/rejects their trade
They submit a new trade before the end of the adjustment period, for 45 MW
It is confirmed by QSE S so the quantity flows through to the self-provision cap for QSE S (and to settlements)
QSE S is able to offer those extra 5 MWs in SCED, if desired
50 MW
RRSNC
QSE B
RRS Obl.=75
RRSNC=45
QSE S
45 MW
RRSNC

## Slide 15: Wrap-up
This proposal is intended to address issues encountered with the self-provision cap as it relates to AS Trades.
  Outside the ISO scope – EEI master agreement amendment.