## Slide 1
RTCTF Subgroup Discussion of Telemetry
Requested Tables Summarizing Resource Status Proposal
ERCOT Staff
WebEx
November 11, 2019

## Slide 2: Background
At the 10/30/19 task force meeting, there was a request to have an additional small group meeting to discuss Real-Time telemetry and Resource Statuses under Real-Time Co-optimization (RTC).
  Raised during discussion on KP1.3 (1) and 1.4 (3)-(4).
The following material is focused on Resources Statuses, but the meeting is intended to be more general regarding Real-Time telemetry.

## Slide 3: RTC Resource Statuses – Resources that are not Load Resources
Resource Status | COP | Telemetry | Going Away under RTC | New under RTC | Remaining under RTC
ONRUC | Y | Y |  |  | x
ONREG | Y | Y | x |  | 
ON | Y | Y |  |  | x
ONDSR | Y | Y |  |  | x
ONOS | Y | Y |  |  | x
ONOSREG | Y | Y | x |  | 
ONDSRREG | Y | Y | x |  | 
FRRSUP | N | Y | x |  | 
ONTEST | Y | Y |  |  | x
ONEMR | Y | Y |  |  | x
ONRR | Y | Y | x |  | 
ONSC | Y | Y |  | x | 

## Slide 4: RTC Resource Statuses – Resources that are not Load Resources cont.
Resource Status | COP | Telemetry | Going Away under RTC | New under RTC | Remaining under RTC
ONECRS | Y | Y | x |  | 
ONOPTOUT | Y | Y |  |  | x
SHUTDOWN | N | Y |  |  | x
STARTUP | N | Y |  |  | x
ONHOLD | N | Y |  | x | 
OFFQS | Y | Y |  |  | x
ONFFRRRS | N | Y | x |  | 
OUT | Y | Y |  |  | x
OFFNS | Y | Y | x |  | 
OFF | Y | Y |  |  | x
EMR | Y | Y |  |  | x
EMRSWGR | Y | Y |  |  | x

## Slide 5: RTC Resource Statuses – Load Resources
Resource Status | COP | Telemetry | Going Away under RTC | New under RTC | Remaining under RTC
ONL | Y | Y |  | x | 
ONRGL | Y | Y | x |  | 
FRRSUP | N | Y | x |  | 
FRRSDN | N | Y | x |  | 
ONCLR | Y | Y | x |  | 
ONRL | Y | Y | x |  | 
ONECL | Y | Y | x |  | 
OUTL | Y | Y |  |  | x
ONFRRRRSL | N | Y | x |  | 

## Slide 6: Additional Detail on New Statuses under RTC
Resource Status | Description | Available for Energy Awards | Available for AS Awards | Count towards PRC
ONSC | Resource is on-line operating as a synchronous condenser. | N (Base Point set equal to Net Telemetered MW) | Y (RRS and ECRS) | Y
ONHOLD | Resources is on-line but temporarily unavailable for being awarded AS or economically dispatched by ERCOT. | N (Base Point set equal to Net Telemetered MW) | N | N
ONL | Resources is on-Line and is available for economic dispatch and/or for providing AS. | Y (If there is a Real-Time Bid to Buy) | Y | Y

## Slide 7: Additional Discussion and Questions