## Slide 1
2020 LTSA
Scenario Development Update
John Bernecker
November 12, 2019

## Slide 2: Scenario Development Update
After considering stakeholder feedback provided via the survey and comments received at RPG meetings, the following scenarios (in addition to Current Trends) are proposed for the 2020 LTSA:
  High Battery Energy Storage
  High Industrial Load
  Existing Transmission Constraints
  Renewable Mandate
High-level descriptions are included on the following slides
ERCOT is currently developing detailed assumptions for these scenarios

## Slide 3: High Battery Energy Storage
Background
Capacity expansion results for Current Trends show lower levels of Battery Energy Storage (BES) than is reflected in recent GIS reports
Story
Battery costs are low
Implementation
Add more BES to the model to be more consistent with the trend in requests
There were over 4000 MW of BES requests in the September 2019 GIS report
Include more EV and behind-the-meter storage (e.g. power walls) as adjustments to the load forecast
High development of grid-scale BES
Increased adoption of EV and behind-the-meter (BTM) storage

## Slide 4: High Industrial Load
Background
There has been higher-than-expected growth in industrial load in some areas (e.g. the Delaware Basin)
Story
Industrial growth in Texas is stronger than Current Trends
Implementation
Add high load assumptions for areas of growing industrial load (e.g. Delaware Basin and Corpus Christi area)
A number of LNG facilities are in development / under study
LNG growth is high
Add high assumptions for LNG facilities

## Slide 5: Existing Transmission Constraints
Background
Transmission constraints are not considered during initial generation expansion for other scenarios
Story
Existing transmission constraints persist
Implementation
Load and cost assumptions same as Current Trends
There is value in having a comparison set of generation expansion results that consider existing transmission constraints
Use “pipe and bubble” model to represent existing transmission constraints for generation expansion
No new bulk transfer pathways are developed

## Slide 6: Renewable Mandate
Background
New regulatory policies for wind, solar, and energy storage projects
Story
ITC and PTC are extended
Implementation
Extend ITC and PTC through 2035
Other regulatory changes / mandates take place (e.g. CSAPR revival)
Include emissions limits
Carbon pricing?
Incentives in place for Battery Energy Storage systems
Few to no new gas-fired Combined Cycle units added after 2021
Major infrastructure-related hurdles are overcome (e.g. sufficient grid investment and construction labor)

## Slide 7: Questions or Comments
John Bernecker
John.Bernecker@ercot.com
512-248-4274
Julie Jin
Julie.Jin@ercot.com
512-248-3982

## Slide 8: LTSA Methodology Improvement
Long-term Capacity Expansion
Long-term Transmission Analysis
New interface limits recommended?
Yes
End
No
Co-optimize capacity expansion and transmission planning through iterative process