## Slide 1
Capacity Short Settlement Changes due to ESR
Austin Rosel
ERCOT
BESTF Meeting
11/15/2019

## Slide 2: KTC - 7
No changes should be required to the formulation of the Capacity Short Charge developed at the RTC Task Force.
The Capacity Short Charge consists of two parts. An “AS Shortage” and an “overall shortage.”
  The “overall shortage” could be considered an “energy shortage” and is similar to the capacity short calculation currently in production.

## Slide 3: KTC - 7
The AS shortage portion of the calculation will consider the full range of the ESR by considering AS offers from the negative LSL value to the positive HSL value.

## Slide 4: KTC - 7
The overall shortage will consider the capacity from 0 to HSL only, and not from the negative LSL to the positive HSL.
This is in accordance with how the ESR will be evaluated in the RUC engine.

## Slide 5: Example
Simplified system.
RUC sees 100MW generation and 100MW load on the system with a 12 MW AS plan.
Only other unit on the system is an ESR.
  10 MW ESR (-10 LSL, 10 HSL)
  12 MW AS Responsibility
  20 MW of Up AS capability
  No forward trades, sales or purchases

## Slide 6: Example
RUC cannot fulfill the AS plan without increasing the load on the system by 2 MW.
  This would be caused by dispatching the ESR to -2 MW in the RUC solution.
The ESR can only supply 10 MW of energy from the generation side of the Resource, the ESR would need to be consuming 2MW in order to be able to provide 12 MW of Up AS.
RUC would see a need to commit additional Resources

## Slide 7: Example
RUC Capacity Short Charge
The ESR would not be short on AS.
  Capability - Responsibility
  20MW – 12MW = 8MW
The ESR would be short “overall”
  HSL – (RTAML + Responsibility)
  10 – (0 + 12) = -2

## Slide 8: Timing
Like today, the RUC Capacity Short calculation will take place in “snapshots”, snapshots at each RUC run and a snapshot before the end of the adjustment period.
The higher shortage between the shortage calculated during the snapshot in which a Resource was RUC committed and the snapshot at the end of the adjustment period is used to allocate RUC Make Whole Charges.

## Slide 9: Timing
Scenario 1: A unit is committed in RUC3. Adjustment period snapshot is used to allocate RUC charges, the higher of RUC3 and ADJ. Shortage = 6.
 | RUC1 | RUC2 | RUC3 | ADJ
HSL | 10 | 5 | 7 | 6
LSL | -10 | -10 | -10 | -10
RTAML | 0 | 0 | 0 | 0
RURESP | 12 | 12 | 12 | 12
RU OFFERS | 20 | 15 | 17 | 16
Overall Shortage | 2 | 7 | 5 | 6
AS Shortage | 0 | 0 | 0 | 0
Capacity Shortage | 2 | 7 | 5 | 6

## Slide 10: Timing
Scenario 2: A unit is committed in RUC3. The RUC 3 period snapshot is used to allocate RUC charges, the higher of RUC3 and ADJ. Shortage = 5.
 | RUC1 | RUC2 | RUC3 | ADJ
HSL | 10 | 5 | 7 | 10
LSL | -10 | -10 | -10 | -10
RTAML | 0 | 0 | 0 | 0
RURESP | 12 | 12 | 12 | 12
RU OFFERS | 20 | 15 | 17 | 20
Overall Shortage | 2 | 7 | 5 | 2
AS Shortage | 0 | 0 | 0 | 0
Capacity Shortage | 2 | 7 | 5 | 2

## Slide 11: Questions?