## Slide 1
Real-Time Co-optimization Task Force (RTCTF) Update to TAC
Matt Mereness
November 20, 2019

## Slide 2: Outline of RTCTF Update
TAC Voting Items for Key Principles (KPs)
TAC Non-Voting KP Item (Informational)
Next Steps
Appendix
  RTC Discussion Points & Issues Schedule
  Reminder of review process for RTCTF, TAC, and ERCOT Board

## Slide 3: TAC Key Principles for Endorsement
TAC is being asked to consider endorsement of the following KP sections:
  KP 1.3 (8)(c), (9), (12), (13)
    Offering and Awarding Ancillary Services in Real-Time
  KP 2 (1)-(6)
    Suite of Ancillary Service Products
  KP 5 (7)
    Day-Ahead Market
*Proposed TAC motion on last slide

## Slide 4: Key Principle 1.3: Offering and Awarding Ancillary Services in Real-Time
KP 1.3 Defines offers and awards of Ancillary Services (AS) in Real-Time by outlining the key mechanisms and timelines for submitted AS Offers, as well as the Ancillary Services considered and awarded under RTC.
KP 1.3 (8)(c), (9), (12), (13) (summarized)
  (c) All Resources providing FFR shall be considered during the RTC runs following an automatic deployment of FFR, including continued awarding of FFR and economic dispatch of the Resource up to the Resource’s limits.
  ERCOT operators will have the ability to manually reduce the amount of AS being awarded to Resources that, when deployed, may violate transmission constraints. ERCOT will notify QSE in Real-Time of any AS capability that has been derated by ERCOT including unit’s new AS limit in MW. ERCOT will exclude any such manually reduced AS amounts from the AS imbalance calculation.
  Proxy AS Offers will be created for Resources that do not have a valid AS offer curve for the entire operating range of the Resource for use in the Real-Time Market (see next slide for more details).
  Proxy AS Offers will not be created for Resources for use in the DAM.

## Slide 5: Key Principle 1.3: Offering and Awarding Ancillary Services in Real-Time (continued)
Details of Proxy Offers (12):
  a. The proxy offer will be a linked AS Offer across all AS products for which a Resource is qualified to provide. For Resources that are not Load Resources, the proxy offer MW will be equal to the Resource’s telemetered HSL. For Load Resources, the proxy offer MW will be equal to the Resource’s telemetered Maximum Power Consumption (MPC).
  b. For each AS, the price in the proxy AS Offer for that AS for the Resource will be set equal to:
    i. For Reg-Up and RRS, the maximum of a proxy offer price floor for that AS, the Resource’s highest submitted offer price for that AS, the Resource highest price offer for ECRS (submitted or proxy), and the Resource’s highest price offer for Non-Spin (submitted or proxy).
    ii. For ECRS, the maximum of a proxy offer price floor for ECRS, the Resource’s highest submitted offer price for ECRS, and the Resource’s highest price offer for Non-Spin (submitted or proxy).
    iii. For Non-Spin, the maximum of a proxy offer price floor for Non-Spin and the Resource’s highest submitted offer price for Non-Spin.
    iv. For Reg-Down, the maximum of a proxy offer price floor for Reg-Down and the Resource’s highest submitted offer price for Reg-Down.
  c. Each of the AS proxy offer price floors will be a separate configurable parameter that can be set equal to a defined $/MWh value.
  d. The system will be designed to allow different proxy offer price floors for instances in which the same AS can be provided by either Off-Line or On-Line Resources (i.e., the proxy offer price floor for an offline Non-Spin offer may be different than the proxy offer price floor for an online Non-Spin offer). It will also be designed to allow different proxy offer price floors for different subcategories of AS (i.e., the proxy offer price floor for a PFR-type RRS offer may be different than the proxy offer price floor for a UFR-type RRS offer).
  e. The RTC optimization will enforce various Resource specific AS constraints to ensure the AS awards are feasible, considering both QSE submitted AS offers and RTC created proxy AS Offers.
Meetings and discussion:
  RTCTF discussion Sep 19, Oct 9, Oct 30.
  October 30th reached consensus on the following: KP 1.3 (8)(c), (9), (12), (13).

## Slide 6: Key Principle 2: Suite of Ancillary Service Products
KP 2 Analyze necessary changes (if any) on the suite of Ancillary Service (AS) products with the implementation of Real-Time Co-Optimization (RTC)
KP 2(1) – (6):
  AS products under RTC will be the products finalized with the approval NPRR863.
  For all AS, the qualification process will determine the maximum MW amount the Resource is qualified to provide. ERCOT will limit awards the qualified quantity.
  Regulation Service continues with current qualification methodology. The MW qualified to provide Regulation Service (excluding Fast Responding Regulation Service (FRRS)) how much Resources can sustain for 15 minutes.
  Responsive Reserve (RRS) for a Generation Resource or Controllable Load Resource, continue with current qualification methodology and include the provision to sustain the qualified MW for 15 minutes. For a Generation Resource operating in synchronous condenser fast-response mode, continue with current qualification methodology. For a Load Resource controlled by high set UFR set at 59.7 Hz, continue with current qualification methodology. For a Resource providing Fast Frequency Response (FFR) including under-frequency relay Controlled Load Resources, ERCOT deployment signal and high-speed site-level data to verify the 15-cycle response along with the sustained 15-minute output.

## Slide 7: Key Principle 2: Suite of Ancillary Service Products (continued)
Cont.
  For Off-Line Non-Spin, continue with current qualification methodology. All SCED-dispatchable Resources are qualified to provide On-Line Non-Spin based on their 30 minute blended ramp rate.
  Off-Line ERCOT Contingency Reserve Service (ECRS) can only be provided by Resources that have met the Quick Start Generation Resources (QSGR) qualification. All SCED-dispatchable Resources are qualified to provide On-Line ECRS based on their 10-minute blended ramp rate. For ECRS from a Load Resource other than a Controllable Load Resource, the same qualification process used today to test manual deployment of Load Resources for RRS, excluding requirements for under-frequency relay response will be used.
Meetings and discussion:
  RTCTF discussion Sep 19, Oct 9, Oct 30.
  October 30th reached consensus on the following: KP 2 (1)-(6)

## Slide 8: Key Principle 5: Day-Ahead Market
KP 5 Identifies necessary changes for the DAM to bring Day-Ahead AS procurement into alignment with implementation of RTC.
KP 5 (7) (summarized)
  AS Virtual Offers
    Allow one part, unlinked offers of AS that do not represent an offer from a physical Resource from Qualified Scheduling Entities (QSEs). The general purpose of adding this new transaction is convergence bidding, in contrast to conventional Resource-specific AS Offers.
    If awarded, the QSE will be paid the DAM price for the capacity times the quantity awarded. The awarded QSE will pay the Real-Time price times the quantity awarded, via the AS Imbalance calculation.
    This proposal does not change the quantity of capacity purchased for each AS. ERCOT will attempt to procure the quantity from its AS Plan from Resource-specific offers as well as virtual offers against respective ASDCs.
    Virtual offers can only be submitted for Conventional Regulation (not Fast Frequency Response Service); RRS – Primary Frequency Response type; ECRS – dispatchable; and Non-Spin.
    The capability to self-arrange AS in excess of a QSE’s AS Obligation will no longer be needed and can be removed.

## Slide 9: Key Principle 5: Day-Ahead Market
(Cont.)
  AS Virtual Offers (cont.)
    Virtual AS Offers will automatically expire at the close of the DAM.
    The QSE will have the award included in the calculation of the QSE’s position regarding any RUC Capacity-Short Charge.
    The credit calculation for Real-Time Liability Estimate (RTLE) will also need to be modified to include this capacity in a fashion similar to the DAM energy short calculations.
    The DAM credit exposure calculations will be modified to validate the virtual AS Offers against the available credit limit, similar to how DAM Energy-Only Offers are treated (evaluating the potential DAM/RT price risk). This will take the form of the 90th percentile of any positive hourly difference between the RT MCPC and the DAM MCPC over the previous 30 days.
Meetings and discussion:
  RTCTF discussion Sep 19, Oct 9, Oct 30.
  October 30th reached consensus on the following: KP 5 (7)

## Slide 10: TAC Voting Items for Key Principles
Requesting TAC consideration today:
  TAC votes to endorse the following Key Principles:
    KP 1.3 (8)(c), (9), (12), (13)
      Offering and Awarding Ancillary Services in Real-Time
    KP 2 (1)-(6)
      Suite of Ancillary Service Products
    KP 5 (7)
      Day-Ahead Market

## Slide 11: TAC Non-Voting Item for Key Principle 1.2
Non-voting Item (informational only):
  KP 1.3 (16) AS Substitution
    Crescent Power proposed and supported this concept in response to the ISO Lessons Learned meeting for consideration of whether RTC should be designed to substitute higher value AS with lower offer for lower value AS in SCED only (substitutes ECRS for Non-Spin; RRS or RUS for ECRS and Non-Spin).
    RTCTF discussion yielded consensus this was not needed, and the concept was removed.
This design decision was captured in “RTCTF Discussion” in the KP1.3 template, but will not be considered by TAC. It may be added as a line item to KP8 Out of Scope at RTCTF.

## Slide 12: Next Steps
Remaining issues to be discussed prior to the January 29, 2020, TAC meeting):
  Schedule status is in the Appendix
Four meetings remaining leading into the January 2020 TAC meeting to submit all RTC Principles.
Questions?

## Slide 13
APPENDIX
Review Schedule
Review processes for RTCTF, TAC, and Board

## Slide 14: RTC Discussion Points & Issues Schedule
Posted in Keydocs: http://www.ercot.com/committee/rtctf

## Slide 15: RTC Discussion Points & Issues Schedule

## Slide 16: TAC Review Process
TAC serves as the stakeholder body to vote on Design Principles from the RTCTF
  Design Principles narrow the scope and codify design decisions to set direction for ERCOT in developing NPRRs upon completion of the Design Principles.
  Principle Templates are being used to capture the key dates of review, any significant contention or modifications, and the TAC vote.
RTC Key Principles are non-binding and will not go directly to the Board after TAC consideration.
  Procedures set forth in Protocol Section 21 do not apply to discussions, opinions or approvals by TAC with respect to RTC Key Principles.
  Section VIII of the ERCOT Board Policies and Procedures does not apply to discussions, opinions or unofficial approvals by TAC with respect to RTC Key Principles.
ERCOT will hold (supplement) the RTC Key Principles pending development and review of all RTC Key Principles by TAC.
  RTC Key Principle subsections will only be reconsidered if new or conflicting interdependencies are discovered. If information is added to an RTC Key Principal following TAC review, the RTC Key Principle will be taken back to TAC consideration.
  ERCOT will maintain TAC reviewed RTC Key Principle language in template form and post in a central location.

## Slide 17: TAC Review Process (continued)
Upon TAC review of all RTC Key Principles, ERCOT will compile the collection of RTC Key Principles into a single package, and will submit it to TAC for a courtesy review prior to Board submission.
  The RTC Key Principle package will contain a full record of TAC votes for Board discussion and consideration.
Following TAC review of the complete RTC Key Principles package, ERCOT will submit it to the Board for consideration.
  Any stakeholder opposed to an RTC Key Principle may request Board consideration in accordance with Section VIII of the ERCOT Board Policies and Procedures.
The Board will review and consider the RTC Key Principles package presented by TAC.

## Slide 18: Review Process for RTCTF, TAC, and Board
At PUCT: Project No. 48540
and other activities/decisions
At RTCTF: Develop design principles and scope
At TAC: Vote on design
principles and scope
Decisions that shape RTC principles/scope
Status updates to TAC and seek endorsement of incremental principles and scope
At Board: Monitor progress and
consider final set of principles and scope
Status updates on TAC decisions and status of principles/scope
Board vote on final design principles

## Slide 19: RTCTF Review Process
Internal ERCOT draft principles and principle concepts (elements)
ERCOT presents concepts for meeting in presentation format
ERCOT takes feedback and posts in 2 days as initial document for MP edits
MPs submit feedback as edits to document and any
- Concerns
Alternatives
MPs share initial feedback, concern, request for additional information
MPs must document concerns and alternative approach prior to meeting, and be prepared to discuss
ERCOT provides responses to finalize supporting principle concept
Meeting #1 Meeting #2 Meeting #3
Take consensus and non-consensus items to TAC for vote
ERCOT posts all MP feedback and responds to MP redlines, concerns, alternatives