## Slide 1
Nov 20, 2019
TAC
ERCOT Staff
Proposed Ancillary Service Methodology for 2020
Preliminary Quantities

## Slide 2: Schedule for Stakeholder Discussion
Sep 11, 2019 – PDCWG (Visit 1)
Sep 16, 2019 – WMWG (Visit 1)
Sep 19, 2019 – OWG (Cancelled)
  Feedback to change Responsive Reserve quantities using an updated Resource Contingency Criteria (RCC) of 2805 MW.
Oct 09, 2019 – PDCWG (Visit 2)
Oct 17, 2019 – OWG
Oct 21, 2019 – WMWG (Visit 2)
Nov 06, 2019 – WMS
Nov 07, 2019 – ROS
Nov 20, 2019 – TAC
Dec 10, 2019 – BOD

## Slide 3: Scope of Discussion
ERCOT is not proposing any changes to the methodologies for determining Ancillary Service (A/S) quantities for 2020.
Based on feedback received, ERCOT will compute Responsive Reserve Service quantities for 2020 by using an updated Resource Contingency Criteria (RCC) of 2805 MW in the associated studies.
The A/S quantities for 2020 contained in this presentation are based on the methodology that was approved in December 2018. These quantities reflect moving forward the historic data on which these are based, unless otherwise noted.
A redline version of the draft methodology and spreadsheets that contain the associated quantities for January through October of 2020 have been posted on the meeting page for this meeting.

## Slide 4: Regulation Service Methodology – 2020
The preliminary Regulation quantities for January 2020 through October 2020 in subsequent slides have been computed using current methodology (2018 and 2019 five-minute net load variability) and updated Wind Adjustment tables.
Wind Adjustment Tables track incremental MWs of Regulation needed to account for additional variability per 1000 MW increase in installed Wind capacity.
  These tables have been updated for 2020

## Slide 5: Hourly Average Regulation Comparison

## Slide 6: Responsive Service Methodology (RRS) - 2020
The preliminary RRS quantities for January 2020 through October 2020 in subsequent slides have been computed using 2018 and 2019 system inertia conditions and an updated RRS table.
The RRS table tracks RRS requirements for different inertia conditions.
  This table has been updated for 2020. For the update, a Resource Contingency Criteria (RCC) of 2805 MW has been used in associated studies.

## Slide 7: RRS January

## Slide 8: RRS March

## Slide 9: RRS August

## Slide 10: Hourly Average RRS Comparison

## Slide 11: Non Spinning Reserve Methodology (Non-Spin) - 2020
The preliminary Non-Spin quantities for January 2020 through October 2020 in subsequent slides have been computed using current methodology (2017, 2018 and 2019 Net load and Net load Forecast) and updated Wind Over-Forecast Error Adjustment tables.
Wind Over-Forecast Error Adjustment Table track estimated increase in wind over forecast error per 1000 MW increase in installed Wind capacity.
  This table has been updated for 2020.

## Slide 12: Hourly Average Non-Spin Comparison

## Slide 13: Summary
ERCOT is not proposing any changes to the methodologies for determining Ancillary Service (A/S) quantities for 2020.
Based on feedback received, ERCOT will compute Responsive Reserve Service quantities for 2020 by using an updated Resource Contingency Criteria (RCC) of 2805 MW in the associated studies.
ERCOT is seeking TAC’s endorsement for the 2020 Ancillary Service Methodology.