## Slide 1
Key Topic 2: Energy Storage Resource PRC and ORDC Reserve Contribution
ERCOT Staff
10/18/2019

## Slide 2: Acronyms
Energy Storage Resource (ESR)
Controllable Load Resource (CLR)
Charging side of ESR modeled as CLR (ESR-CLR)
Discharging side of ESR modeled as Generation (ESR-Gen)
Physical Responsive Capability (PRC)
State of Charge (SOC)
Real-Time On-Line Reserve Capacity (RTOLCAP)

## Slide 3: Physical Responsive Capability (PRC) Definition
“A representation of the total amount of frequency responsive Resource capability On-Line in Real-Time.”
Variable | Description
PRC1 | Generation Resources
PRC2 | WGRs
PRC3 | Hydro under Synchronous Fast Response Mode
PRC4 | Non-Controllable Load Resources (UFR Type)
PRC5 | Controllable Load Resource (CLR) active in SCED and carrying Ancillary Services
PRC6 | Capacity from Controllable Load Resources active in SCED and not carrying Ancillary Service Resource Responsibility
PRC7 | Capacity from Resources capable of providing FFR (NPRR 863)

## Slide 4: PRC Contribution from Energy Storage Resource (ESR)
Currently ERS are considered and accounted in terms of MW.
However, PRC provided by Storage Resources should also consider energy limitations of the Storage Resource besides droop settings.
The approach for considering PRC from Storage Resources is to convert the energy available to a MW equivalent.
To perform this conversion a specific time period is required, which is currently recommended to be 15 minutes.
When online and sitting idle or discharging;
When Charging
PRC = Min(X% of HSL based on droop, HSL-Gen(injection),

## Slide 5: PRC Review
PRC1: Online Gen Headroom EXCEPT:
  Wind Resources
  Nuclear Resources
  ONTEST, STARTUP, SHUTDOWN
  “Low Output” Resources
PRC2: PFR-Capable Wind Gen Headroom
PRC1
PRC2
PRC3
PRC4
PRC5
PRC6
PRC3: Synchronous Condenser Fast Response Mode
PRC4: Non-Controllable Load Resources carrying RRS
PRC5: Controllable Load Resources carrying RRS
PRC6: Controllable Load Resources not carrying RRS
PRC7
PRC8
PRC7: Capacity from Resources capable of providing FFR
PRC8: PFR capable Headroom from ESR

## Slide 6: RT On-Line Reserve Capacity (RTOLCAP)
Definition:
RTOLCAP - the system total Real-Time On-Line reserve capacity of all On-Line Resources for the SCED interval.
SL – Base Points of nine Generation
NCLR RRS * 1.5

## Slide 7: RT On-Line Reserve Capacity (RTOLCAP) – ESR Today
HSL – Base Points of Online Generation
Online Gen Headroom EXCEPT:
  RUC Resources (includes RMR)
  Nuclear Resources
  ONTEST, STARTUP, SHUTDOWN
  Resources output < 95% LSL
CLR Base Points – LPC + CLR REG
NCLR RRS (limited to 150% of responsibility)
Online Controllable Load Resources (SCED qualified) Headroom
ESR-Gen included here
ESR-CLR included here
HSL – Basepoint of Online Generation

## Slide 8: Proposed RTOLCAP contribution from Energy Storage Resource (ESR)
When online and sitting idle or discharging;
When Charging (ESR-CLR Basepoint is a positive number)
RTOLCAP = Min(HSL- “Gen-ESR” Base Point,

## Slide 9: Questions