## Slide 1
KTC-7: Base Point Deviation Charges for Energy Storage Resources-
Single Model Examples
Magie Shanks
ERCOT
BESTF Meeting
11/15/2019

## Slide 2: Overview
Create a new Base Point Deviation (BPD) Settlement for the Single Model Energy Storage Resource (ESR).
  Over performance – Providing a greater response than ERCOT has requested
    Over Generation or Under Consumption
  Under performance- Providing a lesser response than ERCOT has requested
    Under Generation or Over Consumption
Deviation tolerance set to 3MW or 3%

## Slide 3: Over & Under Performance Analysis Scenarios
Chart: Settlement Intervals
| 1 | 2 | 3 | 4
AABP | 36 | -14 | 18 | -20
Gen/Cons | 60 | -4 | 6 | -36
OVER
UNDER
UNDER

## Slide 4: Example – Over Performance
Energy Storage Resource (Over Generation) | 
AABP (BP + RegUp) = (30+6) | 36MW
TGC (Telemetered Gen or Cons) | 60MW
Tolerance: Max(MW, %): | 
MW Limit (AABP + 3MW) | 39MW
% Limit (AABP + Abs(AABP * .03)) | 37.08MW
Deviation (TGC - Tolerance) | 21MW or 5.25MWh
RTSPP | $20/MWh
BPDAMT (RTSPP * Deviation) | $105
Energy Storage Resource (Under Consumption) | 
AABP (BP - RegDn) = (-12 - 2) | -14MW
TGC (Telemetered Gen or Cons) | -4MW
Tolerance: Max(MW, %): | 
MW Limit (AABP + 3MW) | -11MW
% Limit (AABP + Abs(AABP * .03)) | -13.8MW
Deviation (TGC - Tolerance) | 7MW or 1.75MWh
RTSPP | $20/MWh
BPDAMT (RTSPP * Deviation) | $35
AABP = Adjusted Aggregated Base Point
RTSPP = Real-Time Settlement Point Price
BPDAMT = Base Point Deviation Amount

## Slide 5: Example – Under Performance
Energy Storage Resource (Under Generation) | 
AABP (BP + RegUp) = (15+3) | 18MW
TGC (Telemetered Gen or Cons) | 6MW
Tolerance: Min(MW, %): | 
MW Limit (AABP - 3MW) | 15MW
% Limit (AABP - Abs(AABP * .03)) | 17.46MW
Deviation (Tolerance-TGC) | 9MW or 2.25MWh
RTSPP | $20/MWh
BPDAMT (RTSPP * Deviation) | $45
Energy Storage Resource (Over Consumption) | 
AABP (BP - RegDn) = (-19 - 1) | -20MW
TGC (Telemetered Gen or Cons) | -36MW
Tolerance: Min(MW, %): | 
MW Limit (AABP - 3MW) | -23MW
% Limit (AABP - Abs(AABP * .03)) | -20.6MW
Deviation (Tolerance-TGC) | 13MW or 3.25MWh
RTSPP | $20/MWh
BPDAMT (RTSPP * Deviation) | $65
AABP = Adjusted Aggregated Base Point
RTSPP = Real-Time Settlement Point Price
BPDAMT = Base Point Deviation Amount

## Slide 6: Questions?

## Slide 7: Appendix – BPD Settlement
ESR BPD will mimic Generation Resource BPD
Over Performance:
  BPDAMT = Max (PR1, RTSPP) * OPESR
  Where:
  OPESR = Max [0, (TGC – ¼ * Max (AABP + Abs(AABP * 3%), AABP + 3MW))]
AABP = Adjusted Aggregated Base Point
RTSPP = Real-Time Settlement Point Price
BPDAMT = Base Point Deviation Amount
OPESR = Over Performance for ESR
PR1 = $20/MWh; parameter defined in Protocols
TGC = Telemetered Gen or Cons

## Slide 8: Appendix – BPD Settlement (cont.)
Under Performance:
  BPDAMT = (-1) * Min (PR2, RTSPP) * UPESR
  Where:
  UPESR = Max [0, ( ¼ * Max (AABP - Abs(AABP * 3%), AABP - 3MW)- TGC)]
AABP = Adjusted Aggregated Base Point
RTSPP = Real-Time Settlement Point Price
BPDAMT = Base Point Deviation Amount
UPESR = Under Performance for ESR
PR2 = -$20/MWh; parameter defined in Protocols
TGC = Telemetered Gen or Cons