## Slide 1
Wholesale Storage Load
KTC-8
Paul Wattles
ERCOT Staff
BESTFORCE
Nov. 15, 2019

## Slide 2: Topics
ERCOT’s proposal for Energy Storage Resource (ESR) pricing
  Separating the issue of nodal pricing from the issue of Wholesale Storage Load (WSL) treatment
WSL discussion, including KTC-8 decision points

## Slide 3: Separating nodal pricing from WSL
WSL is not a prerequisite for nodal pricing
Under KTC-3, ERCOT proposes to require ESRs to be settled at a nodal price whether discharging (injecting) or charging (withdrawing) -- irrespective of whether the ESR is receiving Wholesale Storage Load treatment

## Slide 4: ESR Settlements
Nodal settlement for charging requires separate metering of the ESR Load
ESR load will be treated the same in Energy Imbalance Settlement -- both settled using 15-minute nodal prices
WSL ESR treatment will continue to be exempt from Load Ratio Share or per-MWh-based charges and allocations
Non-WSL ESR load will be subject to Load Ratio Share and per MWh-based charges and allocations

## Slide 5: Proposal for the BESTFORCE
ESR settlement at nodal for both charging and discharging is appropriate market design
Market Rules can be developed for ESRs without the need to modify WSL provisions

## Slide 6
WSL Discussion and KTC-8 Decision Points

## Slide 7: BESTF KTC-8 Decision Points (current draft)
Should WSL treatment implementation extend to batteries that can self-serve PUN Load with the stored energy?
Should WSL treatment implementation extend to non-dispatched generators? If yes, should there be differentiation between a SOG that is co-located with customer load and one that only has auxiliary loads behind the metering point?

## Slide 8: Background: PUC Subst. R. 25.501 (m)
(m) Energy Storage.
For a storage facility that has more than one delivery point, ERCOT shall net the impact of those delivery points on the ERCOT system for settlement purposes.
Wholesale storage occurs when electricity is used to charge a storage facility; the storage facility is separately metered from all other facilities including auxiliary facilities; and energy from the electricity is stored in the storage facility and subsequently re-generated and sold at wholesale as energy or ancillary services. Wholesale storage is wholesale load and ERCOT shall settle it accordingly, except that ERCOT shall settle wholesale storage using the nodal energy price at the electrical bus that connects the storage facility to the transmission system, or if the storage facility is connected at distribution voltage, the nodal price of the nearest electrical bus that connects to the transmission system. Wholesale storage is not subject to retail tariffs, rates, and charges or fees assessed in conjunction with the retail purchase of electricity. Wholesale storage shall not be subject to ERCOT charges and credits associated with ancillary service obligations, or other load ratio share or per megawatt-hour based charges and allocations. The owner or operator of electric storage equipment or facilities shall not make purchases of electricity for storage during a system emergency declared by ERCOT unless ERCOT directs that such purchases occur.

## Slide 9: Background: PUC Subst. R. 25.501 (m)
(m) Energy Storage.
For a storage facility that has more than one delivery point, ERCOT shall net the impact of those delivery points on the ERCOT system for settlement purposes.
Wholesale storage occurs when electricity is used to charge a storage facility; the storage facility is separately metered from all other facilities including auxiliary facilities; and energy from the electricity is stored in the storage facility and subsequently re-generated and sold at wholesale as energy or ancillary services. Wholesale storage is wholesale load and ERCOT shall settle it accordingly, except that ERCOT shall settle wholesale storage using the nodal energy price at the electrical bus that connects the storage facility to the transmission system, or if the storage facility is connected at distribution voltage, the nodal price of the nearest electrical bus that connects to the transmission system. Wholesale storage is not subject to retail tariffs, rates, and charges or fees assessed in conjunction with the retail purchase of electricity. Wholesale storage shall not be subject to ERCOT charges and credits associated with ancillary service obligations, or other load ratio share or per megawatt-hour based charges and allocations. The owner or operator of electric storage equipment or facilities shall not make purchases of electricity for storage during a system emergency declared by ERCOT unless ERCOT directs that such purchases occur.

## Slide 10: Background: PUC Subst. R. 25.501 (m)
(m) Energy Storage.
For a storage facility that has more than one delivery point, ERCOT shall net the impact of those delivery points on the ERCOT system for settlement purposes.
Wholesale storage occurs when electricity is used to charge a storage facility; the storage facility is separately metered from all other facilities including auxiliary facilities; and energy from the electricity is stored in the storage facility and subsequently re-generated and sold at wholesale as energy or ancillary services. Wholesale storage is wholesale load and ERCOT shall settle it accordingly, except that ERCOT shall settle wholesale storage using the nodal energy price at the electrical bus that connects the storage facility to the transmission system, or if the storage facility is connected at distribution voltage, the nodal price of the nearest electrical bus that connects to the transmission system. Wholesale storage is not subject to retail tariffs, rates, and charges or fees assessed in conjunction with the retail purchase of electricity. Wholesale storage shall not be subject to ERCOT charges and credits associated with ancillary service obligations, or other load ratio share or per megawatt-hour based charges and allocations. The owner or operator of electric storage equipment or facilities shall not make purchases of electricity for storage during a system emergency declared by ERCOT unless ERCOT directs that such purchases occur.

## Slide 11: Background: Preamble to the Rule
The preamble to the storage rulemaking (Project 39917, approved March 7, 2012) indicates that WSL should be optional
Commission Response (pg. 14)
  ‘…. For any of these scenarios, the storage facility could choose not to separately meter the storage facility and treat all energy purchased from the ERCOT system as retail sales. …’
Commission Response (identical sentences pp. 34, 43)
  ‘In its discussion of question 1, the commission decided that storage load may be treated as wholesale load. …’

## Slide 12: Who gets WSL?
Per the Rule language, the storage facility must be ‘…separately metered from all other facilities including auxiliary facilities...’
Based on this language, ERCOT’s current implementation requires approval of an ESR’s metering configuration when WSL is requested
NOTE: All ESRs in the System to date have requested and are receiving WSL treatment

## Slide 13: Who gets WSL?
There are potentially three types of ESRs that would not get WSL:
  The ESR chooses not to apply for WSL treatment via a metering design proposal
  The configuration of the ESR site includes other Load behind the ESR metering point
  The configuration of the ESR site includes retail Load behind the Point of Interconnection

## Slide 14: KTC-8 Decision Points…..
Should WSL treatment implementation extend to batteries that can self-serve PUN Load with the stored energy?
  The PUC Rule states: ‘wholesale storage occurs when …energy from the electricity is stored in the storage facility and subsequently re-generated and sold at wholesale as energy or ancillary services.’
  ERCOT would consider a metering design proposal that allowed an ESR to serve PUN Load to be inconsistent with this Rule language
  This is out of scope for the BESTFORCE

## Slide 15: KTC-8 Decision Points…..
Should WSL treatment implementation extend to non-dispatched generators?
  This is also out of scope for the BESTFORCE

## Slide 16: Proposal for the BESTFORCE
No need to revise WSL-specific Protocols
Discussion around WSL for Settlement-Only Energy Storage (SOES) -- TBD
  (NOTE: SOES will continue to be known as SODG until storage terminology NPRR is submitted by RTF and approved)

## Slide 17
Questions?